## Slide 1
Fundamental Communications Concepts
1

## Slide 2: Introduction
Communications Systems and Modulation
  Function of any communication system is to transfer information from one point to another.
  All systems consist of three elements:
    Transmitter
    Receiver
    Channel

## Slide 3: Introduction
Communications Systems and Modulation
  Modulation
    Impressing low-frequency voltages (information) onto high-frequency signal (carrier) for transmission.
  Demodulation or detection
    Recovering (separating) information from the high frequency carrier.

## Slide 4: Introduction
Communications Systems and Modulation
  Carriers often sine waves; amplitude, frequency, and phase are the only characteristics of a sine-wave carrier that can be modified.

## Slide 5: Introduction
The Electromagnetic Spectrum
  Magnetic fields surround moving electric charges (currents).
  Electric and magnetic fields both result from voltage potentials and current flows.
  Electromagnetic energy
    Electric and magnetic fields form at right angles to each other and at right angles to direction of travel.

## Slide 6: Introduction
The Electromagnetic Spectrum
  Magnitudes of both electric and magnetic fields are constant.
  Transducer
    Converts energy
  Electromagnetic spectrum
    Entire range of signals occupying all frequencies

## Slide 7: Introduction
The Electromagnetic Spectrum
  Audio frequencies
    Can be heard by human ear
  Radio frequencies
    Above 50 kHz
  Transmission of signals
    Wireless/physical media

## Slide 8: Introduction
The Electromagnetic Spectrum
  Communications systems limited by two factors:
    Bandwidth
    Noise

## Slide 9: The Decibel in Communications Work
Logarithms
  Decibel (dB)
    Unit of sound intensity; ratios related to sound pressure levels.
  Logarithms are exponents.
  Antilogarithm (antilog)
    Base raised to that number

## Slide 10: The Decibel in Communications Work
The Decibel as a Power Ratio
  In electronics, decibel is defined as a power ratio.
The Decibel as a Voltage or Current Ratio
  Voltages and currents expressed as decibel relationships provided input and output impedances taken into account.

## Slide 11: The Decibel in Communications Work
Reference Levels
  By itself, the decibel has no absolute value; they represent ratios of powers, voltages, or currents.
  Only decibel measurements with explicit or implied reference can be expressed in terms of absolute value.

## Slide 12: The Decibel in Communications Work
Approximating with Decibels
  True utility of decibels is their ability to provide quick approximations.
    See Table 1-2: Common Decibel Relationships

## Slide 13: Table 1-2: Common Decibel Relationships

## Slide 14: The Decibel in Communications Work
Stage Gains and Losses
  Decibel relationships useful for determining gains (or losses) through pieces of equipment with multiple stages.

## Slide 15: Information and Bandwidth
Bandwidth
  Defines frequency range over which a circuit or system operates.
  Greater the bandwidth, greater the amount of information transferred.
  Hartley’s law
    Information transmitted directly proportional to product of bandwidth used and time of transmission

## Slide 16: Information and Bandwidth
Bandwidth
  Radio-frequency spectrum is a scarce and valuable public resource.

## Slide 17: Information and Bandwidth
Understanding Frequency Spectra
  The locations on spectrum of all frequencies produced as the result of modulation are what determine bandwidth of the modulated signal.
  Fourier: developed means to break down periodic waveforms into a series of sine and/or cosine waves at multiples of the fundamental frequency.

## Slide 18: Information and Bandwidth
Time- and Frequency-Domain Representations
  Time domain
    Waveform amplitude as a function of time
  Oscilloscope is a time-domain representation.

## Slide 19: Information and Bandwidth
Time- and Frequency-Domain Representations
  Frequency domain
    Amplitude viewed as function of frequency rather than of time
  Spectrum analyze
    Signals in frequency domain

## Slide 20: Information and Bandwidth
The Fast Fourier Transform
  Conversion from time to frequency domain approximated with fast Fourier transform (FFT).
  Algorithm suited to computer-based implementation.
  It allows for large number of calculations to be reduced to a manageable number through elimination of redundancies.

## Slide 21: Noise
External Noise
  Human-made
    Caused by electronic or mechanical devices operating in proximity to communications system
  Atmospheric
    Caused by natural phenomena occurring either within Earth’s atmosphere or in outer space

## Slide 22: Noise
External Noise
  Space
    Arrives from outer space

## Slide 23: Noise
Internal Noise
  Thermal
    Result of thermal interactions between free electrons and vibrating ions in a conductor
  Transistor
    Shot noise results from currents flowing within emitter-base/collector-base diodes.

## Slide 24: Noise
Internal Noise
  Frequency noise effects
    Low-frequency effect (excess)
    High-frequency noise (transit-time)

## Slide 25: Noise Designation and Calculation
Signal-to-Noise Ratio
  Measure of desired signal power to noise power.
Noise Figure
  Specifies exactly how noisy a device is.
Reactance Noise Effects
  Reactive circuits do limit frequency response; significant effect on noise characteristics.

## Slide 26: Noise Designation and Calculation
Noise Created by Amplifiers in Cascade
  Friiss’s formula
    Overall noise effect of multistage system

## Slide 27: Noise Designation and Calculation
Equivalent Noise Temperature
  Means of representing noise produced at output of real-world device or system.
  Noise generated by resistor placed at input to noiseless amplifier with the same gain as device or system under consideration.

## Slide 28: Noise Designation and Calculation
Equivalent Noise Resistance
  Manufacturers represent noise generated by a device with a fictitious resistance.

## Slide 29: Troubleshooting
General Troubleshooting Techniques
  Ask the right questions.
  Take time to learn test equipment, its capabilities, and limitations.
  Maintain clear, up-to-date records of all changes made to equipment.
  Replace suspicious unit with known good one.
  Plot a game plan or strategy.

## Slide 30: Troubleshooting
Reasons Electronic Circuits Fail
  Complete failures
  Intermittent faults
  Poor system performance
  Induced failures

## Slide 31: Troubleshooting
Troubleshooting Plan
  Symptoms as clues to faulty stages
  Signal tracing and signal injection
  Voltage and resistance measurements
  Substitution