## Slide 1
Amplitude Modulation
2

## Slide 2: Overview of Amplitude Modulation
Modulation
  Combining information signal, often one whose instantaneous peak voltage is constantly changing and whose range of occupied frequencies is relatively low, with a carrier, which is a relatively high-frequency sine wave of constant amplitude.

## Slide 3: Overview of Amplitude Modulation
Three characteristics of a sine wave carrier—amplitude, frequency, phase—can be modified to convey information.
Notes: <number>

## Slide 4: Overview of Amplitude Modulation
AM has virtue of simplicity, both in generation at transmitter and detection at receiver.
  Double-sideband, full-carrier (DSBFC)
  Single-sideband (SSB)
  Citizens band (CB)
Notes: <number>

## Slide 5: Double-Sideband AM
Linear device
  Current is linear function of voltage.
Nonlinear device or circuit
  Changes in current not directly proportional to changes in applied voltage.

## Slide 6: Double-Sideband AM
AM Waveforms
  Maximum amplitude when intelligence amplitude reaches maximum positive value; minimum when intelligence amplitude is at maximum negative value.

## Slide 7: Double-Sideband AM
Modulation Index
  Overmodulation
    Modulating signal amplitude continues to increase.
    Must never be allowed to occur.

## Slide 8: Double-Sideband AM
Modulation Index
  Overmodulation
    Violation of law in licensed systems.
    Modulation index (factor)
      Symbolized by m; ratio of intelligence amplitude to carrier amplitude; quantifies extent to which intelligence varies carrier voltage.

## Slide 9: Double-Sideband AM
Amplitude Modulation/Mixing in Frequency Domain
  Mixing
    Two signals at different frequencies combined in nonlinear device.
  Intermodulation distortion (intermod)
    Undesired mixing.

## Slide 10: Double-Sideband AM
Amplitude Modulation/Mixing in Frequency Domain
  Intermod products
    Additional frequencies created.
  Transmitter modulator circuit
    Combines carrier and intelligence signals widely separated in frequency.

## Slide 11: Double-Sideband AM
Amplitude Modulation/Mixing in Frequency Domain
  Combining any two sine waves through nonlinear device produces following frequency components:
    A dc level
    Components at each of the two original frequencies

## Slide 12: Double-Sideband AM
Amplitude Modulation/Mixing in Frequency Domain
  Combining any two sine waves through nonlinear device produces following frequency components:
    Components at sum and difference frequencies of two original frequencies
    Harmonics of two original frequencies

## Slide 13: Double-Sideband AM
Amplitude Modulation in the Time Domain
  Modulated AM signal produces side frequencies or sidebands, one on each side of the carrier.
  Oscilloscope display
    Time domain representation.
  Observation of side frequencies require frequency domain display, such as spectrum analyzer.

## Slide 14: Double-Sideband AM
Phasor Representation of AM
  Side frequencies
    Sidebands.
  AM signal composed of the:
    Carrier
    Upper sideband (usb) at one-half carrier amplitude with frequency equal to carrier frequency plus modulating signal frequency.

## Slide 15: Double-Sideband AM
Phasor Representation of AM
  AM signal composed of the:
    Lower sideband (lsb) at one-half carrier amplitude at carrier frequency minus modulation frequency.

## Slide 16: Double-Sideband AM
Power Distribution in Carrier and Sidebands
  AM Transmission
    Carrier amplitude and frequency always remain constant.
    Sidebands changing in amplitude and frequency.

## Slide 17: Double-Sideband AM
Power Distribution in Carrier and Sidebands
  AM Transmission
    Carrier contains no information since it never changes; it does contain the most power.
    Sidebands contain information.

## Slide 18: Double-Sideband AM
Summary of Amplitude Modulation
  Total power of modulated AM signal higher than carrier alone.
  Maximum power achieved at 100% modulation.
  Most power contained within carrier.
  No information resides in carrier; its amplitude is constant.
  All information contained within varying-amplitude sidebands.

## Slide 19: Double-Sideband AM
Summary of Amplitude Modulation
  Modulated AM waveform result of multiplication of carrier and intelligence frequencies; special instance of mixing.
  Mixing (modulation) achieved when signals applied to nonlinear device.
  Sidebands redundant, mirror images of each other; same information contained in each.

## Slide 20: Double-Sideband AM
Summary of Amplitude Modulation
  Bandwidth of modulated waveform is always twice highest modulating frequency.
  Modulation index must not exceed 1 (100% modulation).
  Maintaining as close to 100% modulation desirable; power in sidebands greatest with high modulation percentages.

## Slide 21: Suppressed Carrier and Single-Sideband AM
Power Measurement
  Total power output of DSBFC AM transmitter is equal to carrier power plus sideband power.
  Conventional AM transmitters rated in terms of carrier power output.

## Slide 22: Suppressed Carrier and Single-Sideband AM
Power Measurement
  SSB systems used for voice communications; do not generate a sinusoidal waveform.
  SSB transmitters and linear power amplifiers are rated in terms of peak envelope power (PEP).

## Slide 23: Suppressed Carrier and Single-Sideband AM
Advantages of SSB
  More effective utilization of available frequency spectrum.
  Less subject to effects of selective fading.
  Power saved by not transmitting the carrier and one sideband.

## Slide 24: Suppressed Carrier and Single-Sideband AM
Types of Sideband Transmission
  Standard single sideband (SSB)
  Single-sideband suppressed carrier (SSBSC)
  Twin-sideband suppressed carrier or independent sideband (ISB) transmission
  Vestigial sideband
  Amplitude-compandored single sideband (ACSSB)