## Slide 1
Angle Modulation
3

## Slide 2: Frequency Modulation in the Time Domain
Simple FM Generator
  Frequency of impinging sound waves determines rate of frequency change.
  Amplitude of impinging sound waves determines amount of frequency change, or deviation from frequency produced by oscillator in absence of modulation.

## Slide 3: Frequency Modulation in the Time Domain
Concept of Deviation
  Deviation constant defines how much carrier frequency will deviate for input voltage level.
  Deviation constant dependent on system design.
  Knowing deviation on either side of carrier is essential for determining occupied bandwidth of modulated signal.

## Slide 4: Frequency Modulation in the Time Domain
Time-Domain Representation
  Amplitude of carrier never changes.
  Modulation causes carrier to shift (deviate) both above and below its rest or center frequency that preserves both amplitude and frequency characteristics of the intelligence.

## Slide 5: Frequency Modulation in the Time Domain
Two Major Concepts
  Frequency deviation
    Amount by which oscillator frequency increases and decreases from fc.
  Direct FM transmitter
    Modulating signal applied directly to frequency-determining element of carrier oscillator.

## Slide 6: Frequency Modulation in the Time Domain
Two Major Concepts
  Indirect FM causes instantaneous phase angle of carrier to be varied in response to modulating signal and is example of phase modulation.

## Slide 7: FM in the Frequency Domain
Determining bandwidth
  Determining where the power resides in modulated signal.
Determining modulation index
  First step in determining occupied bandwidth of modulated carrier.

## Slide 8: FM in the Frequency Domain
FM
  Both modulating signal frequency and amplitude affect index.
AM
  Instantaneous modulating signal amplitude (not frequency) affect modulation index.

## Slide 9: FM in the Frequency Domain
Bandwidth Determination
  Bessel function
    High-level mathematical tool for solving frequency components of frequency-modulated signal.
  Modulated FM signal will often occupy a wider bandwidth than its equivalent AM counterpart.

## Slide 10: FM in the Frequency Domain
Bandwidth Determination
  AM bandwidth always equal to twice the highest frequency of modulating signal, regardless of its amplitude.
  Determine how power is distributed among carrier and sidebands.
  Depends on identifying number of significant sideband pairs.

## Slide 11: FM in the Frequency Domain
Bandwidth Determination
  Bessel table is table of percentages expressed in decimal form.
    See Table 3-1: FM Side Frequencies from Bessel Functions

## Slide 12: Table 3-1 FM Side Frequencies from Bessel Functions

## Slide 13: FM in the Frequency Domain
Bandwidth Determination
  Total occupied bandwidth of signal
    Frequency difference between highest-order significant side frequencies on either side of carrier.

## Slide 14: FM in the Frequency Domain
Bandwidth Determination
  Sideband or side frequency significant if its amplitude is 1% (0.01) or more of unmodulated carrier amplitude.
  Higher modulation indices produce wider-bandwidth signals.

## Slide 15: FM in the Frequency Domain
FM Spectrum Analysis/Power Distribution
  Bessel table shows carrier and side-frequency levels in terms of normalized amplitudes.
  Expressing levels in decibel terms useful from practical standpoint; it matches measurement scale of spectrum analyzer.

## Slide 16: FM in the Frequency Domain
FM Spectrum Analysis/Power Distribution
  Bessel table used to determine power distribution in carrier and sidebands.

## Slide 17: FM in the Frequency Domain
Carson’s Rule Approximation
  Predicts bandwidth necessary for FM signal.
Zero-Carrier Amplitude
  Zero-carrier conditions (carrier nulls) suggest a convenient means of determining deviation produced in FM modulator.

## Slide 18: FM in the Frequency Domain
Wideband and Narrowband FM
  Wideband FM transmissions
    Require more bandwidth than e occupied by AM transmissions with same maximum intelligence frequency.
  Specialized mobile radio (SMR)
    Two-way voice communication rather than entertainment.

## Slide 19: FM in the Frequency Domain
Wideband and Narrowband FM
  Narrowband FM (NBFM) systems
    Occupied bandwidths no greater than those of equivalent AM transmissions.

## Slide 20: FM in the Frequency Domain
Percentage of Modulation and Deviation Ratio
  FM percentage
    Modulation index at 100% varies inversely with intelligence frequency.
  Contrasts with AM
    Full or 100% modulation means modulation index of 1 regardless of intelligence frequency.

## Slide 21: FM in the Frequency Domain
Percentage of Modulation and Deviation Ratio
  FM percentage of modulation describes maximum deviation permitted by law or regulation.

## Slide 22: FM in the Frequency Domain
Percentage of Modulation and Deviation Ratio
  Deviation ratio (DR)
    Maximum frequency deviation divided by maximum input frequency.
  Common term in television and FM broadcasting.
  Convenient characterization of FM systems as wideband or narrowband.

## Slide 23: Phase Modulation
Phase Modulation
  Modulating signal causes instantaneous carrier phase, rather than its frequency, to shift from its reference (unmodulated) value.
  Carrier phase angle in radians either advanced or delayed from its reference value by amount proportional to modulating signal amplitude.

## Slide 24: Phase Modulation
Phase Modulation
    Phasor speeds up or slows down in response to modulating signal.
  Frequency of modulating signal does not affect deviation in FM; in PM, it does.
  Amplitude of modulating signal has effect on rate of change.
  Rate of change describes calculus derivative.

## Slide 25: Noise Suppression
FM Noise Analysis
  Important advantage of FM over AM
    FM has superior noise characteristics.
  Addition of noise to received signal causes change in its amplitude.
  FM has inherent noise reduction capability not possible with AM.

## Slide 26: Noise Suppression
Capture Effect
  Inherent ability of FM to minimize effect of undesired signals applies to reception of undesired station operating at same or nearly same frequency as desired station.
  Causes receiver to lock on stronger signal by suppressing weaker but can fluctuate back and forth when two are nearly equal.

## Slide 27: Noise Suppression
Preemphasis
  FM transmissions provide artificial boost to electrical amplitude of higher frequencies.
  Increasing relative strength of high-frequency components of audio signal before it is fed to modulator.

## Slide 28: Noise Suppression
Preemphasis
  Noise remains the same; desired signal strength increased.
  Deemphasis network normally inserted between detector and audio amplifier in receiver.