## Slide 1
Communications Circuits
4

## Slide 2: Amplifiers
Classes of Amplification
  Amplifier
    Uses one or more active devices to increase voltage or current amplitude of electrical signal applied to its input.
  Classified by amount of time during each input cycle that active device within circuit conducts current.

## Slide 3: Amplifiers
Classes of Amplification
  Conduction angle defines portion of input signal during which active device is turned on.

## Slide 4: Amplifiers
Classes of Amplification
  Class A
    Most linear form; active device conducts current over full 360° of input cycle; inefficient.
  Class B
    Conduction angle of 180°; active device conducts for exactly half of each input cycle; nonlinear, but efficiency improved over class A.

## Slide 5: Amplifiers
Classes of Amplification
  Class C
    Produce brief, high-energy pulses at output of active device; efficiencies in excess of 75%.
  Class D
    Switching amplifiers; rely in part on principle of pulse-width modulation.

## Slide 6: Oscillators
Oscillator
  Generates waveform by converting direct-current energy to alternating current; first stages of transmitters.
  Choice of oscillator type based on:
    Output frequency required.
    Frequency stability required.
    Range of frequency variability, if needed.
    Allowable waveform distortion.
    Power output required.

## Slide 7: Oscillators
LC Oscillator
  Parallel-resonant circuit.
  Basically feedback amplifiers; feedback serving to increase or sustain self-generated output.

## Slide 8: Oscillators
LC Oscillator
  Positive feedback
    Fed-back signal in phase with input signal.
  Criteria for oscillation
    Barkhausen criteria.
  Types of oscillators
    Hartley, Colpitts, Clapp.

## Slide 9: Oscillators
Crystal Oscillator
  Uses piezoelectric crystal as inductive element of LC circuit.
  Crystal (usually quartz) has resonant frequency of its own.
  Optimum performance obtained when coupled with external capacitance.
    See Table 4-1: Typical Performance Comparison for Crystal Oscillators

## Slide 10: Table 4-1 Typical Performance Comparison for Crystal Oscillators

## Slide 11: Frequency-Selective Circuits
Reactance
  Inductors and capacitors exhibit reactance.
  Manifests as opposition to current flow in ac circuits; measured in ohms.
  Any quantity expressed in ohms ultimately defined as ratio of voltage to current.

## Slide 12: Frequency-Selective Circuits
Reactance
  Reactance
    Directly proportional to both inductance and frequency.
  Capacitive reactance
    Inversely proportional to both frequency and capacitance.

## Slide 13: Frequency-Selective Circuits
Practical Inductors and Capacitors
  Inductors
    Store energy in surrounding magnetic field; lose energy in their winding resistances.
  Capacitors
    Store energy in electric field between plates; lose energy from leakage between plates.

## Slide 14: Frequency-Selective Circuits
Resonance
  Inductive and capacitive reactances are equal.

## Slide 15: Frequency-Selective Circuits
LC Bandpass Filter
  Filter’s quality factor provides a measure of how selective (narrow) its passband is compared to its center frequency.
Parallel LC Circuits
  Sometimes called tank circuit.
  Energy is stored in each reactive element (L and C), first in one and then released to the other.

## Slide 16: Frequency-Selective Circuits
Types of LC Filters
  Constant-k filters
    Capacitive and inductive reactances made equal to constant value, k.
  M-derived filters
    Tuned circuit in filter to provide nearly infinite attenuation at a specific frequency.

## Slide 17: Frequency-Selective Circuits
Types of LC Filters
  Roll-off
    Rate of attenuation is steepness of filter’s response curve.

## Slide 18: Frequency-Selective Circuits
High-Frequency Effects
  Simple wire exhibits small amount of inductance; longer the wire, greater the inductance.
  Minimize all lead lengths in RF circuits.

## Slide 19: Frequency-Selective Circuits
Crystal Filters
  Designed to exhibit very high values of Q.
  Improved performance possible when two or more crystals combined in a single filter circuit.

## Slide 20: Frequency-Selective Circuits
Ceramic Filters
  Utilize piezoelectric effect as crystals do; constructed from lead zirconate-titanate.
  Low cost, rugged, smaller size than crystal filters.

## Slide 21: Frequency-Selective Circuits
Mechanical Filters
  Mechanically resonant; receives electrical energy, converts it to mechanical vibration, then converts mechanical energy back into electrical energy as the output.

## Slide 22: Frequency-Selective Circuits
SAW Filters
  Modern variant of mechanical filter; surface-acoustic-wave (SAW).
  Use in high-quality, analog color televisions.
  Rely on surface effects in piezoelectric material.

## Slide 23: Mixing and Multiplication Circuits
Amplitude modulation is a form of mixing.
Mixing
  Two or more signals applied to nonlinear device.

## Slide 24: Mixing and Multiplication Circuits
Frequency/phase modulation
  Multiplication of carrier and intelligence signals.
Balanced Modulator
  Suppress the carrier, leaving only two sidebands.

## Slide 25: Mixing and Multiplication Circuits
LIC Balanced Modulator
  Superior component-matching characteristics obtainable when devices fabricated on same silicon chip.
Product Detector
  Most common method of detecting SSB signal.

## Slide 26: The Phase-Locked Loop and Frequency Synthesis
Phase-Locked Loop (PLL)
  Electronic feedback control system.
Varactor Diodes
  Acts as variable capacitor in oscillator tank circuit.

## Slide 27: The Phase-Locked Loop and Frequency Synthesis
PLL Capture and Lock
  PLL in lock whenever VCO frequency matched to the reference.
  Capture range contains frequencies over which PLL circuit can initially acquire lock.

## Slide 28: The Phase-Locked Loop and Frequency Synthesis
Frequency Synthesis
  PLL frequency synthesizer allows a range of frequencies to be generated from stable, single-frequency reference (crystal-controlled oscillator).

## Slide 29: The Phase-Locked Loop and Frequency Synthesis
Programmable Division
  Most common programmable dividers are decades or divide-by-16 counters.
  Various logic families
    CMOS and TTL.

## Slide 30: The Phase-Locked Loop and Frequency Synthesis
Two-Modulus Dividers
  In one mode synthesizer divides by N and in the other mode, by N + 1.
Direct Digital Synthesis (DDS)
  Improves on repeatability and drift problems of analog units that require select-by-test components.
  Limited maximum output frequency and greater complexity/cost considerations.