## Slide 1
Transmitters
5

## Slide 2: AM Transmitted Systems
Modulator Circuits
  Amplitude modulation (AM) generated as result of mixing or combining carrier and intelligence frequencies within nonlinear device or circuit.
  Modulator
    Transmitter mixer circuit designed to produce modulation directly.
  Modulation type
    Where intelligence is injected.

## Slide 3: AM Transmitted Systems
Neutralization
  Vacuum tubes still found in areas of electronic communications.
  Neutralizing capacitor
    Path for return of a signal 180° out of phase with signal returned from plate to grid.
  Self-oscillation a problem for all RF amplifiers.

## Slide 4: AM Transmitted Systems
High- and Low-Level Modulation
  High-level modulation scheme
    Intelligence added at last possible point before transmitting antenna.
  Low-level modulation
    Intelligence injected at a point before final output stage.
  Choice of high- or low-level modulation driven by required power output and trade-offs.

## Slide 5: AM Transmitted Systems
Transistor High-Level Modulator
  Class-C operation provides abrupt nonlinearity when device switches on and off.
  This is in contrast to gradual nonlinearities offered by transistor at high and low levels of class A bias.

## Slide 6: AM Transmitter Measurements
Trapezoid Patterns
  Standard oscilloscope display of transmitted AM signal will indicate any gross deficiencies.
  Technique is better if dual-trace scope used to allow intelligence signal to be superimposed on AM signal.
  Trapezoidal pattern
    Improvement to this method.

## Slide 7: AM Transmitter Measurements
Meter Measurement
  It is possible to make transmitter checks with a dc ammeter in collector of modulated stage.

## Slide 8: AM Transmitter Measurements
Spectrum Analyzers
  Transmitter troubleshooting in frequency domain reliant on spectrum analyzers for determining spectral characteristics of output and identifying unwanted and potentially interfering frequency components.

## Slide 9: AM Transmitter Measurements
Harmonic Distortion Measurements
  Made by applying spectrally pure signal source to device under test (DUT).
  Quality of measurement dependent on harmonic distortion of signal source and spectrum analyzer.
  Source provides signal to DUT; spectrum analyzer used to monitor output.

## Slide 10: AM Transmitter Measurements
Special RF Signal Measurement Precautions
  Effects must be understood when testing RF signals as compared to audio frequencies.
    Loading of high-Q parallel-resonant circuits by relatively low impedance instrument.
    Frequency response shift caused by test lead and instrument input capacitance.

## Slide 11: AM Transmitter Measurements
Measuring Transmitter Output Power
  Dummy antenna
    Resistive load used in place of regular antenna.
  Prevents undesired transmissions that may otherwise occur and damage to output circuits that may occur under unloaded conditions.

## Slide 12: SSB Transmitters
Filter Method
  Unwanted sideband suppressed.
  Traditional method; widely used in analog SSB applications.
Phase Method
  Phase discrimination may be used to cancel one sideband of DSB signal.
  Sine and cosine waves lend themselves to digital processing techniques.

## Slide 13: FM Transmitters
Composed of oscillators, amplifiers, filters, and modulating stages.
Direct FM Generation
  Frequency of carrier oscillator directly varied by modulating signal.
  Varactor diode used to generate FM directly.
  Reactance modulator
    Transistor made to function as variable capacitance.

## Slide 14: FM Transmitters
Direct FM Generation
  Crosby systems
    FM systems utilizing direct generation with AFC.
  Exciter
    Circuitry that generates modulated signal.
  Discriminator
    Opposite of a VCO; provides a dc level output based on frequency input.

## Slide 15: FM Transmitters
Indirect FM Generation
  Armstrong
    Modulation of stable crystal oscillator without cumbersome AFC circuitry; provides carrier accuracies identical to crystal accuracy.
  Indirectly generates FM by changing the phase of a crystal oscillator’s output.

## Slide 16: FM Transmitters
Indirect FM Generation
  Not capable of much frequency deviation.
  Dynamic action of phase detector/VCO and feedback path is basis of a PLL.

## Slide 17: Stereo FM
Stereo radio broadcast
  Two separate 30-Hz to 15-kHz signals used to modulate the carrier.
    Stereo transmitter has modulating signal.
    Frequency-division multiplexing
      Two different signals multiplexed together by having them coexist in two different frequency ranges.
    Stereo FM more prone to noise than monophonic (monaural) broadcasts.