## Slide 1
Receivers
6

## Slide 2: Receiver Characteristics: Sensitivity and Selectivity
Sensitivity
  Minimum input signal (voltage) required to produce specified output.
  Noise floor
    Input noise.
Selectivity
  Extent to which receiver capable of differentiating between desired signal and other frequencies.

## Slide 3: The Tuned Radio-Frequency Receiver
Tuned Radio Frequency (TRF) Receivers
  Three stages of RF amplification; each stage preceded by separate variable-tuned circuit.
  Adjusted by individual variable capacitors.
  Variable selectivity over its intended tuning range.

## Slide 4: Superheterodyne Receivers
Frequency Conversion
  Mixer (first detector) performs frequency conversion process.
Tuned-Circuit Adjustment
  Key to superheterodyne operation
    To make LO frequency track with circuit or circuits that are tuning incoming radio signal so difference is constant frequency (the IF).

## Slide 5: Superheterodyne Receivers
Image Frequency
  Undesired received signal.
  Most of gain in superheterodyne receiver occurs in IF amplifiers at fixed frequency.
  Double conversion
    Solve image frequency problems.
  RF amplifier with its own input tuned circuit helps to minimize problem.

## Slide 6: Superheterodyne Receivers
Double Conversion
  Stepping down RF signal to a first, high IF frequency and then mixing down again to second, lower, final IF frequency.
  Image frequencies not major problem for low-frequency carriers.

## Slide 7: Superheterodyne Receivers
Up-Conversion
  IF at higher frequency than received signal.
  Preselector
    Responsible for image frequency rejection characteristics of receiver.

## Slide 8: Superheterodyne Receivers
A Complete AM Receiver
  Auxiliary AGC diode
    Additional gain control for strong signals; enhances range of signals that can be compensated for by receiver.

## Slide 9: Superheterodyne Receivers
SSB Receivers
  Additional mixer and beat-frequency oscillator (BFO) must replace detection scheme employed by AM receiver designed for reception of full-carrier, double-sideband transmissions.

## Slide 10: Superheterodyne Receivers
FM Receivers
  Discriminator
    Amplitude variations derived in response to frequency or phase variations.
  RF amplifiers
  FET RF amplifiers
  MOSFET RF amplifiers
  Limiters
  Limiting and sensitivity

## Slide 11: Superheterodyne Receivers
Discrete Component FM Receiver
  Layout of superheterodyne receiver composed of discrete analog components
    Understanding of how individual subsystem blocks fit together to form complete system.
  Modern receiver designs rely heavily on large-scale integrated circuits and digital signal processing techniques.

## Slide 12: Direct Conversion Receivers
Direct Conversion Receivers
  Perform frequency-conversion and demodulation functions in one step, rather than two.
  Mixer difference-frequency output is intelligence rather than higher-frequency IF.
  Requires no IF filter; no need for separate demodulator stage.
  Immune to image-frequency problem.

## Slide 13: Demodulation and Detectors
AM Diode Detector
  Difference frequencies created by AM receiver detector represent the intelligence; nonlinear device.
  Result confirmed in time and frequency domains.
  Diode will rectify incoming signal, distorting it.
  Advantages of diode detector is its simplicity.

## Slide 14: Demodulation and Detectors
Detection of Suppressed-Carrier Signals
  Simple diode detector cannot be used to demodulate SSB signal because one of frequencies, carrier, is absent.
  Simple way to form SSB detector
    Use mixer stage (product detector).
  Synchronous detector
    Regenerates carrier from received signal.

## Slide 15: Demodulation and Detectors
Demodulation of FM and PM
  FM discriminator extracts intelligence modulated onto carrier in form of frequency variations.
    Slope detector
    Foster-Seeley discriminator
    Ratio detector
    Quadrature detector
    PLL FM demodulator

## Slide 16: Demodulation and Detectors
SCA Decoder
  Subsidiary communication authorization (SCA)
    Frequency-multiplexed on FM modulating signal.

## Slide 17: Receiver Noise, Sensitivity, and Dynamic Range Relationships
Noise and Receiver Sensitivity
  Wider the bandwidth, greater noise power and higher noise floor.
  If lower S/N required, better receiver sensitivity necessary.
  SINAD (SIgnal plus Noise and Distortion)

## Slide 18: Receiver Noise, Sensitivity, and Dynamic Range Relationships
Dynamic Range
  Amplifier or receiver is input power range over which it provides useful output.
Intermodulation Distortion Testing
  Test amplifier for its IMD by comparing two test frequencies to level of specific IMD product.

## Slide 19: Automatic Gain Control And Squelch
Obtaining the AGC Level
  Most AGC systems obtain AGC level just following the detector.
Controlling the Gain of a Transistor
  Variable dc AGC level used to control gain of common-emitter transistor amplifier stage.

## Slide 20: Automatic Gain Control And Squelch
Delayed AGC
  Simple automatic gain control (AGC).
  Presents no reduction in gain for weak signals.

## Slide 21: Automatic Gain Control And Squelch
Auxiliary AGC
  Used to cause step reduction in receiver gain at arbitrarily high value of received signal.
Variable Sensitivity
  Manual AGC control; user controls receiver gain (sensitivity) to suit requirement.

## Slide 22: Automatic Gain Control And Squelch
Variable Selectivity
  Variable bandwidth tuning (VBT): obtain variable selectivity.

## Slide 23: Automatic Gain Control And Squelch
Noise Limiter
  Silence receiver for duration of noise pulse.
Metering
  S meter
    Provides visual indication of received signal strength; reads dc current.

## Slide 24: Automatic Gain Control And Squelch
Squelch
  Communications receivers have squelch circuits to silence audio amplifier stages until carrier detected.
  Received audio amplified and passed on to speaker.

## Slide 25: Automatic Gain Control And Squelch
Squelch
  Continuous Tone Coded Squelch System (CTCSS)
    Allows multiple user groups to share common communications channel without having to listen to each other’s transmissions.
  Digital Coded Squelch (DCS)
    More-advanced squelch system.