## Slide 1
Digital Communications Techniques
7

## Slide 2: Introduction to Digital Communications
For communications to take place digitally, analog signals converted to discrete samples for transmission as data.
Data coded (prepared) for transmission over communications channel that does not provide direct electrical continuity between transmitter and receiver.

## Slide 3: Introduction to Digital Communications
Error detection/correction techniques deployed to enhance performance in presence of noise.

## Slide 4: Pulse Modulation and Multiplexing
Pulse Modulation
  Transmit only samples and let receiver reconstruct total signal with high degree of accuracy.
Multiplexing
  Conveying two or more information signals over single transmission channel.

## Slide 5: Pulse Modulation and Multiplexing
Time-division Multiplexing (TDM)
  Computer time sharing; several users make use of computer simultaneously.

## Slide 6: Pulse Modulation and Multiplexing
Pulse-Amplitude Modulation (PAM)
  Pulse amplitude made proportional to amplitude of modulating signal.
Pulse-Width Modulation (PWM)
  Form of PTM.
  Pulse-duration modulation (PDM).
  Pulse-length modulation (PLM).
  Basis for class D power amplification.

## Slide 7: Pulse Modulation and Multiplexing
Pulse-Position Modulation (PPM)
  Superior noise characteristics.
  Major use for PWM is to generate PPM.
Demodulation
  Reproducing original analog signal.
  PPM signal converted to PWM, then demodulated using technique for demodulating PWM.

## Slide 8: Sample Rate and Nyquist Frequency
Act of sampling an analog waveform is form of modulation because of interaction that takes place between sampled pulses and information signal.

## Slide 9: Sample Rate and Nyquist Frequency
Sample rate must be at least twice the highest frequency of intelligence or information signal to be sampled.
Nyquist rate
  Minimum sample rate.

## Slide 10: Pulse-Code Modulation
PCM Encoding Steps
  Sampling
  Quantizing
  Coding
PCM Decoding Steps
  Regeneration
  Decoding
  Reconstruction

## Slide 11: Pulse-Code Modulation
The Sample-and-Hold Circuit
  Functions as modulator in PCM system; information signal sampled.
  Junction field-effect transistor (JFET).
  Metaloxide semiconductor field-effect transistor (MOSFET).

## Slide 12: Pulse-Code Modulation
The Sample-and-Hold Circuit
  Acquisition time
    Amount of time it takes for hold circuit to reach its final value.
  Aperture time
    Time S/H circuit must hold sampled voltage.

## Slide 13: Pulse-Code Modulation
Natural and Flat-top Sampling
  Natural sampling
    Tops of sampled waveform retain their natural shape.
  Flat-top sampling
    Sample signal voltage held constant between samples.

## Slide 14: Pulse-Code Modulation
Quantization
  Each level corresponds to different binary number.
  Each quantization level step-size
    Quantile or quantile interval; determines resolution of digitizing system.

## Slide 15: Pulse-Code Modulation
Dynamic Range/Signal-to-Noise Calculations
  Dynamic range (DR)
    Ratio of maximum input or output voltage level to smallest voltage level quantized and/or reproduced by converters.
  Signal-to-noise ratio (S/N).
  Signal-to-quantization-noise level (S/N)q.

## Slide 16: Pulse-Code Modulation
Companding
  Nonlinear or nonuniform coding
    Each quantile interval step-size may vary in magnitude.

## Slide 17: Pulse-Code Modulation
Idle Channel Noise
  Noise source of small amplitude that exists in channel independent of analog input signal and quantized by ADC converter.
Amplitude Companding
  Volume compression before transmission and expansion after detection.

## Slide 18: Pulse-Code Modulation
Coding and Analog-to-Digital Conversion
  Coding
    Each quantized value as binary word.
  Function of analog-to-digital (ADC) conversion.

## Slide 19: Pulse-Code Modulation
Digital-to-Analog Converters
  Digital-to-analog (DAC) conversion
    Reconstruction of analog signal from PCM representation.
  Convert digital (binary) bit stream to analog signal.

## Slide 20: Coding Principles
Decreasing an error depends on transmission system used and digital encoding and modulation techniques employed.
Hamming distance
  Distance between each defined state (minimum distance).
  See Table 7-1: Error Detection and Correction Based on Dmin

## Slide 21: Table 7-1 Error Detection and Correction Based on Dmin

## Slide 22: Coding Principles
XOR operation that yields smallest result tells which is correct code.

## Slide 23: Code Error Detection and Correction
Parity
  Most common method of error detection.
  Single (parity) bit added to each code representation.
  Automatic request for retransmission (ARQ).
  Display of unused symbol for character with parity error (symbol substitution).

## Slide 24: Code Error Detection and Correction
Block Check Character (BCC)
  Block
    Group of characters transmitted with no time gap between them.
  Followed by end-of-message (EOM) indicator and then BCC.
  Longitudinal redundancy check (LRC).

## Slide 25: Code Error Detection and Correction
Cyclic Redundancy Check (CRC)
  One of the most powerful error-detection schemes; mathematical technique.
CRC Code-Dividing Circuit
  At receive side, received code verified by feeding received serial CRC code into CRC dividing circuit.

## Slide 26: Code Error Detection and Correction
Hamming Code
  Techniques that allow correction at receiver are forward error-correcting (FEC) codes.
  Requirement
    Sufficient redundancy to allow error correction without further input from transmitter.
  Can detect only single error.

## Slide 27: Code Error Detection and Correction
Reed–Solomon Codes
  Forward error-correcting codes (FEC) like Hamming code.
  Can detect multiple errors.
  Interleaving
    Technique used to rearrange data into nonlinear ordering scheme to improve chance of correcting data errors.

## Slide 28: Digital Signal Processing
Digital Signal Processing (DSP)
  Mathematical functions to control characteristics of digitized signal.
  Extract information from processed signal, usually in presence of noise.
  Occurs in real time/nearly real time.

## Slide 29: Digital Signal Processing
Digital Signal Processing (DSP)
  Easily reprogrammed; more flexible.
  Emulates almost all communications system functions.
  DSP processing and filtering used in almost every area of electronic communication.

## Slide 30: Digital Signal Processing
DSP Filtering
  Impulse
    Infinitely narrow pulse.
  Filters that exhibit properties of sinc function (sin(x)/x filters).

## Slide 31: Digital Signal Processing
DSP Filtering
  Filter to which impulse applied at its input will output signal whose impulse response is equal to that of filter frequency response.
  IIR filter recursive.
  FIR filter nonrecursive.

## Slide 32: Digital Signal Processing
DSP Filtering
  Difference equation
    Present digital sample value of input signal with number of previous input values (possibly previous output values) to generate output signal.
  Algorithms employing previous output values are recursive or iterative.
  DSP techniques increasingly form heart of digital implementations of all types.