## Slide 1
Digital Modulation and Demodulation
8

## Slide 2: Digital Modulation Techniques
Digital Modulation
  Modifying amplitude, frequency, or phase characteristics of carrier with data stream representing ones and zeroes of computer language.
  Simplest schemes change carrier state with each bit of data.
  Amplitude-shift keying (ASK).
  Phase-shift keying (PSK).

## Slide 3: Digital Modulation Techniques
Amplitude-Shift Keying
  “Keying” holdover from Morse code era.
  Continuous wave (CW)
    Carrier conveying intelligence by simply turning it on or off according to prearranged code.
  Two-tone modulation
    Form of AM, but in it carrier always transmitted.

## Slide 4: Digital Modulation Techniques
Frequency-shift Keying
  Frequency modulation
    Modulating wave shifts output between two predetermined frequencies.
  Generation of FSK accomplished by switching additional capacitor into tank circuit of oscillator when transmitter keyed.

## Slide 5: Digital Modulation Techniques
Phase-shift Keying
  Transmitted binary data cause phase of sine-wave carrier to shift by defined amount.

## Slide 6: Digital Modulation Techniques
Synchronization and Carrier Reinsertion
  Carrier synchronizer
    Producing reference carrier signal for product detector.
  PLL
    Heart of carrier synchronizer; used for all forms of digital modulation.

## Slide 7: Digital Modulation Techniques
Differential Phase-shift Keying (DPSK)
  DPSK uses BPSK vector relationship for generating an output.
  DPSK receiver simpler to implement.
  Does not require coherent carrier recovery subsystem.

## Slide 8: Digital Modulation Techniques
Minimum Shift Keying
  Widely used variation on FSK/PSK; used in cordless phones.
  Continuous-phase FSK
    Periods of mark and space frequencies such that cycles of sine-wave carrier cross zero right at edges of modulating-signal pulse transitions.
  Minimizes bandwidth by ensuring smooth transition between data states.

## Slide 9: Bandwidth Considerations of Modulated Signals
Bandwidth of channel will not be infinite.
Transmitted pulse not perfect rectangle.
Bandwidth requirements for data stream depend on encoding method used to transmit data.
Sidebands
  Sum and difference frequencies.

## Slide 10: Bandwidth Considerations of Modulated Signals
Bandwidth of modulated signal twice that of highest modulating signal frequency.
Symbol
  Grouping of two or more bits.
Baud rate
  Symbol rate.

## Slide 11: M-Ary Modulation Techniques
M-Ary PSK
  Employs two data channels; one phase-shifted by 90° with respect to the other.
  Non-phase-shifted channel
    I (for “in-phase”).
  Phase-shifted channel
    Q (for “quadrature”).

## Slide 12: M-Ary Modulation Techniques
M-Ary PSK
  Each channel contributes to direction of vector within phase constellation.
  QPSK transmissions
    Data bandwidth compression.

## Slide 13: M-Ary Modulation Techniques
M-Ary PSK
  QPSK and forms of M-Ary modulation carried out with DSP-based chipsets.
  I and Q bit streams considered two independent components of modulated signal that, when combined, form composite signal.

## Slide 14: M-Ary Modulation Techniques
Quadrature Amplitude Modulation
  QPSK technique can be extended to more than four phase states.
  If eight states, each point on constellation represents 3-bit binary symbol.
  Constellation pattern visual indication of system linearity and noise performance.

## Slide 15: M-Ary Modulation Techniques
Offset Modulation
  Because QAM schemes based in part on amplitude modulation, they suffer from drawbacks associated with any form of AM.

## Slide 16: Spectral Efficiency, Noise Performance, and Filtering
Spectral Efficiency
  Combining bits into multiple-bit symbols improves bandwidth efficiency.
  Bandwidth efficiency
    Measure of how well modulation scheme handles data within defined bandwidth.
    See Table 8-2: Spectral Efficiencies of Digital Modulation Formats

## Slide 17: Table 8-2 Spectral Efficiencies of Digital Modulation Formats

## Slide 18: Spectral Efficiency, Noise Performance, and Filtering
Noise Performance
  Modulation methods having fewest symbols or lower spectral efficiencies have best performance in presence of noise.
    Bit error rate (BER)
    Signal-to-noise (S/N) ratio
    Carrier-to-noise (C/N) ratio

## Slide 19: Spectral Efficiency, Noise Performance, and Filtering
Filtering
  Goal
    Reduce transmitted bandwidth without removing content of data to be transmitted.

## Slide 20: The Complex Exponential and Analytic Signals
Complex Numbers
  Impedance
    AC quantity (Z) composed of both resistance (R) and reactance (X).
  Reactive components 90° out of phase with resistive component.
  Complex operations
    Arithmetic operations involving both real and imaginary quantities.

## Slide 21: The Complex Exponential and Analytic Signals
Analytic Frequency
  Concept abstract; useful in how digital modulation and demodulation carried out in DSP.

## Slide 22: The Complex Exponential and Analytic Signals
DSP Modulation and Demodulation
  Modulation of I/Q signal
    Process of frequency up-conversion; moving baseband frequency range to higher frequency range of carrier.
  Baseband signal both positive and negative frequency components.
  Implementations of modulators and demodulators as DSP functions avoid all problems of analog circuitry.

## Slide 23: Wideband Modulation
Spread-Spectrum Techniques
  Occupied bandwidth deliberately made to be much greater than specified by Hartley’s law.
  Frequency hopping and direct sequence
    Spreading out transmitted energy over wide bandwidth.

## Slide 24: Wideband Modulation
Spread-Spectrum Techniques
  Cellular telephones, mobile Internet, wireless local-area networks (WLANs), automated data collection systems using portable scanners of universal product code (UPC) codes.

## Slide 25: Wideband Modulation
Spread-Spectrum Techniques
  Based on stream of data bits displaying pseudonoise (PN) characteristics.
  Spread-spectrum circuits have PN sequence generators integrated into system IC.

## Slide 26: Wideband Modulation
Spread-Spectrum Techniques
  Frequency-hopping spread spectrum
    Information signal modulates carrier switched in frequency in pseudorandom fashion.
  Direct-sequence spread spectrum (DSSS)
    Basis for cellular systems employing CDMA standard.

## Slide 27: Wideband Modulation
Orthogonal Frequency-Division Multiplexing (OFDM)
  Multi-carrier (multi-tone) modulation.
  Transmits data at slow rates over multiple carriers simultaneously; achieves high spectral efficiencies.
  Information divided into multiple data streams.

## Slide 28: Wideband Modulation
Orthogonal Frequency-Division Multiplexing (OFDM)
  OFDM modulation converse of demodulation.
  HD radio technology
    In-band on-channel (IBOC).
  Flash OFDM
    Spread-spectrum technology.