## Slide 1
Telephone Networks
9

## Slide 2: Basic Telephone Operation
Telephone Systems
  Tele means “far” and phone means “sound.”
  Worldwide grid of connections; point-to-point communications between many subscribers.

## Slide 3: Basic Telephone Operation
Telephone Systems
  Function of PBX and central office is the same
    Switching one telephone line to another.
  BORSCHT function for their line
    Circuitry residing on line cards handles.

## Slide 4: Basic Telephone Operation
Line Quality Considerations
  Existing cable infrastructure in U.S. 50 years old.

## Slide 5: Basic Telephone Operation
Attenuation Distortion
  Local loop for telephone transmissions
    Two-wire twisted-pair cable.
  Transmission dependent on wire diameter, conductor spacing, dielectric constant of insulation.
  Resistance of copper causes signal attenuation.

## Slide 6: Basic Telephone Operation
Attenuation Distortion
  Higher-frequency attenuation greatly curtailed by adding inductance in series with the cable.
  Attenuation distortion
    Difference in gain or loss at frequency with respect to reference tone 1004 Hz.

## Slide 7: Basic Telephone Operation
Delay Distortion
  Signal traveling down transmission line experiences some delay from input to output.

## Slide 8: Basic Telephone Operation
Telephone Traffic
  Intensifies between 9:00 and 11:00 in morning and 2:00 and 4:00 in afternoon.

## Slide 9: Basic Telephone Operation
The Unit of Traffic
  Trunk
    Circuit or path that carries its usage for one traffic call at a time.
  Traffic capacity of group of trunks
    Nature or distribution of call durations or holding time.

## Slide 10: Basic Telephone Operation
Congestion
  Calls unable to reach their destination as result of excess demand for system capacity.

## Slide 11: Basic Telephone Operation
Traffic Observation and Measurement
  Continuous traffic measurement done to detect and resolve potential sources of congestion.
  Traffic measurement studies determine customer calling patterns; basis for discounted toll rates.

## Slide 12: Digital Wired Networks
Communication Links and Protocols
  Simplex communication
    One direction only.
  Half duplex communication
    Both directions but only one can talk at a time.
  Full duplex
    Both parties can talk at same time.

## Slide 13: Digital Wired Networks
Communication Links and Protocols
  Synchronous operation
    Transmit- and receive-data clocks locked together.
  Asynchronous
    Clocks on transmitter and receiver not locked together.

## Slide 14: Digital Wired Networks
Communication Links and Protocols
  Protocol major functions:
    Framing
    Line control
    Flow control
    Sequence control

## Slide 15: Digital Wired Networks
Communication Links and Protocols
  Protocols
    Responsible for integration of control characters within data stream and classified according to their framing technique.

## Slide 16: Digital Wired Networks
Line Codes
  Format of pulses sent over communications link.
  Data first be coded or prepared for transmission.
  Eliminates need for data states to be represented in terms of absolute voltage levels.

## Slide 17: Digital Wired Networks
Line Codes
  Maintaining synchronization between transmitter and receiver clocks.
  Enable a form of error detection.

## Slide 18: Digital Wired Networks
Line Codes
  NRZ group of codes: encoding binary data.
    See Table 9-1: NRZ Codes

## Slide 19: Table 9-1 NRZ Codes

## Slide 20: Digital Wired Networks
Line Codes
  RZ codes: return-to-zero line-coding formats.
    See Table 9-2: RZ Codes

## Slide 21: Table 9-2 RZ Codes

## Slide 22: Digital Wired Networks
Line Codes
  Biphase codes
    Use in optical systems, satellite telemetry links, magnetic recording systems.
    See Table 9-3: Phase-Encoded and Delay-Modulation (Miller) Codes

## Slide 23: Table 9-3 Phase-Encoded and Delay-Modulation (Miller) Codes

## Slide 24: Digital Wired Networks
Line Codes
  Multilevel binary codes
    More than two levels representing the data.
    See Table 9-4: Multilevel Binary Codes

## Slide 25: Table 9-4 Multilevel Binary Codes

## Slide 26: Digital Wired Networks
Line Codes
  Transition between logic states results in fast change in rise or fall times of transmitted pulses.

## Slide 27: Digital Wired Networks
Line Codes
  Coding scheme chosen determined by available bandwidth and need for transmitter and receiver to maintain synchronization.

## Slide 28: The T-Carrier System and Multiplexing
Time-Division Multiplexing (TDM)
  Each information signal accesses entire channel bandwidth for only small part of available time.

## Slide 29: The T-Carrier System and Multiplexing
Time-Division Multiplexing (TDM)
  Time-division multiple access (TDMA)
    Transport data from multiple sources over same serial data channel.
  T-carrier TDM system
    PCM data from channel 1 transmitted first, then data from channel 2, and so on in sequence before process repeats.

## Slide 30: The T-Carrier System and Multiplexing
Time-Division Multiplexing (TDM)
  T1 line
    Capacity for 24 individual, 64-kbps, time-division-multiplexed telephone calls.
  Fractional T1 (FT1)
    Only portion of T1 bandwidth being used.

## Slide 31: The T-Carrier System and Multiplexing
Time-Division Multiplexing (TDM)
  Point of presence
    Point where communication carrier brings in service to a facility.
  Channel service unit/data service unit (CSU/DSU).
    See Table 9-7: The CSU/DSU Alarms

## Slide 32: Table 9-7 The CSU/DSU Alarms

## Slide 33: The T-Carrier System and Multiplexing
Time-Division Multiplexing (TDM)
  Framing
    Maintain synchronization of receiving equipment.
    See Table 9-8: The Function of the 24 ESF Framing Bits

## Slide 34: Table 9-8 The Function of the 24 ESF Framing Bits

## Slide 35: The T-Carrier System and Multiplexing
Time-Division Multiplexing (TDM)
  Loopback capability
    Causes transmitted data to be routed back to originating location.

## Slide 36: The T-Carrier System and Multiplexing
Time-Division Multiplexing (TDM)
  T1 line coding
    AMI and B8ZS.
  System capacity and bit rate are not unlimited.

## Slide 37: Packet-Switched Networks
Frame Relay
  Packet switching network designed to carry data traffic over public data network (PDN).
  Data channels will not introduce bit errors or, at worst-case, minimal bit errors.
  Committed information rate (CIR).
  Committed burst information rate (CBIR).

## Slide 38: Packet-Switched Networks
Asynchronous Transfer Mode (ATM)
  Cell relay technique designed for voice, data, video traffic.
  Packets or cells processed at switching centers and directed to best network for delivery.
  Virtual path connection (VPC).
  Virtual channel connection (VCC).
    See Table 9-9: The Five ATM Service Classes

## Slide 39: Table 9-9 The Five ATM Service Classes

## Slide 40: Signaling System 7
SS7 uses physical out-of-band signaling.
ISDN and SS7 follow guidelines provided by OSI model.
Protocol analyzers
  Sort through messages to identify a problem.

## Slide 41: Troubleshooting
Digital communications troubleshooting
  Recognize digital pulse distortion and identify what causes it.
  Identify good pulse waveform.
  Identify frequency distortion.
  Describe effects of incorrect impedance on square wave.
  Identify noise on digital waveform.

## Slide 42: Troubleshooting
The Digital Waveform
  Square-wave signal is digital waveform.
Effects of Noise on the Pulse
  Signal’s amplitude changed by noise adding to it or subtracting from it.
Effects of Impedance on the Pulse
  Square wave pulse can show effects of impedance mismatches.

## Slide 43: Troubleshooting
Effects of Frequency on the Pulse
  Digital pulses will not be distorted when passing through amplifier with sufficient bandwidth or transmission line with sufficient bandwidth.
Eye Patterns
  Generated by “overlaying” on oscilloscope all digital bit signals received.