## Slide 1
Wave Propagation
13

## Slide 2: Electrical to Electromagnetic Conversion
Electrical energy fed into transmitting antenna must be converted to another form of energy for transmission.
Transmitting antenna converts its input electrical energy into electromagnetic energy.
Receiving antenna intercepts transmitted wave and converts it back into electrical energy.

## Slide 3: Electromagnetic Waves
Electromagnetic field
  Electric field and magnetic field.
Radio-frequency interference (RFI)
  Undesired radiation from radio transmitter.

## Slide 4: Electromagnetic Waves
Electromagnetic interference (EMI)
  Noise.
Maxwell’s equations
  Gauss’s law for electric fields, Gauss’s law for magnetic fields, Faraday’s law, Ampère-Maxwell law.

## Slide 5: Electromagnetic Waves
Wavefronts
  Surface joining all points of equal phase.
  Isotropic point source
    Electromagnetic wave radiates equally in all directions from point source in free space; spherical wavefront results.
  Isotropic source
    Radiates equally in all directions.

## Slide 6: Waves Not in Free Space
Reflection
  Radio waves reflected by any medium.
  Angle of incidence equal to angle of reflection.
Refraction
  When waves pass from a medium of one density to another medium with a different density.

## Slide 7: Waves Not in Free Space
Diffraction
  Waves traveling in straight paths bend around an obstacle.

## Slide 8: Ground- and Space-Wave Propagation
Four modes of getting radio wave from transmitting to receiving antenna:
  Ground wave
  Space wave
  Sky wave
  Satellite communications

## Slide 9: Ground- and Space-Wave Propagation
Ground-Wave Propagation
  Ground wave
    Radio wave that travels along Earth’s surface; changes in terrain strong effect.
  Attenuation of ground waves directly related to surface impedance of Earth; function of conductivity and frequency.
  Only way to communicate into ocean with submarines.
Notes: <number>

## Slide 10: Ground- and Space-Wave Propagation
Space-Wave Propagation
  Direct wave most widely used mode of antenna communications; limited to line-of-sight transmission distances.
  Propagated wave
    Direct from transmitting to receiving antenna; does not travel along ground.

## Slide 11: Sky-Wave Propagation
Sky Wave
  Ability to strike ionosphere, be refracted from it to ground, strike ground, be reflected back toward ionosphere.
  Skipping
    Refracting and reflecting action of ionosphere and ground.

## Slide 12: Sky-Wave Propagation
Sky Wave
  Method of long-distance transmission.
  Ionosphere
    Three layers designated from lowest level to highest level as D, E, and F.

## Slide 13: Sky-Wave Propagation
Effects of the Ionosphere on the Sky Wave
  Critical frequency
    Highest frequency returned to Earth when transmitted vertically under given ionospheric conditions.
  Critical angle
    Highest angle wave of specific frequency can be propagated and returned from ionosphere.

## Slide 14: Sky-Wave Propagation
Effects of the Ionosphere on the Sky Wave
  Maximum usable frequency (MUF)
    Highest frequency returned to Earth at given distance.

## Slide 15: Sky-Wave Propagation
Effects of the Ionosphere on the Sky Wave
  Optimum working frequency
    Most consistent communication and best one to use.
  Skip zone
    No signal will be heard.

## Slide 16: Sky-Wave Propagation
Effects of the Ionosphere on the Sky Wave
  Fading
    Variations in signal strength that occur at receiver during time signal received.
  Ionospheric storms
    Cause radio communications to become erratic.
  Tropospheric scatter
    Signal aimed at troposphere.

## Slide 17: Satellite Communications
Satellite Communication System
  Uplink (transmitter)
  Orbiting satellite
  Downlink (receiver)
  Uplink and downlink
    Earth station (ground base).

## Slide 18: Satellite Communications
Satellite Communication System
  Transponder
    Electronic system performing reception, frequency translation, retransmission.
  Attitude controls
    Orbital corrections on satellite.
  Footprint
    Limited coverage area.

## Slide 19: Satellite Communications
Orbital Patterns
  Orbital patterns of satellites elliptical.
  Perigee (closest distance of orbit to Earth).
  Apogee (farthest distance of orbit from Earth).

## Slide 20: Satellite Communications
Orbital Patterns
  Geostationary orbits use equatorial orbit.
  Look angle
    Azimuth and elevation angles for Earth station antenna calculated so correct satellite can be seen.

## Slide 21: Satellite Communications
Global Positioning System
  Pinpoint geographic location information.
  GPS satellites transmit position data signals; GPS receiver processes time to receive each one.

## Slide 22: Satellite Communications
Multiplexing Techniques
  Frequency-division multiple access (FDMA).
  Time-division multiple access (TDMA).

## Slide 23: Satellite Communications
Earth Station Distance to and from Satellites
  Distance from Earth station to satellite; estimate time delay for transmitted signal to travel from Earth to satellite and back.
    See Table 13-2: Earth Satellite Measurements

## Slide 24: Table 13-2 Earth Satellite Measurements

## Slide 25: Satellite Communications
Earth Station Distance to and from Satellites
  Code division multiple access (CDMA).
  Very small aperture terminal (VSAT) fixed satellite communication systems.
  Ultrasmall aperture terminal mobile satellite (MSAT) systems.

## Slide 26: Satellite Communications
Satellite Radio
  U.S. two satellite radio services
    XM and Sirius.
  XM Satellite Radio service
    Two geostationary satellites.
  Sirius Satellite Radio service
    Three satellites in inclined orbit.

## Slide 27: Figure of Merit and Satellite Link Budget Analysis
Figure of merit (G/T)
  Provides performance measure for different satellite Earth stations.
  Larger the figure of merit (G/T), the better the Earth station system.
Satellite link budget
  Verifies required C/N and signal level to satellite receiver will be met to ensure satellite receiver outputs signal that meets specifications.

## Slide 28: Figure of Merit and Satellite Link Budget Analysis
Satellite Link Budget Calculation
  Evaluates quality of satellite link signal in terms of C/N; makes sure satellite link meets required C/N specifications.
  Determined from both uplink budget and downlink budget.
  Free-space path loss
    Attenuation of RF signal as it propagates through space and Earth’s atmosphere to and from satellite.