## Slide 1
Antennas
14

## Slide 2: Basic Antenna Theory
Transmit Antenna
  Conductor or system of conductors; transition from guided wave of electrical energy to electromagnetic wave propagating in free space.
Receive Antenna
  Single conductor or array of conductors; converts electromagnetic wave cutting across it back to electrical signal in alternating voltages/currents.

## Slide 3: Basic Antenna Theory
Electromagnetic Energy
  Accelerating and decelerating electric charges moving within conductor.
Reciprocity
  Interchangeability for transmitting and receiving operations.
Polarization
  Orientation of electric field; same as antenna’s physical configuration.

## Slide 4: Half-Wave Dipole Antenna
Half-Wave Dipole Antenna
  Antenna having electrical length of one-half wavelength at applied frequency.
  Used with frequencies above 2 MHz.
  Impedance is ratio of voltage applied to antenna to current flowing in it at any point.
  Feeding Hertz antenna at center results in input impedance that is purely resistive.

## Slide 5: Half-Wave Dipole Antenna
Half-Wave Dipole Antenna
  Resonance
    Antenna with purely resistive impedance.
  Complex
    Antenna no longer half wavelength; impedance both resistive and reactive properties.

## Slide 6: Half-Wave Dipole Antenna
Half-Wave Dipole Antenna
  Antenna will work as long as there is current flow and ability to radiate.
  Maximum power transfer
    Only take place when source, feed-line, antenna impedances are equal.

## Slide 7: Half-Wave Dipole Antenna
Half-Wave Dipole Antenna
  Radiation pattern
    Radiated field strength around antenna.
  Directional
    Energy in certain directions at expense of lower energy in other directions.

## Slide 8: Half-Wave Dipole Antenna
Half-Wave Dipole Antenna
  Beamwidth
    Separation between half-power points on radiation pattern.
  Antenna gain
    Radiated energy in preferred direction at expense of other directions.

## Slide 9: Half-Wave Dipole Antenna
Half-Wave Dipole Antenna
  Effective radiated power (ERP)
    Gain of antenna multiplied by its power input.
  Effective isotropic radiated power (EIRP)
    Effective-power calculations involving antennas with gains expressed in dBi.

## Slide 10: Half-Wave Dipole Antenna
Half-Wave Dipole Antenna
  Polar plots
    Cross-sectional view; show three-dimensional radiation pattern in two dimensions.

## Slide 11: Radiation Resistance
Radiation Resistance
  Portion of antenna’s input impedance; result of power radiated into space.
  Varies with antenna length and height of antenna above ground.

## Slide 12: Radiation Resistance
Radiation Resistance
  Antenna constructed of very thin wire and isolated in space; electrical length corresponds closely to its physical length.
  Trial-and-error procedure to find exact length for optimum antenna performance.

## Slide 13: Antenna Feed Lines
Transfer energy from generator to antenna by transmission line (antenna feed line).
Resonant Feed Line
  Transmission line connected to center of antenna.

## Slide 14: Antenna Feed Lines
Nonresonant Feed Line
  Negligible standing waves if properly terminated in its impedance at antenna end.
  Operation practically independent of its length.

## Slide 15: Antenna Feed Lines
Delta Match
  When line does not match impedance of antenna, it is necessary to use special impedance matching techniques.
Quarter-Wave Matching
  To match low impedance of antenna to line of higher impedance.

## Slide 16: Monopole Antenna
Effects of Ground Reflection
  Used with frequencies below 2 MHz.
  Transmitter connected between antenna and ground; quarter-wave in physical length, half-wave operation may be obtained.

## Slide 17: Monopole Antenna
Effects of Ground Reflection
  Counterpoise
    Structure of wire erected short distance above ground and insulated from ground.
  Radiation pattern
    Omnidirectional.
  Loading coil
    Tune out capacitive appearance of antenna.

## Slide 18: Antenna Arrays
Half-Wave Dipole Antenna/Parasitic Element
  Antenna array
    More than one element or component.
  Parasitic array
    One or more of elements not electrically connected; also termed reflector because it “reflects” energy from driven element.

## Slide 19: Antenna Arrays
Half-Wave Dipole Antenna/Parasitic Element
  Driven array
    All elements connected.
  Yagi–Uda antenna
    Driven element and two or more parasitic elements.

## Slide 20: Antenna Arrays
Driven Collinear Array
  Combination of half-wave elements in which all elements placed end to end to form straight line.
Broadside Array
  Group of half-wave elements mounted vertically, one over the other.
Vertical Array
  Omnidirectional in horizontal plane.

## Slide 21: Special-Purpose Antennas
Log-Periodic Antenna
  Special case of driven array; wide-bandwidth or broadband antenna.
Small-Loop Antenna
  Magnetic field everywhere perpendicular to loop.

## Slide 22: Special-Purpose Antennas
Ferrite Loop Antenna
  Large number of loops wound about highly magnetic core (usually ferrite); increases greatly effective diameter of loops.

## Slide 23: Special-Purpose Antennas
Folded Dipole Antenna
  Same radiation pattern as standard half-wave dipole antenna; broadband operation.
Slot Antenna
  UHF and microwave frequencies; energy coupled into slot by waveguides or coaxial line feed connected across dimension of rectangular slot.

## Slide 24: Microwave Antennas
Use optical theory more than standard antenna theory.
Highly directive and provide high gain compared to half-wavelength dipole.
Microwaves divided into bands.
  See Table 14-1: Microwave Frequency Designations

## Slide 25: Table 14-1 Microwave Frequency Designations

## Slide 26: Microwave Antennas
Horn Antenna
  Gradual flare to waveguide to allow maximum radiation and minimum reflection back into guide
    Circular, pyramidal, sectoral horns.

## Slide 27: Microwave Antennas
The Parabolic Reflector Antenna
  Satellite and terrestrial communication systems; high gain and directivity.
  Name from geometric shape
    Paraboloid.

## Slide 28: Microwave Antennas
Lens Antenna
  Principle of zoning; savings in bulk and expense justify use of zoned lens.
Patch Antenna
  Square or round “island” of conductor on dielectric substrate backed by conducting ground plane.

## Slide 29: Microwave System Link Budget and Path-Loss Calculations
Many terrestrial communications systems involve point-to-point links where path of interest directly between transmitter and receiver, both installed at fixed locations.
Terrestrial microwave systems operate with relatively low transmitter powers.

## Slide 30: Microwave System Link Budget and Path-Loss Calculations
Radio transceivers available that provide very high data rates on unlicensed bands.

## Slide 31: Microwave System Link Budget and Path-Loss Calculations
Threshold sensitivity of receiver: minimum signal level present at receiver antenna input to produce acceptable bit-error rate (BER).
Because microwave communications are line of sight, a path study must be made to ensure no obstructions lie anywhere in line between transmitter and receiver.

## Slide 32: Microwave System Link Budget and Path-Loss Calculations
Ensure no objects close enough to produce diffraction effects.