## Slide 1
Waveguides and Radar
15

## Slide 2: Comparison of Transmission Systems
Mode of energy transmission depends on:
  Initial cost and long-term maintenance
  Frequency band to be used and information-carrying capacity
  Selectivity or privacy offered
  Reliability and noise characteristics
  Power level and efficiency

## Slide 3: Types of Waveguides
Any surface separating two media of distinctly different conductivities or permittivities has guiding effect on electromagnetic waves.

## Slide 4: Types of Waveguides
Best guiding surface is between good dielectric and good conductor.
Waveguide
  Hollow metal tube or pipe used to conduct electromagnetic waves through its interior.

## Slide 5: Types of Waveguides
Waveguide Operation
  Wave propagated by waveguide
    Electromagnetic.
  Energy propagates down waveguide in radio signal.

## Slide 6: Types of Waveguides
Waveguide Operation
  Configuration of fields determines mode of operation.
  TM (transverse magnetic)
    Mode of waveguide operation; magnetic field has no component in direction of propagation.

## Slide 7: Types of Waveguides
Dominant Mode of Operation
  TE 10 mode of operation dominant mode; most “natural” one for operation.
  Waveguide thought of as high-pass filter; only very high frequencies.
  Those above waveguide cutoff frequency, can be propagated.
    See Table 15-1: Waveguide Bands/Sizes

## Slide 8: Table 15-1 Waveguide Bands/Sizes

## Slide 9: Physical Picture of Waveguide Propagation
For wave to exist in waveguide, it must satisfy Maxwell’s equations through the waveguide.
  There can be no tangential component of electric field at walls of waveguide.
  Fields in TE10 waveguide resultant fields produced by ordinary plane electromagnetic wave that travels back and forth between sides of the guide.

## Slide 10: Other Types of Waveguides
Circular
  Found in radar applications where it is necessary to have continuously rotating section.
  Modes can be rotationally symmetrical.
  Cross-sectional area must be more than double that of rectangular guide.
  More expensive; takes up more space than rectangular guide.

## Slide 11: Other Types of Waveguides
Ridged
  Allows operation at lower frequencies for a given set of outside dimensions.
  Greater attenuation and combined with its higher cost, limits it to special applications.

## Slide 12: Other Types of Waveguides
Flexible
  Laboratory or applications where continuous flexing occurs.
  Spiral-wound ribbons of brass or copper.

## Slide 13: Other Waveguide Considerations
Waveguide Attenuation
  Waveguides propagate huge amounts of power.
  Frequencies below cutoff, attenuation in waveguide very large.

## Slide 14: Other Waveguide Considerations
Waveguide Attenuation
  Frequencies above cutoff, guide supports traveling waves.
    Bends and twists
      H bend, E bend, twist
    Tees
      Shunt, series, hybrid or magic
    Tuners
      Slide-screw and double-slug

## Slide 15: Termination and Attenuation
Impedance of waveguide
  Equal to ratio of strength of electric field to strength of magnetic field.
No place to connect fixed resistor to terminate it in its characteristic (wave) impedance as there is on coaxial cable.
Terminations designed to match impedance of guide to ensure minimum of reflection.

## Slide 16: Termination and Attenuation
Variable Attenuators
  Isolate source from reflections at its load to preclude frequency pulling.
  Adjust signal level.
  Measure signal levels.
  Flap attenuator and vane attenuator.

## Slide 17: Directional Coupler
Two-hole directional coupler
  Two pieces of waveguide with one side common to both guides and two holes in this common side.
Directional coupler
  Transfers energy from primary to adjacent secondary waveguide for energy traveling in guide in one direction only.

## Slide 18: Coupling and Waveguide Energy and Cavity Resonators
Three methods of coupling energy into or out of a waveguide:
  Probe, loop, aperture
Cavity Resonators
  Metal-walled chambers fitted with devices for admitting and extracting electromagnetic energy.
  Various physical forms; basic principles of operation the same for all.

## Slide 19: Coupling and Waveguide Energy and Cavity Resonators
Cavity Tuning
  Resonant frequency of a cavity varied by changing any of three parameters:
    Cavity volume
    Cavity inductance
    Cavity capacitance

## Slide 20: Radar
Radar acronym formed from words radio detection and ranging.
Process of locating objects measurement of three coordinates
  Range, angle of azimuth (horizontal direction), angle of elevation.

## Slide 21: Radar
Radar set
  Transmitter and receiver.
Larger a radar antenna; the better the system’s resolution.

## Slide 22: Radar
Radar Waveform and Range Determination
  Pulse repetition frequency (PRF) or pulse repetition rate (PRR)
    Number of pulses transmitted per second.
  Pulse repetition time (PRT)
    Time from beginning of one pulse to beginning of next pulse.

## Slide 23: Radar
Radar Waveform and Range Determination
  Time between pulses
    Rest time or receiver time.
  Radar mile equal to 2000 yd or 6000 ft.

## Slide 24: Radar
Radar System Parameters
  Second return echoes
    Arrive after transmission of next pulse.
  Maximum unambiguous range
    Range beyond which targets appear as second return echoes.

## Slide 25: Radar
Radar System Parameters
  Radar transmitter
    RF energy in extremely short pulses with long intervals of rest time.
  High peak power
    Desirable for strong echo.

## Slide 26: Radar
Basic Radar Block Diagram
  Pulse-forming circuits in modulator triggered by timer and generate high-voltage pulses of rectangular shape and short duration.
Doppler Effect
  Frequency of reflected signal shifted if there is relative motion between source and reflecting object.

## Slide 27: Microintegrated Circuit Waveguiding
Microwave integrated circuits (MICs)
  Thin-film hybrid and monolithic integrated circuits used at microwave frequencies.
  Stripline and microstrip determined by physical dimensions and type of dielectric.
  Microstrip circuit equivalents and dielectric waveguide.

## Slide 28: Troubleshooting
Waveguide problems similar to ordinary transmission line problems.
Waveguide used to carry large amounts of microwave power capable of burning skin and damaging eyesight.
Never work on waveguide runs or antennas connected to transmitter or radar system is off and cannot be turned on.