## Slide 1: EE 350 / ECE 490 Analog Communication Systems
Ch. 3 – Amplitude Modulation:
Receivers

## Slide 2: Objectives
Define the sensitivity and selectivity of a radio receiver
Describe the operation of a diode detector in n AM receiver
Sketch block diagrams for TRF and superheterodyne receivers
Understand the generation of image frequencies and describe how to suppress them
Recognize and analyze RF and IF amplifiers
Describe the need for automatic gain control and show how it can be implemented
Analyze the operation of a complete AM receiver system
Perform a test analysis on the power levels (dBm) at each stage of an AM receiver system

## Slide 3: 3-1 Receiver Characteristics
Figure 3-1 Simple radio receiver block diagram.
Low-noise RF amplifier from antenna, tuned to desired carrier and side-band frequencies
Circuit to separate intelligence from RF
Amplification of intelligence to drive speaker

## Slide 4: Sensitivity & Selectivity
Sensitivity is the minimum input needed to generate a discernible output. May be millivolts (for cheap) or nanovolts (for high-end). Must be able to distinguish the signal from the noise floor, and not inject more noise into the signal during amplification.
Selectivity is the ability to differentiate between the desired signal and other frequencies (interference and noise). You can be too selective, which will limit your bandwidth and cause loss of fidelity.

## Slide 5: TRF Sensitivity
Tuned Radio Frequency (TRF) sensitivity varies when spanning the broadcast spectrum from 550 kHz to 1550 kHz
Q for bandwidth at center frequency
However, at the two extremes the bandwidth
Is too selective or not enough

## Slide 6: 3-2 AM Detection
Figure 3-2 Nonlinear device used as a detector.
Passing the AM signal through a nonlinear device generates sum and difference frequencies, which are the intelligence.

## Slide 7: Figure 3-3 The Diode detector is a nearly ideal nonlinear device
Advantages:
High power signals
Acceptable distortion
Highly efficient
DC voltage for AGC
Disadvantages:
Diode absorbs power from tuned circuit reducing Q and selectivity
No amplification

## Slide 8: Diagonal Clipping
Figure 3-4 Diode detector component considerations. Dashed lines indicate average voltage during pulse.
R must be chosen such that RC is not too long or too short. C2 cannot be so small that it would be comparable to C1.

## Slide 9: Synchronous Detection
Figure 3-5(a) A synchronous AM detector circuit as implemented in Electronics WorkbenchTM Multisim.
Called product or heterodyne detectors.
Low distortion <1%
Better at following fast-modulation waveforms
Gain
3 dB better S/N

## Slide 10: Figure 3-5(b) The waveforms obtained from TP1 and TP2 for the synchronous AM detector provided in Figure 3-5(a).

## Slide 11: 3-3 Superheterodyne Receivers
Figure 3-6 Superheterodyne receiver block diagram.
The mixer is a nonlinear device, which generates sum and difference frequencies between the LO and carrier
Invented by Armstrong.

## Slide 12: Figure 3-7 Frequency conversion process.
The Mixer outputs are replicas of the AM signal, but with different carrier frequencies. The intelligence is the same.
The Intermediate Frequency (IF) amplifier can be designed and tuned to 455kHz (standard for AM) rather than having to vary like the TRF receiver.

## Slide 13: Figure 3-8 Frequency conversion.
By tuning the local oscillator together with the RF amplifier and mixer (ganging) the IF can always be maintained at the same 455 kHz.

## Slide 14: Figure 3-9 Variable ganged capacitor. Three capacitor elements on a common variable rotor to vary all three simultaneously. Each can be trimmed to fine tune their relative capacitance

## Slide 15: 3-4 Superheterodyne Tuning
Figure 3-10 Tracking considerations.
Tracking at all frequencies is nearly impossible so the circuit is tuned at three frequencies, resulting minor imperfections between those three points.

## Slide 16: Electronic Tuning
Figure 3-11 Varactor diode symbols and C/V characteristic.
Reverse biased diodes can be used as variable capacitors instead of ganged capacitors. These are known as varactor diodes, varicap diodes, or VVC diodes.

## Slide 17: Figure 3-12 Broadcast-band AM receiver front end with electronic tuning.

## Slide 18: 3-5 Superheterodyne Analysis
Figure 3-13 Image frequency illustration. Since the attenuation of the mixer input is not perfect, it is possible for other frequencies to be passed. These may be mixed into our desired signal and presented to the IF amplifier.
The image is not the only possible spurious response. Others are due to harmonics of the signal and LO mixing to create energy in the IF BW. (e.g. The “Half IF” spur.

## Slide 19: Figure 3-14 Image frequency not a problem in AM.
Image frequencies are not as much of a problem in AM broadcast due to the attenuation at the likely image frequencies. Higher frequency communication systems can suffer however, and so use tuned circuits at the RF and mixer inputs to increase image attenuation prior to mixing.

## Slide 20: RF Amplifiers
Figure 3-15 Dual-gate MOSFET RF amplifier.
RF Amp advantages:
Image freq. rejection
More gain
Improved noise
FET advantages:
High input impedance
Dual-gate FETs for AGC
I/O square-law relationship lowers distortion

## Slide 21: Mixer / LO
Figure 3-16 Typical mixer circuits.
Diodes are the simplest mixers. Schottky Diodes can be used up to 100 GHz.
Transistors can be used to mix and generate LO
LICs make implementation simpler

## Slide 22: Transistor IF Amplifier
Figure 3-17 Typical IF amplifiers. Transistor IF amp using 40673 Dual-Gate MOSFET. Notice the dual tuning circuits at the input and output. These are sold as blocks for common IF frequencies, with a variable transformer for fine-tuning. AGC is injected at the second gate.

## Slide 23: LIC IF Amplifer

## Slide 24: LIC IF Amplifier
Figure 3-17 (continued) Typical IF amplifiers.

## Slide 25: 3-6 Automatic Gain Control (AGC)
Figure 3-18 Development of AGC voltage.
Why you need AGC:
Tuning would be difficult, you’d miss weak stations, and strong stations would blow out your speakers
Signal changes constantly due to atmospheric effects
When mobile you need the radio to compensate for changing locations

## Slide 26: Controlling Transistor Gain
Figure 3-19 AGC circuit illustration.

## Slide 27: IF/AGC Amplifier
Figure 3-20 Wide-range IF/AGC amplifier. (Reprinted with permission from Electronic Design, Penton Publishing Company.)

## Slide 28: 3-7 AM Receiver System
Figure 3-21 AM broadcast superheterodyne receiver.

## Slide 29: LIC AM Receiver
Figure 3-22 TDA1572T AM receiver. (Courtesy of Philips Semiconductors.)

## Slide 30: AM Stereo
Figure 3-23 AM stereo block diagram showing the Motorola C-Quam Stereo method

## Slide 31: AM Stereo Phase
Figure 3-24 Phase relationships in AM stereo.

## Slide 32
Figure 3-25 C-Quam receiver system. (Courtesy of Motorola, Inc.) MC13024, uses PLL and VCLO

## Slide 33: Receiver Analysis
Figure 3-26 Receiver block diagram. Using dBm or dBW is very convenient for dealing with subsequent stages of amplification

## Slide 34: 3-8 Troubleshooting
Figure 3-27 Troubleshooting a self-excited mixer.

## Slide 35: Figure 3-28 Regulated power supply.

## Slide 36: Figure 3-29 Bridge rectifier and filter operating properly.

## Slide 37: Figure 3-30 Ripple increase caused by open diode.

## Slide 38: Figure 3-31 Testing an audio amplifier.

## Slide 39: 3-9 Troubleshooting with Multisim
Figure 3-32 An AM diode detector circuit as implemented with Electronics WorkbenchTM Multisim.

## Slide 40: Figure 3-33 Oscilloscope output traces from the diode detector.