## Slide 1: EE359 – Lecture 20 Outline
Direct Sequence Spread Spectrum
ISI and Inteference Rejection
Spreading Codes and Maximal Linear Codes
Synchronization
RAKE Receivers
Multiuser Spread Spectrum

## Slide 2: Review of Last Lecture FFT Implementation of OFDM
Design Issues
  PAPR, frequency offset, fading, complexity
  MIMO-OFDM
  v
x
cos(2pfct)
R bps
QAM
Modulator
Serial
To
Parallel
Converter
IFFT
X0
XN-1
x0
xN-1
Add cyclic
prefix and
Parallel
To Serial
Convert
D/A
TX
x
cos(2pfct)
R bps
QAM
Modulator
FFT
Y0
YN-1
y0
yN-1
Remove
cyclic
prefix and
Serial to
Parallel
Convert
A/D
LPF
Parallel
To Serial
Convert
RX

## Slide 3: Intro. to Spread Spectrum
Modulation that increases signal BW
  Mitigates or coherently combines ISI
  Mitigates narrowband interference/jamming
  Hides signal below noise (DSSS) or makes it hard to track (FH)
  Also used as a multiple access technique
Two types
  Frequency Hopping:
    Narrowband signal hopped over wide bandwidth
  Direction Sequence:
    Modulated signal multiplied by faster chip sequence

## Slide 4: Direct Sequence Spread Spectrum
Bit sequence modulated by chip sequence
Spreads bandwidth by large factor (G)
Despread by multiplying by sc(t) again (sc(t)=1)
Mitigates ISI and narrowband interference
s(t)
sc(t)
Tb=KTc
Tc
S(f)
Sc(f)
1/Tb
1/Tc
S(f)*Sc(f)
2

## Slide 5: ISI and Interference Rejection
Narrowband Interference Rejection (1/K)
Multipath Rejection (Autocorrelation r(t))
S(f)
S(f)
I(f)
S(f)*Sc(f)
Info. Signal
Receiver Input
Despread Signal
I(f)*Sc(f)
S(f)
aS(f)
S(f)*Sc(f)[ad(t)+b(t-t)]
Info. Signal
Receiver Input
Despread Signal
brS’(f)

## Slide 6: Maximal Linear Codes
Autocorrelation determines ISI rejection
  Ideally equals delta function
Maximal Linear Codes
  No DC component
  Large period (2n-1)Tc
  Linear autocorrelation
  Recorrelates every period
  Short code for acquisition, longer for transmission
  In SS receiver, autocorrelation taken over Tb
  Poor cross correlation (bad for MAC)
1
-1
N
Tc
-Tc

## Slide 7: Synchronization
Adjusts delay of sc(t-t) to hit peak value of autocorrelation.
  Typically synchronize to LOS component
Complicated by noise, interference, and MP
Synchronization offset of Dt leads to signal attenuation by r(Dt)
1
-1
2n-1
Tc
-Tc
Dt
r(Dt)

## Slide 8: RAKE Receiver
Multibranch receiver
  Branches synchronized to different MP components
These components can be coherently combined
  Use SC, MRC, or EGC
x
x
sc(t)
sc(t-iTc)
x
sc(t-NTc)
Demod
Demod
Demod
y(t)
Diversity
Combiner
dk
^

## Slide 9: Multiuser DSSS
Each user assigned a unique spreading code; transmit simultaneously over same bandwidth
Interference between users mitigated by code cross correlation
In downlink, signal and interference have same received power
In uplink, “close” users drown out “far” users (a1>>a2: near-far problem)
a
a
a1
a2

## Slide 10: Main Points
Spread spectrum increases signal bandwidth above that required for information transmission
  Benefits include ISI and interference rejection, multiuser technique
DSSS rejects ISI by code autocorrelation
  Maximal linear codes have good autocorrelation properties but poor cross correlation
Synchronization depends on autocorrelation properties of spreading code.
RAKE receivers combine energy of all MP
  Use same diversity combining techniques as before