## Slide 1: EE359 – Lecture 3 Outline
Log Normal Shadowing
Combined Path Loss and Shadowing
Cell Coverage Area
Model Parameters from Measurements

## Slide 2: Lecture 2 Review
Ray Tracing Models
Free Space Model
  Power falloff with distance proportional to d-2
Two Ray Model
  Power falloff with distance proportional to d-4
General Ray Tracing
  Used for site-specific models
Empirical Models
Simplified Model: Pr=PtK[d0/d]g, 2g8.
  Captures main characteristics of path loss

## Slide 3: Shadowing
Models attenuation from obstructions
Random due to random # and type of obstructions
Typically follows a log-normal distribution
  dB value of power is normally distributed
  m=0 (mean captured in path loss), 4<s<12 (empirical)
  LLN used to explain this model
  Decorrelated over decorrelation distance Xc
Xc

## Slide 4: Combined Path Loss and Shadowing
Linear Model: y lognormal
dB Model
Pr/Pt
(dB)
log d
Very slow
Slow
10logK
-10g

## Slide 5: Outage Probability and Cell Coverage Area
Path loss: circular cells
Path loss+shadowing: amoeba cells
  Tradeoff between coverage and interference
Outage probability
  Probability received power below given minimum
Cell coverage area
  % of cell locations at desired power
  Increases as shadowing variance decreases
  Large % indicates interference to other cells

## Slide 6: Model Parameters from Empirical Measurements
Fit model to data
Path loss (K,g), d0 known:
  “Best fit” line through dB data
  K obtained from measurements at d0.
  Exponent is MMSE estimate based on data
  Captures mean due to shadowing
Shadowing variance
  Variance of data relative to path loss model (straight line) with MMSE estimate for g
Pr(dB)
log(d)
10g
K (dB)
log(d0)
sy
2

## Slide 7: Main Points
Random attenuation due to shadowing modeled as log-normal (empirical parameters)
Shadowing decorrelates over decorrelation distance
Combined path loss and shadowing leads to outage and amoeba-like cell shapes
Cellular coverage area dictates the percentage of locations within a cell that are not in outage
Path loss and shadowing parameters are obtained from empirical measurements