## Slide 1: EE359 – Lecture 7 Outline
Multipath Intensity Profile
Doppler Power Spectrum
Shannon Capacity
Capacity of Flat-Fading Channels
  Fading Statistics Known
  Fading Known at RX

## Slide 2: Review of Last Lecture
Signal envelope distributions:
  CLT approx.  Rayleigh distribution (power exponential)
  When LOS present, Ricean distribution used
  Measurements support Nakagami distribution
Average Fade Duration:
  Rayleigh fading AFD
Wideband Channels
  Individual multipath components resolvable
  True when time difference between multipath components exceeds signal bandwidth
R
t1
t2
t3

## Slide 3: Characterizing Wideband Channels
Wideband channels introduce time-distortion (t) and time-variation (Doppler, r)
Wideband channels c(t,t) characterized by scattering function from Ac(t1,t2,Dt)=Ac(t,Dt)
t
Narrowband
t
Wideband
t
r
s(t,r)=FDt[Ac(t,Dt)]
Characterizes delay spread & Doppler

## Slide 4: Multipath Intensity Profile
Defined as Ac(t,Dt=0)= Ac(t)
  Determines average (TM ) and rms (st) delay spread
  Approximate max delay of significant m.p.
Coherence bandwidth Bc=1/TM
  Maximum frequency over which Ac(Df)=F[Ac(t)]>0
  Ac(Df)=0 implies signals separated in frequency by Df will be uncorrelated after passing through channel
t
Ac(t)
TM
t
f
Ac(f)
0
Bc

## Slide 5: Doppler Power Spectrum
Sc(r)=F[Ac(t=0,Dt)]= F[Ac(Dt)]
Doppler spread Bd is maximum doppler for which Sc (r)=>0.
Coherence time Tc=1/Bd
  Maximum time over which Ac(Dt)>0
  Ac(Dt)=0 implies signals separated in time by Dt will be uncorrelated after passing through channel
r
Sc(r)
Bd

## Slide 6: Shannon Capacity
Defined as the maximum MI of channel
Maximum error-free data rate a channel can support.
Theoretical limit (not achievable)
Channel characteristic
  Not dependent on design techniques

## Slide 7: Capacity of Flat-Fading Channels
Capacity defines theoretical rate limit
  Maximum error free rate a channel can support
Depends on what is known about channel
Fading Statistics Known
  Hard to find capacity
Fading Known at Receiver Only

## Slide 8: Capacity with Fading Known at Transmitter and Receiver
For fixed transmit power, same as with only receiver knowledge of fading
Transmit power P(g) can also be adapted
Leads to optimization problem

## Slide 9: Optimal Adaptive Scheme
Power Adaptation
Capacity
1
g
g0
g
Waterfilling

## Slide 10: Channel Inversion
Fading inverted to maintain constant SNR
Simplifies design (fixed rate)
Greatly reduces capacity
  Capacity is zero in Rayleigh fading
Truncated inversion
  Invert channel above cutoff fade depth
  Constant SNR (fixed rate) above cutoff
  Cutoff greatly increases capacity
    Close to optimal

## Slide 11: Capacity in Flat-Fading
Rayleigh
Log-Normal

## Slide 12: Main Points
Delay spread defines maximum delay of significant multipath components. Inverse is coherence BW
Doppler spread defines maximum nonzero doppler, its inverse is coherence time
Fundamental channel capacity defines maximum data rate that can be supported on a channel
  Capacity in fading depends what is known at TX & RX
  Capacity with RX CSI is average of AWGN capacity
  Capacity with TX/RX knowledge: variable-rate variable-power transmission (water filling) optimal
  Almost same capacity as with RX knowledge only
  Channel inversion practical, but should truncate