## Slide 1
KIRCHHOFF CURRENT LAW
ONE OF THE FUNDAMENTAL CONSERVATION PRINCIPLES
IN ELECTRICAL ENGINEERING
“CHARGE CANNOT BE CREATED NOR DESTROYED”

## Slide 2
NODES, BRANCHES, LOOPS
NODE: point where two, or more, elements
are joined (e.g., big node 1)
LOOP: A closed path that never goes
twice over a node (e.g., the blue line)
BRANCH: Component connected between two
nodes (e.g., component R4)
The red path is NOT a loop
A NODE CONNECTS SEVERAL COMPONENTS.
BUT IT DOES NOT HOLD ANY CHARGE.
TOTAL CURRENT FLOWING INTO THE NODE
MUST BE EQUAL TO TOTAL CURRENT OUT
OF THE NODE
(A CONSERVATION OF CHARGE PRINCIPLE)
NODE

## Slide 3
KIRCHHOFF CURRENT LAW (KCL)
SUM OF CURRENTS FLOWING INTO A NODE IS
EQUAL TO SUM OF CURRENTS FLOWING OUT OF
THE NODE
ALGEBRAIC SUM OF CURRENTS FLOWING INTO A
NODE IS ZERO
ALGEBRAIC SUM OF CURRENT (FLOWING) OUT OF
A NODE IS ZERO
A GENERALIZED NODE IS ANY PART OF A
CIRCUIT WHERE THERE IS NO ACCUMULATION
OF CHARGE
... OR WE CAN MAKE SUPERNODES BY
AGGREGATING NODES
INTERPRETATION: SUM OF CURRENTS LEAVING
NODES 2&3 IS ZERO
VISUALIZATION: WE CAN ENCLOSE NODES 2&3
INSIDE A SURFACE THAT IS VIEWED AS A
GENERALIZED NODE (OR SUPERNODE)

## Slide 4
PROBLEM SOLVING HINT: KCL CAN BE USED
TO FIND A MISSING CURRENT
SUM OF CURRENTS INTO
NODE IS ZERO
Which way are charges
flowing on branch a-b?
...AND PRACTICE NOTATION CONVENTION AT
THE SAME TIME...
NODES: a,b,c,d,e
BRANCHES: a-b,c-b,d-b,e-b
WRITE ALL KCL EQUATIONS
THE FIFTH EQUATION IS THE SUM OF THE
FIRST FOUR... IT IS REDUNDANT!!!

## Slide 5
FIND MISSING CURRENTS
KCL DEPENDS ONLY ON THE INTERCONNECTION.
THE TYPE OF COMPONENT IS IRRELEVANT
KCL DEPENDS ONLY ON THE TOPOLOGY OF THE CIRCUIT

## Slide 6
WRITE KCL EQUATIONS FOR THIS CIRCUIT
THE PRESENCE OF A DEPENDENT SOURCE
DOES NOT AFFECT APPLICATION OF KCL
KCL DEPENDS ONLY ON THE TOPOLOGY
THE LAST EQUATION IS AGAIN LINEARLY
DEPENDENT OF THE PREVIOUS THREE

## Slide 7
Here we illustrate the use
of a more general idea of
node. The shaded surface
encloses a section of the
circuit and can be considered
as a BIG node
THE CURRENT I5 BECOMES INTERNAL TO THE
NODE AND IT IS NOT NEEDED!!!

## Slide 10
THE PLAN
MARK ALL THE KNOWN CURRENTS
FIND NODES WHERE ALL BUT ONE CURRENT
ARE KNOWN
DETERMINE THE CURRENTS INDICATED

## Slide 12
This question tests KCL and
convention to denote currents
Use sum of currents leaving node = 0
-8A
B
D
6A
E
F