## Slide 1
The second systematic technique to determine all currents and voltages in a circuit
IT IS DUAL TO NODE ANALYSIS - IT FIRST DETERMINES ALL CURRENTS IN A CIRCUIT
AND THEN IT USES OHM’S LAW TO COMPUTE NECESSARY VOLTAGES
THERE ARE SITUATION WHERE NODE ANALYSIS IS NOT AN EFFICIENT TECHNIQUE
AND WHERE THE NUMBER OF EQUATIONS REQUIRED BY THIS NEW METHOD IS
SIGNIFICANTLY SMALLER
LOOP ANALYSIS

## Slide 2
Apply node analysis to this circuit
There are 4 non reference nodes
There is one supernode
There is one node connected to the
reference through a voltage source
We need three equations to compute
all node voltages
…BUT THERE IS ONLY ONE CURRENT FLOWING THROUGH ALL COMPONENTS AND IF
THAT CURRENT IS DETERMINED ALL VOLTAGES CAN BE COMPUTED WITH OHM’S LAW
I
STRATEGY:
1. Apply KVL
(sum of voltage drops =0)
2. Use Ohm’s Law to express
voltages in terms of the “loop current.”
RESULT IS ONE EQUATION IN THE LOOP CURRENT!!!
SHORTCUT
Skip this equation
Write this one
directly

## Slide 3
LOOPS, MESHES AND LOOP CURRENTS
EACH COMPONENT
IS CHARACTERIZED
BY ITS VOLTAGE
ACROSS AND ITS
CURRENT THROUGH
A LOOP IS A CLOSED PATH THAT DOES NOT
GO TWICE OVER ANY NODE.
THIS CIRCUIT HAS THREE LOOPS
fabcdef
A MESH IS A LOOP THAT DOES NOT ENCLOSE
ANY OTHER LOOP.
fabef, ebcde ARE MESHES
A LOOP CURRENT IS A (FICTICIOUS) CURRENT
THAT IS ASSUMED TO FLOW AROUND A LOOP
fabef
ebcde
A MESH CURRENT IS A LOOP CURRENT
ASSOCIATED TO A MESH. I1, I2 ARE MESH
CURRENTS
CLAIM: IN A CIRCUIT, THE CURRENT THROUGH
ANY COMPONENT CAN BE EXPRESSED IN TERMS
OF THE LOOP CURRENTS
FACT: NOT EVERY LOOP CURRENT IS REQUIRED
TO COMPUTE ALL THE CURRENTS THROUGH
COMPONENTS
THE DIRECTION OF THE LOOP
CURRENTS IS SIGNIFICANT
FOR EVERY CIRCUIT THERE IS A MINIMUM
NUMBER OF LOOP CURRENTS THAT ARE
NECESSARY TO COMPUTE EVERY CURRENT
IN THE CIRCUIT.
SUCH A COLLECTION IS CALLED A MINIMAL
SET (OF LOOP CURRENTS).

## Slide 4
FOR A GIVEN CIRCUIT LET
B NUMBER OF BRANCHES
N NUMBER OF NODES
THE MINIMUM REQUIRED NUMBER OF
LOOP CURRENTS IS
MESH CURRENTS ARE ALWAYS INDEPENDENT
AN EXAMPLE
TWO LOOP CURRENTS ARE
REQUIRED.
THE CURRENTS SHOWN ARE
MESH CURRENTS. HENCE
THEY ARE INDEPENDENT AND
FORM A MINIMAL SET
KVL ON LEFT MESH
KVL ON RIGHT MESH
USING OHM’S LAW
REPLACING AND REARRANGING
IN MATRIX FORM
THESE ARE LOOP EQUATIONS FOR THE
CIRCUIT
DETERMINATION OF LOOP CURRENTS

## Slide 5
WRITE KVL ON EACH MESH
LEARNING BY DOING: WRITE THE MESH EQUATIONS
IDENTIFY ALL VOLTAGE DROPS
BOOKKEEPING
BRANCHES = 8
NODES = 7
LOOP CURRENTS NEEDED = 2
USE OHM’S LAW
AND WE ARE TOLD TO
USE MESH CURRENTS!
THIS DEFINES THE LOOP
CURRENTS TO BE USED

## Slide 6
DRAW THE MESH CURRENTS. ORIENTATION
CAN BE ARBITRARY. BUT BY CONVENTION
THEY ARE DEFINED CLOCKWISE
NOW WRITE KVL FOR EACH MESH AND APPLY
OHM’S LAW TO EVERY RESISTOR.
AT EACH LOOP FOLLOW THE PASSIVE SIGN
CONVENTION USING LOOP CURRENT REFERENCE
DIRECTION
DEVELOPING A SHORTCUT
WHENEVER AN ELEMENT
HAS MORE THAN ONE
LOOP CURRENT FLOWING
THROUGH IT WE COMPUTE
NET CURRENT IN THE
DIRECTION OF TRAVEL

## Slide 7
SHORTCUT: POLARITIES ARE NOT NEEDED.
APPLY OHM’S LAW TO EACH ELEMENT AS KVL
IS BEING WRITTEN
REARRANGE
EXPRESS VARIABLE OF INTEREST AS FUNCTION
OF LOOP CURRENTS
THIS SELECTION IS MORE EFFICIENT
REARRANGE
LEARNING EXAMPLE: FIND Io USING LOOP ANALYSII
AN ALTERNATIVE SELECTION OF LOOP CURRENTS

## Slide 8
IF THE CIRCUIT CONTAINS ONLY INDEPENDENT
SOURCE THE MESH EQUATIONS CAN BE WRITTEN
“BY INSPECTION”
THE RIGHT HAND SIDE IS THE ALGEBRAIC SUM
OF VOLTAGE SOURCES AROUND THE LOOP
(VOLTAGE RISES - VOLTAGE DROPS)
MUST HAVE ALL MESH CURRENTS WITH THE
SAME ORIENTATION
IN LOOP K
THE COEFFICENT OF Ik IS THE SUM OF
RESISTANCES AROUND THE LOOP.
THE COEFFICIENT OF Ij IS THE SUM OF
RESISTANCES COMMON TO BOTH k AND j AND
WITH A NEGATIVE SIGN.
LOOP 1
LOOP 2
A PRACTICE EXAMPLE
LOOP 1
LOOP 2
Loop 3

## Slide 9
1. DRAW THE MESH CURRENTS
2. WRITE MESH EQUATIONS
MESH 1
MESH 2
DIVIDE BY 1k. GET NUMBERS FOR COEFFICIENTS
ON THE LEFT AND mA ON THE RHS
LEARNING
EXTENSION
3. SOLVE EQUATIONS

## Slide 10
BOOKKEEPING: B = 7, N = 4
1. DRAW MESH CURRENTS
2. WRITE MESH EQUATIONS. USE KVL
EQUATIONS BY INSPECTION
CHOOSE YOUR FAVORITE TECHNIQUE
TO SOLVE THE SYSTEM OF EQUATIONS

## Slide 11
CIRCUITS WITH INDEPENDENT CURRENT SOURCES
THERE IS NO RELATIONSHIP BETWEEN V1 AND
THE SOURCE CURRENT! HOWEVER ...
MESH 1 CURRENT IS CONSTRAINED
MESH 1 EQUATION
MESH 2
“BY INSPECTION”
CURRENT SOURCES THAT ARE NOT SHARED
BY OTHER MESHES (OR LOOPS) SERVE TO
DEFINE A MESH (LOOP) CURRENT AND
REDUCE THE NUMBER OF REQUIRED EQUATIONS
TO OBTAIN V1 APPLY KVL TO ANY CLOSED
PATH THAT INCLUDES V1
KVL

## Slide 12
TWO MESH CURRENTS ARE DEFINED BY CURRENT
SOURCES
MESH 3
“BY INSPECTION”
KVL FOR Vo
USE KVL TO
COMPUTE Vo
LEARNING EXAMPLE

## Slide 13
WE ACTUALLY NEED THE CURRENT ON THE
RIGHT MESH. HENCE, USE MESH ANALYSIS
MESH 1:
MESH 2:
MESH 1:
MESH 2:
LEARNING EXTENSIONS

## Slide 14
1. Select loop currents.
In this case we use meshes.
We note that the current source
could define one mesh.
2. Write loop equations.
Loop 1
Loop 2
Loop 3
Since we need to compute Vo it is
efficient to solve for I3 only.
HINT: Divide the loop equations by 1k. Coefficients
become numbers and voltage source becomes mA.
3 non-reference nodes. 3 meshes
One current source, one super node
SELECTING THE SOLUTION METHOD
BOTH APPROACHES SEEM COMPARABLE. CHOOSE
LOOP ANALYSIS
We use the fact that I1 = Is
Loop 2
Loop 3

## Slide 15
CURRENT SOURCES SHARED BY LOOPS - THE SUPERMESH APPROACH
1. SELECT MESH CURRENTS
2. WRITE CONSTRAINT EQUATION DUE TO
MESH CURRENTS SHARING CURRENT SOURCES
3. WRITE EQUATIONS FOR THE OTHER MESHES
4. DEFINE A SUPERMESH BY (MENTALLY)
REMOVING THE SHARED CURRENT SOURCE
SUPERMESH
5. WRITE KVL FOR THE SUPERMESH
NOW WE HAVE THREE EQUATIONS IN THREE
UNKNOWNS. THE MODEL IS COMPLETE

## Slide 16
CURRENT SOURCES SHARED BY MESHES - THE GENERAL LOOP APPROACH
THE STRATEGY IS TO DEFINE LOOP CURRENTS
THAT DO NOT SHARE CURRENT SOURCES -
EVEN IF IT MEANS ABANDONING MESHES
FOR CONVENIENCE START USING MESH CURRENTS
UNTIL REACHING A SHARED SOURCE. AT THAT
POINT DEFINE A NEW LOOP.
IN ORDER TO GUARANTEE THAT IF GIVES AN
INDEPENDENT EQUATION ONE MUST MAKE SURE
THAT THE LOOP INCLUDES COMPONENTS THAT
ARE NOT PART OF PREVIOUSLY DEFINED LOOPS
A POSSIBLE STRATEGY IS TO CREATE A LOOP
BY OPENING THE CURRENT SOURCE
THE LOOP EQUATIONS FOR THE LOOPS WITH
CURRENT SOURCES ARE
THE LOOP EQUATION FOR THE THIRD LOOP IS
THE MESH CURRENTS OBTAINED WITH THIS
METHOD ARE DIFFERENT FROM THE ONES
OBTAINED WITH A SUPERMESH. EVEN FOR
THOSE DEFINED USING MESHES.

## Slide 17
Three independent current sources.
Four meshes.
One current source shared by two
meshes.
For loop analysis we notice...
Careful choice of loop currents
should make only one loop equation
necessary. Three loop currents can
be chosen using meshes and not
sharing any source.
SOLVE FOR THE CURRENT I4.
USE OHM’S LAW TO C0MPUTE REQUIRED
VOLTAGES
Now we need a loop current that does
not go over any current source and
passes through all unused components.
HINT: IF ALL CURRENT SOURCES ARE REMOVED
THERE IS ONLY ONE LOOP LEFT
MESH EQUATIONS FOR LOOPS WITH
CURRENT SOURCES
KVL OF REMAINING LOOP

## Slide 18
A COMMENT ON METHOD SELECTION
The same problem can be solved by node analysis
but it requires 3 equations

## Slide 19
CIRCUITS WITH DEPENDENT SOURCES
Treat the dependent source as though
it were independent.
Add one equation for the controlling
variable
COMBINE EQUATIONS. DIVIDE BY 1k

## Slide 20
SOLVE USING MATLAB
PUT IN MATRIX FORM
» R=[1,0,0,0; %FIRST ROW
1,1, -1, 0; %SECOND ROW
0,1,3,-2; %THIRD ROW
0,-1,-1,2] %FOURTH ROW
R =
1 0 0 0
1 1 -1 0
0 1 3 -2
0 -1 -1 2
DEFINE THE MATRIX
DEFINE THE RIGHT HAND SIDE VECTOR
» V=[4;0;8;12]
V =
4
0
8
-12
Since we divided by
1k the RHS is mA and
all the coefficients
are numbers
SOLVE AND GET THE ANSWER
» I=R\V
I =
4
-6
-2
-10
The answers are in mA
>> is the MATLAB prompt. What
follows is the command entered

## Slide 21
LEARNING EXTENSION: Dependent Sources
We treat the dependent source as one more voltage source
and solve...
The selection of loop currents
simplifies expression for Vx
and computation of Vo.
USING LOOP CURRENTS
USING MESH CURRENTS
MESH 1
LOOP 1
MESH 2
LOOP 2
NOW WE EXPRESS THE CONTROLLING VARIABLE IN TERMS OF THE LOOP CURRENTS
REPLACE AND REARRANGE
SOLUTIONS
NOTICE THE DIFFERENCE BETWEEN MESH
CURRENT I1 AND LOOP CURRENT I1 EVEN
THOUGH THEY ARE ASSOCIATED TO THE
SAME PATH
Find Vo

## Slide 22
DEPENDENT CURRENT SOURCE. CURRENT SOURCES NOT SHARED BY MESHES
We treat the dependent source as a
conventional source
Then KVL on the remaining loop(s)
And express the controlling variable,
Vx, in terms of loop currents
Equations for meshes with current sources
WE ARE ASKED FOR Vo. WE ONLY NEED
TO SOLVE FOR I3
REPLACE AND REARRANGE

## Slide 23
DRAW MESH CURRENTS
WRITE MESH EQUATIONS.
CONTROLLING VARIABLE IN TERMS OF
LOOP CURRENTS
REPLACE AND REARRANGE
SOLVE FOR I2