## Slide 1
MAGNETICALLY COUPLED NETWORKS
LEARNING GOALS
Mutual Inductance
Behavior of inductors sharing a common magnetic field
Energy Analysis
Used to establish relationship between mutual reluctance and
self-inductance
The ideal transformer
Device modeling components used to change voltage and/or
current levels
Safety Considerations
Important issues for the safe operation of circuits with transformers

## Slide 2
Induced links
on second
coil
MUTUAL INDUCTANCE
Overview of Induction Laws
Magnetic
flux
If linkage is created by a current flowing
through the coils…
(Ampere’s Law)
The voltage created at the terminals of
the components is
(Faraday’s Induction Law)
What happens if the flux created by the
current links to another coil?
One has the effect of mutual inductance
Assume n circuits interacting
Special case n=2

## Slide 3
THE DOT CONVENTION
Currents and voltages follow
passive sign convention
Flux 2 induced
voltage has + at dot
LEARNING EXAMPLE
For other cases change polarities or
current directions to convert to this
basic case

## Slide 4
Equivalent to a
negative mutual
inductance
More on the dot convention

## Slide 5
LEARNING EXTENSION
Convert to
basic case
PHASORS AND MUTUAL INDUCTANCE
Phasor model for mutually
coupled linear inductors
Assuming complex
exponential sources

## Slide 6
LEARNING EXAMPLE
The coupled inductors can be connected in four different ways.
Find the model for each case
CASE I
Currents into dots
CASE 2
Currents into dots

## Slide 7
CASE 3
Currents into dots
CASE 4
Currents into dots

## Slide 8
LEARNING EXAMPLE
1. Coupled inductors. Define their
voltages and currents
2. Write loop equations
in terms of coupled
inductor voltages
3. Write equations for
coupled inductors
4. Replace into loop equations
and do the algebra

## Slide 9
LEARNING EXAMPLE
Write the mesh equations
1. Define variables for coupled inductors
2. Write loop equations in terms of coupled
inductor voltages
3. Write equations for coupled inductors
4. Replace into loop equations and
rearrange terms

## Slide 10
LEARNING EXTENSION
1. Define variables for coupled inductors
2. Loop equations
3. Coupled inductors equations
4. Replace and rearrange
Voltages in Volts
Impedances in Ohms
Currents in ____

## Slide 11
LEARNING EXTENSION
WRITE THE KVL EQUATIONS
1. Define variables for coupled inductors
2. Loop equations in terms of inductor
voltages
3. Equations for coupled inductors
4. Replace into loop equations and
rearrange

## Slide 12
LEARNING EXAMPLE
DETERMINE IMPEDANCE SEEN BY THE SOURCE
1. Variables for coupled inductors
2. Loop equations in terms of coupled
inductors voltages
3. Equations for coupled inductors
4. Replace and do the algebra
WARNING: This is NOT a phasor

## Slide 13
LEARNING EXTENSION
DETERMINE IMPEDANCE SEEN BY THE SOURCE
4. Replace and do the algebra
1. Variables for coupled inductors
One can choose directions
for currents.
If I2 is reversed one gets
the same equations than
in previous example.
Solution for I1 must be the
same and expression for
impedance must be the same
2. Loop equations
3. Equations for coupled inductors

## Slide 14
ENERGY ANALYSIS
We determine the total energy stored in a coupled network
This development is different from the one in the book. But the final
result is obviously the same
Coefficient of
coupling

## Slide 15
LEARNING EXAMPLE
Compute the energy stored in the mutually coupled inductors
Assume steady state operation
We can use frequency domain techniques
Circuit in frequency domain
Merge the writing of the loop and coupled
inductor equations in one step

## Slide 16
LEARNING EXTENSION
Go back to time domain

## Slide 17
THE IDEAL TRANSFORMER
Insures that ‘no magnetic flux
goes astray’
First ideal transformer
equation
Ideal transformer is lossless
Second ideal transformer
equations
Circuit Representations
Since the equations
are algebraic, they
are unchanged for
Phasors. Just be
careful with signs

## Slide 18
REFLECTING IMPEDANCES
For future reference
Phasor equations for ideal transformer

## Slide 19
LEARNING EXAMPLE
Determine all indicated voltages and currents
Strategy: reflect impedance into the
primary side and make transformer
“transparent to user.”
SAME
COMPLEXITY
CAREFUL WITH POLARITIES AND
CURRENT DIRECTIONS!

## Slide 20
LEARNING EXTENSION
Strategy: reflect impedance into the
primary side and make transformer
“transparent to user.”
Voltage in Volts
Impedance in Ohms
...Current in Amps
LEARNING EXTENSION
Strategy: Find current in secondary and then use Ohm’s Law

## Slide 21
USING THEVENIN’S THEOREM TO SIMPLIFY CIRCUITS WITH IDEAL TRANSFORMERS
Replace this circuit with its Thevenin
equivalent
To determine the Thevenin impedance...
Reflect impedance into
secondary
Equivalent circuit with transformer
“made transparent.”
One can also determine the Thevenin
equivalent at 1 - 1’

## Slide 22
USING THEVENIN’S THEOREM: REFLECTING INTO THE PRIMARY
Find the Thevenin equivalent of
this part
Thevenin impedance will be the
secondary impedance reflected into
the primary circuit
Equivalent circuit reflecting
into primary
Equivalent circuit reflecting
into secondary

## Slide 23
LEARNING EXAMPLE
Draw the two equivalent circuits
Equivalent circuit reflecting
into primary
Equivalent circuit reflecting
into secondary

## Slide 24
LEARNING EXAMPLE
But before doing that it is better to simplify the primary using Thevenin’s Theorem
Thevenin equivalent of this part
This equivalent circuit is now transferred to
the secondary

## Slide 25
LEARNING EXAMPLE (continued…)
Thevenin equivalent of primary side
Circuit with primary transferred to secondary
Transfer to
secondary

## Slide 26
LEARNING EXTENSION
Equivalent circuit reflecting
into primary
Notice the position of the
dot marks

## Slide 27
LEARNING EXTENSION
Transfer to
secondary

## Slide 28
LEARNING EXAMPLE
Nothing can be transferred. Use
transformer equations and circuit
analysis tools
Phasor equations for ideal transformer
4 equations in 4 unknowns!

## Slide 29
SAFETY CONSIDERATIONS: AN EXAMPLE
Houses fed from different distribution
transformers
Braker X-Y opens, house B
is powered down
Good neighbor runs an extension
and powers house B
When technician resets the
braker he finds 7200V between
points X-Z
when he did not expect to find any

## Slide 30
LEARNING BY APPLICATION
Why high voltage transmission lines?
CASE STUDY: Transmit 24MW over 100miles with 95% efficiency
A. AT 240V
B. AT 240kV

## Slide 31
LEARNING EXAMPLE
Rating a distribution transformer
Determining ratio
Determining power rating

## Slide 32
LEARNING BY DESIGN
Use a 120V - 12V transformer to build a 108V autotransformer
Conventional transformer
Auto transformer connections
Circuit representations
Use the subtractive connection
on the 120V - 12V transformer
Transformers