## Slide 1: Chapter #11: Output Stages and Power Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 2: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  The classification of amplifier output stages on the basis of the fraction of the cycle of an input sine wave during which the transistor conducts.
  Analysis and design of a variety of output-stage types ranging from the simple but power-inefficient emitter follower class (class A) to the popular push-pull class AB circuit in both bipolar and CMOS technologies.
  Thermal considerations in the design and fabrication of high-output power circuits.

## Slide 3: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  Useful and interesting circuit techniques employed in the design of power amplifiers.
  Special types of MOS transistors optimized for high-power applications.

## Slide 4: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
One important aspect of an amplifier is output resistance.
This affects its ability to deliver a load without loss of gain (or significant loss).
Large signals are of interest and small-signal models cannot be applied.
Total harmonic distortion is good measure of linearity of output stage.

## Slide 5: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Most challenging aspect of output stage design is efficiency.
Power dissipation is highly correlated to internal junction temperature.

## Slide 6: 11.1. Classification of Output Stages
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Output stages are classified according to collector current waveform that results when input signal is applied.
They are outlined in Figure 11.1.
Figure 11.1: Collector current waveforms for transistors operating in (a) class A, (b) class B, (c) class AB, and (d) class C amplifier stages.

## Slide 7: 11.2. Class A Output Stage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 8
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 9
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 10: 11.2.3. Power Dissipation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Maximum instantaneous power dissipation in Q1 is VCCI.
  It is equal to power dissipation in Q1 with no signal applied (quiescent power dissipation).
Emitter-follower transistor dissipates the largest amount of power when vO = 0.
Since this condition (no input signal) may be maintained or long periods of time, transistor Q1 must be able to withstand a continuous power dissipation of VCCI.

## Slide 11
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.4: Maximum signal waveforms in the class A output stage of Fig. 11.2 under the condition I = VCC /RL or, equivalently, RL = VCC/I. Note that the transistor saturation voltages have been neglected.

## Slide 12: 11.2.4. Power Conversion Efficiency
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 13: 11.3. Class B Output Stage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 14
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.5: A class B output stage.

## Slide 15
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.6: Transfer characteristic for the class B output stage in Fig. 11.5.

## Slide 16: 11.3.4. Power Dissipation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 17
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.8: Power dissipation of the class B output stage versus amplitude of the output sinusoid.

## Slide 18: 11.3.5. Reducing Crossover Distortion
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Crossover distortion of class B output stage may be reduced substantially:
  Employing High-gain Op-amp
  Overall Negative Feedback
0.7V deadband is reduced to 0.7/A0.
Slew-rate limitation of op-amp will cause alternate turning on and off of output transistors to be noticeable
More practical solution is class AB stage.

## Slide 19
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.9: Class B circuit with an op amp connected in a negative-feedback loop to reduce crossover distortion.

## Slide 20
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.10: Class B output stage operated with a single power supply.

## Slide 21: 11.4. Class AB Output Stage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Crossover distortion can be virtually eliminated by biasing the complementary output transistor with small nonzero current.
A bias voltage VBB is applied between QN and QP.

## Slide 22: 11.4. Class AB Output Stage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 23
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.12: Transfer characteristic of the class AB stage in Fig. 11.11.

## Slide 24: 11.4.2. Output Resistance
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 25
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.13: Determining the small-signal output resistance of the class AB circuit of Fig. 11.11.

## Slide 26: 11.5. Biasing the Class AB Circuit
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.14 shows class AB circuit with bias voltage VBB.
Constant current IBIAS is passed through pair of diodes D1 and D2.
In circuits that supply large amounts of power, the output transistors are large-geometry devices.
Biasing diodes, however, need not be large.

## Slide 27: 11.5. Biasing the Class AB Circuit
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.14: A class AB output stage utilizing diodes for biasing. If the junction area of the output devices, QN and QP, is n-times that of the biasing devices D1 and D2, a quiescent current IQ = nIBIAS flows in the output devices.

## Slide 28: 11.5.2. Biasing Using the VBE Multiplier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 29
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.15: A class AB output stage utilizing a VBE multiplier for biasing.
Figure 11.16: A discrete-circuit class AB output stage with a potentiometer used in the VBE multiplier.

## Slide 30: 11.7. Power BJT’s
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
11.7.1. Junction Temperature
  150OC to 200OC
11.7.2. Thermal Resistance
  (eq11.69) TJ – TA = JAPD
11.7.3. Power Dissipation Versus Temperature
  One must examine power-derating curve.
11.7.4. Transistor Case and Heat Sink
  (eq11.72) JA = JC + CA

## Slide 31
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.25: The popular TO3 package for power transistors. The case is metal with a diameter of about 2.2 cm; the outside dimension of the “seating plane” is about 4 cm. The seating plane has two holes for screws to bolt it to a heat sink. The collector is electrically connected to the case. Therefore an electrically insulating but thermally conducting spacer is used between the transistor case and the “heat sink.”

## Slide 32
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.27: Maximum allowable power dissipation versus transistor-case temperature.
Figure 11.26: Electrical analog of the thermal conduction process when a heat sink is utilized.

## Slide 33: 11.7.5. The BJT Safe Operating Area
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The maximum allowable current ICMax. Exceeding this current on a continuous basis can result in melting the wires that bond the device to the package terminals.
The maximum power dissipation hyperbola. This is the locus of the points for which vCEiC = PDmax (at TC0). For temperatures TC > TC0, the power derating curves described in Section 11.7.4 should be used to obtain the applicable PDmax and thus a correspondingly lower hyperbola.

## Slide 34: 11.7.5. The BJT Safe Operating Area
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The second-breakdown limit. Second breakdown is a phenomenon that results because current flow across the emitter-base junction is not uniform. Rather, the current density is greatest near the periphery of the junction.
  Hot Spots
  Thermal Runaway
The collector-to-emitter breakdown voltage (BVCEO).

## Slide 35
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.29: Safe operating area (SOA) of a BJT.

## Slide 36: 11.7.6. Parameter Values of Power Transistors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
At high currents, the exponential iC-vBE relationship exhibits a factor of 2 reduction in the exponent.
 is low, typically 30 to 80 (but can be as low as 5). It is important to note that b has a positive temperature coefficient.
At high currents r becomes very small (a few ohms) and rx becomes important.
fT is low (a few MHz), C is large, C is even larger.
ICBO is large, BVCEO is typically 50 to 100V.
ICmax is typically in ampere range, as high as 100A.

## Slide 37: 11.9. IC Power Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
High-gain, small-signal amplifier followed by class AB output stage.
Overall negative feedback is already applied.
Output current-driving capability of any general-purpose op-amp may be increased by cascading it with class B or class AB output stage.
Hybrid IC

## Slide 38
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.35: Thermal-shutdown circuit.

## Slide 39
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.36 The simplified internal circuit of the LM380 IC power amplifier. (Courtesy National Semiconductor Corporation.)

## Slide 40
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 11.37: Small-signal analysis of the circuit in Fig. 11.36. The circled numbers indicate the order of the analysis steps.

## Slide 41: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Output stages are classified according to the transistor conduction angle: class A (360O), class AB (slightly more than 180O), class B (180O), and class C (less than 180O).
The most common class A output stage is the emitter-follower. It is biased at a current greater than the peak load current.
The class A output stage dissipates its maximum power under quiescent conditions (vO = 0). It achieves a maximum power conversion efficiency of 25%,

## Slide 42: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The class B stage is biased at zero current, and thus dissipates no power in quiescence.
The class B stage can achieve a power conversion efficiency as high as 78.5%.
The class B stage suffers from crossover distortion.
The class AB output stage is biased at a small current; thus both transistors conduct for small input signals, and crossover distortion is virtually eliminated.

## Slide 43: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Except for an additional small quiescent power dissipation, the power relationships of the class AB stage are similar to those in class B.
To guard against the possibility of thermal runaway, the bias voltage of the class AB circuit is made to vary with temperature in the same manner as does VBE of the output transistors.
The classical CMOS class AB output stage suffers from reducing output signal-swing. This problem may be overcome by replacing the source-follower output transistor with a pair of complementary devices.