## Slide 1: Chapter #12: Operational-Amplifier Circuits
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 2: Introduction
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  The design and analysis of the two basic CMOS op-amp architectures: the two-stage circuit and the single-stage, folded cascode circuit.
  The complete circuit of an analog IC classic: the 741 op-amp. Though 40 years old, the 741 circuit includes so many interesting and useful design techniques that its study is still a must.
  Applications of negative feedback within op-amp circuits to achieve bias stability and increased CMRR.

## Slide 3: Introduction
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  How to break a large analog circuit into its recognizable blocks, to be able to make the analysis amendable to a pencil-and-paper approach – which is the best way to learn design.
  Some of the modern techniques employed in the design of low-voltage single-supply BJT op amps.
  Most importantly, how the different topics we learned about in the preceding chapters come together in the design of the most important analog IC – the op amp.

## Slide 4: 12.1. The Two Stage CMOS Op Amp
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Two-stage op amp is shown in Figure 12.1.
It was studied in Section 8.6.1 as example of multi-stage CMOS amplifier.
Figure 12.1 The basic two-stage CMOS op-amp configuration.

## Slide 5: 12.1.1. The Circuit
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Two Stages:
  Differential Pair Q1/Q2.
    Biased by current source Q5
    Fed by a reference current IREF
  Current Mirror Load Q3/Q4.
    Frequency Compensation
Voltage Gain 20V/V to 60V/V
Reasonable Common-Mode Rejection Ratio (CMRR)

## Slide 6: 12.1.1. Input Common-Mode Range and Output Swing
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 7: 12.1.3. Voltage Gain
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Consider simplified equivalent circuit model for small-signal operation of CMOS amplifier.
  Figure 12.2.
Input resistance is practically infinite (Rin).
First-stage transconductance (Gm1) is equal to values for Q1 and Q2.
Since Q1 and Q2 are operated at equal bias currents (I/2) and equal overdrive voltages, equation (12.7) applies.

## Slide 8: 12.1.1. Input Common-Mode Range and Output Swing
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 9: 12.1.1. Input Common-Mode Range and Output Swing
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 10: 12.1.1. Input Common-Mode Range and Output Swing
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.2: Small-signal equivalent circuit for the op amp in Fig. 12.1.

## Slide 11: 12.1.4. Common-Mode Rejection Ratio
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
CMRR of two-stage amplifier is determined by first stage
  CMRR = [gm1(ro2||ro4)[2gm3RSS]
RSS is output resistance of the bias source Q5
CMRR is of the order of (gmro)2
  This is high.
Gmro is proportional to VA/VOV
CMRR is increased if long channels are used.

## Slide 12: 12.1.5. Frequency Response
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 13
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 14
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.4: Typical frequency response of the two-stage op amp.

## Slide 15: 12.1.5. Frequency Response
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 16
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.5: Small-signal equivalent circuit of the op amp in Fig. 12.1 with a resistance R included in series with CC.

## Slide 17: 12.1.6. Slew Rate
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.6: A unity-gain follower with a large step input. Since the output voltage cannot change immediately, a large differential voltage appears between the op-amp input terminals.

## Slide 18: 12.1.6. Slew Rate
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.7: Model of the two-stage CMOS op-amp of Fig. 12.1 when a large differential voltage is applied.

## Slide 19: Relationship Between SR and ft
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Simple relationship exists between unity-gain bandwidth (ft) and slew rate.
  Equations (12.31) through (12.40).
SR = 2ftVOV
Slew rate is determined by the overdrive voltage at which first-stage transistors are operated.
For a given bias current I, a larger VOV is obtained if Q1 and Q2 are p-channel devices.

## Slide 20: 12.1.7. Power Supply Rejection Ratio
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
mixed-signal circuit – IC chip which combines analog and digital devices.
  Switching activity in digital portion results in ripple within power supplies.
  This ripple may affect op amp output.
power-supply rejection ratio – the ability of a circuit to eliminate any ripple in the circuit power supplies.
  PSRR is generally improved through utilization of capacitors.

## Slide 21: 12.1.7. Power Supply Rejection Ratio
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 22: 12.1.8. Design Trade-Offs
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
The performance of the two-stage CMOS amplifier are primarily determined by two design parameters:
  Length (L) of channel of each MOSFET
  Overdrive voltage (VOV) at which transistor is operated.
transition frequency (fT) – is defined below. It determined high-frequency operation.

## Slide 23: 12.2. The Folded-Cascode CMOS Op Amp
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.8: Structure of the folded-cascode CMOS op amp.

## Slide 24: 12.7.1. The Circuit
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.9: A more complete circuit for the folded-cascode CMOS amplifier of Fig. 12.8.

## Slide 25: 12.2.2. Input Common-Mode Range and Output Swing
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 26: 12.2.3. Voltage Gain
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 27: 12.7.1. The Circuit
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.10: Small-signal equivalent circuit of the folded-cascode CMOS amplifier. Note that this circuit is in effect an operational transconductance amplifier (OTA).

## Slide 28: 12.3. The 741 Op-Amp Circuit
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Sections 12.3. through 12.6 focus on the 741 op-amp circuit.
  Figure 12.13. provides a circuit schematic.
  The design uses many transistors, few resistors.
741 requires two power supplies.
VCC = VEE = 15V

## Slide 29: 12.7.1. The Circuit
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.13: The 741 op-amp circuit: Q11, Q12, and R5 generate a reference bias current; IREF. Q10, Q9, and Q8 bias the input stage, which is composed of Q1 to Q7. The second gain stage is composed of Q16 and Q17 with Q13B acting as active load. The class AB output stage is formed by Q14 and Q20 with biasing devices Q13A, Q18, and Q19, and an input buffer Q23. Transistors Q15, Q21, Q24, and Q22 serve to protect the amplifier against output short circuits and are normally cut off.

## Slide 30: 12.3.3. The Input Stage
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
741 consists of three-stages:
  Input Differential Stage (Q1 through Q7)
    Emitter Followers: Q1, Q2
    Differential Common-Base: Q3, Q4
    Load Circuit: Q5, Q6, Q7
    Biasing: Q8, Q9, Q10
  Intermediate Single-Ended High-Gain Stage
  Output-Buffering Stage (other transistors)

## Slide 31: 12.3.4. The Second Stage
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Consists of Q16, Q17, and Q13B
  Emitter Follower: Q16
  Common-Emitter: Q17
  Load: Q13B
Output of second stage is taken at collector of Q17.
Capacitor CC is connected in feedback path of second stage.
  Frequency compensation using Miller Technique.

## Slide 32: 12.3.5. The Output Stage
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Provides low output resistance.
Able to supply relatively large load current.
  With minimal power dissipation.
Consists of Q14 and Q20.
  Complementary pair.
Transistors Q18 and Q19 are fed by current source Q13A and bias transistors Q14 and Q20.

## Slide 33: 12.3.6. Device Parameters
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
npn: IS = 10-14A,  = 200, VA = 125V
pnp: IS = 10-14A,  = 50, VA = 50V
Q13A and Q13B: ISA = 0.25(10-14)A, ISB = 0.75(10-14)A
  These devices are non-standard.
Q14 and Q20 will be assumed to have area three times of the standard device – for increased loading.

## Slide 34: 12.4. DC Analysis of the 741
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 35: 12.7.1. The Circuit
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.14: The Widlar current source that biases the input stage.

## Slide 36: 12.7.1. The Circuit
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.15: The dc analysis of the 741 input stage.

## Slide 37: 12.7.1. The Circuit
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.16: The dc analysis of the 741 input stage, continued.

## Slide 38: 12.4. DC Analysis of the 741
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 39: 12.5. Small Signal Analysis of 741
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
One may use small-signal analysis (as in previous chapters) to analyze linear behavior of the 741.
  Figures 12.18 – 12.21 describe this process for input stage.
  Figures 12.25 – 12.27 describe this process for gain stage.
  Figures 12.28 – 12.30 describe this process for output stage.

## Slide 40: 12.5. Small Signal Analysis of 741
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.21: Small-signal equivalent circuit for the input stage of the 741 op amp.

## Slide 41: 12.5. Small Signal Analysis of 741
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 12.25: Small-signal equivalent-circuit model of the second stage.

## Slide 42: Summary
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Most CMOS op-amps are designed to operate as part of a VLSI circuit and thus required to drive only small capacitive loads. Therefore, most do not have a low-output-resistance stage.
There are basically two approaches to the design of CMOS op-amps: a two-stage configuration and a single-stage topology using the folded-cascode circuit.
In the two-stage CMOS op-amp, approximately equal gains are realized in the two stages.

## Slide 43: Summary
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
The threshold mismatch together with the low transconductance of the input stage result in a larger input offset voltage for the CMOS op-amps than for bipolar units.
Miller compensation is employed in the two-stage CMOS op-amp, but a series resistor is required to place the transmission zero at either s = infinity or on the negative real axis.
CMOS op-amps have better slew rates (than alt’s).

## Slide 44: Summary
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Use of the cascode configuration increases the gain of a CMOS amplifier stage by about two orders of magnitude, thus making possible a single-stage op-amp.
The dominant pole of the folded-cascode op-amp is determined by the total capacitance at the output CL. Increasing CL improves the phase margin at the expense of reducing bandwidth.
By using two complementary input differential pairs in parallel, the common-mode range may be extended.

## Slide 45: Summary
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
The output voltage swing of the folded-cascode op-amp may be extended by utilizing a wide-swing current mirror in place of the cascode mirror.
The internal circuit of the 741 op-amp embodies many of the design techniques employed in bipolar analog integrated circuits.
The 741 circuit consists of an input differential stage, a high-gain single-ended second stage, and a class AB output stage. It is the basis for many other devices.

## Slide 46: Summary
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
To obtain low input offset voltage and current, and high CMRR, the 741 input stage is designed to be perfectly balanced. The CMRR is increased by common-mode feedback, which also stabilizes the dc operating point.
To obtain high input resistance and low input bias current, the input stage of the 741 is operated as a very low current level.
The use of Miller Frequency compensation in the 741 circuit enables locating the dominant pole at a very low frequency, while utilizing a relatively small compensating capacitance.

## Slide 47: Summary
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Two-stage op-amps may be modeled as a transconductance amplifier feeding an ideal integrator with CC as the integrating capacitor.
The slew rate of a two-stage op-amp is determined by the first-stage bias current and frequency-compensation capacitor.
While the 741 and similar op-amps nominally operate from 15V power supplies, modern BJT op-amps typically utilize a single ground-referenced supply of only 2 or 3V.