## Slide 1: Chapter #13: CMOS Digital Logic Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 2: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  How the operation of the basic element in digital circuits, the logic inverter, is characterized by such parameters as noise margins, propagation delay, and power dissipaption, and how it is implemented by using one of the three possible arangements of voltage-controlled swicthes (transistors).
  That the three most significant metrics in digital IC design are speed, power dissipation, and area.

## Slide 3: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  How and why CMOS has become the dominant technology for digital IC design.
  The structure, circuit operation, static and dynamic performance analysis, and the design of the CMOS inverter.
  The synthesis and design optimization of CMOS logic circuits.
  The implications of technology scaling (Moore’s Law).

## Slide 4: 13.1. Digital Logic Inverters
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Most basic element in design of digital circuits.
Plays a role parallel to the amplifier in analog circuits.
13.1.1. Function of the Inverter
  Convert 0 to 1, 1 to 0.
13.1.2. Voltage Transfer Characteristics (VTC)
  Described in Figure 13.3.

## Slide 5: 13.1.2. Voltage-Transfer Charactristic (VTC)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.2. demonstrates utilization of transistor as logic inverter.
  logic = 1: vo = VDD, logic = 0: vI = VDD
To utilize transistor-based amplifier as an inverter, extreme regions of operation are employed.
ViL is maximum value vI can have while being interpreted as logic 0.
ViH is minimum value vI can have while being interpreted as logic 1.

## Slide 6
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.1: A logic inverter operating from a dc supply VDD.

## Slide 7
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 8
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.3: Voltage transfer characteristic of an inverter. The VTC is approximated by three straight-line segments. Note the four parameters of the VTC (VOH, VOL, VIL, and VIH) and their use in determining the noise margins (NMH and NML).

## Slide 9: 13.1. Noise Margins
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 10: 13.1. Noise Margins
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Insensitivity of inverter output to exact value of vI is advantageous (sensitivity is low).

## Slide 11: 13.1. Noise Margins
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Four parameters (VOH, VOL, VIH, VIL) define the VTC of an inverter.
  As well as determine noise margins.
Inverter is good at rejecting noise.
  aka. restoring signal levels to the desirable VOL and VOH.
Formal definitions are provided in Figure 13.5.

## Slide 12
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 13
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.5: Typical voltage transfer characteristic (VTC) of a logic inverter, illustrating the definition of the critical points.

## Slide 14: 13.1.4. The Ideal VTC
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
An ideal VTC is one that maximizes:
  Range of Output
  Noise Margins
To obtain maximum output swing:
  VOH = VDD, VOL = 0
To obtain maximum noise margins, transition region should be as narrow as possible.
  They are equalized to “transition” at midpoint of the power supply (VDD/2).

## Slide 15: 13.1.5. Inverter Implementation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Inverters using transistors (Chapters 5 and 6) operate as voltage-controlled switches.
  When vI is low, switch is open.
  When vI is high, switch is closed.
Transistors, however, are not perfect.
  off resistance exists
  on resistance exists
For transistor: VOL = VDD( Ron / ( R + Ron ))

## Slide 16
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.6: The VTC of an ideal inverter.

## Slide 17
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 18: 13.1.5. Inverter Implementation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
More elaborate implementations of logic inverter exist:
  complementary pull-up switch (PU) – when vI is low, PU is closed.
  complementary pull-down switch (PD) when vI is low, PD is open.
Figure 13.8: A more elaborate implementation of the logic inverter utilizing two complementary switches. This is the basis of the CMOS inverter that we shall study in Section 13.2.

## Slide 19
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.8: A more elaborate implementation of the logic inverter utilizing two complementary switches. This is the basis of the CMOS inverter that we shall study in Section 13.2.

## Slide 20
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 21: 13.1.6. Power Dissipation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Digital circuits use large number of logic gates.
  As such, power / heat dissipation is concern.
very-large-scale integration (VLSI) – describes methods to design and implement very compact integrated chips.
  More than one million gates per chip.
static power dissipation – power lost when switch is open / closed (not moving).
dynamic power dissipation – power lost when switch is opening / closing (moving).

## Slide 22: 13.1.6. Power Dissipation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 23
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 24: 13.1.6. Power Dissipation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Equation (13.35) indicates that to minimize dynamic power dissipation:
  Capacitance should be minimal.
    This shortens length of transients.
  VDD should be minimal.
    This is why modern devices use 5V supplies, as opposed to 12 or 15V.
  Although reduction of f is possible, it goes against the need for increased speed in digital technology.

## Slide 25: 13.1.7. Propagation Delay
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
One important issue, especially in digital computers, is maximum speed at which a device is capable of operating.
propagation delay – is the time difference between an change in input and reaction at output.
Generally, this value is characterized employing “pulse” input.

## Slide 26
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.13: An inverter fed with the ideal pulse in (a) provides at its output the pulse in (b). Two delay times are defined as indicated.

## Slide 27: 13.1.7. Propagation Delay
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.3. yields several observations:
  1. Output is no longer ideal pulse.
    The shape of the output differs from input. The process is no longer linear.
  2. There is time delay between edges of input pulse and corresponding change in output.
    Switching time is defined as the time at which output passes threshold for switching (generally ½ maximum).
  3. Inverter propagation delay is defined by (eq13.36) tp = ½(tPLH + tPHL).

## Slide 28: 13.1.7. Propagation Delay
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Two additional follow-up points may be made:
  A fundamental relationship in analyzing the dynamic operation of a circuit is (eq13.39) It = Q = CV
  A thorough familiarity with time response of single-time-constant (STC) circuits is essential to analysis of such dynamic circuits.
    A review is presented in Appendix E of text.
Example 13.3 demonstrates this link.

## Slide 29
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.15: Definitions of propagation delays and transition times of the logic inverter.

## Slide 30: 13.1.10. Digital IC Technologies and Logic-Circuit Families
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.16: Digital IC technologies and logic-circuit families.

## Slide 31: 13.1.10. Digital IC Technologies and Logic-Circuit Families
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Reasons for CMOS displacing bipolar technology in digital applications:
  CMOS logic circuits dissipate less power.
  MOS transistors offer higher input impedance.
  The size of MOS transistors has been reduced drastically in recent past, more so than bipolar technologies.

## Slide 32: 13.2. The CMOS Inverter
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
CMOS logic inverter is shown in Figure 13.17, consists of:
  p-channel device (QP)
  n-channel device (QN)
vI is employed to manipulate output.
  logic 0 / 1
Figure 13.17: The CMOS inverter.

## Slide 33
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 34: 13.1.6. Power Dissipation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 35
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.20: The voltage-transfer characteristic of the CMOS inverter when QN and QP are matched.

## Slide 36
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.22: Dynamic operation of a capacitively loaded CMOS inverter: (a) circuit; (b) input and output waveforms; (c) equivalent circuit during the capacitor discharge; (d) trajectory of the operating point as the input goes high and C discharges through QN.

## Slide 37: 13.1.6. Power Dissipation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 38: 13.3. Dynamic Operation of the CMOS Inverter
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
How does one analyze the switching operation of the CMOS inverter?
  Step #1: Replace all capacitances in circuit (the various capacitances associated with QN and QP) by a single equivalent capacitance C.
  Step #2: Analyze the resulting capacitively loaded inverter to determine its tPLH and tPHL.

## Slide 39: 13.3.1. Determining Propagation Delay
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.22(a) shows a CMOS inverter with a capacitance C connected between its input node and ground.
To determine propagation delays, apply an ideal pulse.
If circuit is symmetric, both propagation delays may be analyzed together.

## Slide 40: 13.3.3. Dynamic Operation of the CMOS Inverter
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Equations (13.64) through (13.68) in textbook yield several observations:
  Two components of tP can be equalized by selecting W/L ratios to equalize kn and kp.
  Since tp is proportional to C, the designer should strive to reduce C.
  Using a process technology with larger transconductance parameter k’ can result in shorter propagation delays.

## Slide 41: 13.3.3. Dynamic Operation of the CMOS Inverter
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Equations (13.64) through (13.68) in textbook yield several observations:
  Using larger W/L ratios can result in reduction of tP.
  A larger supply voltage VDD results in lower tP.
These observations demonstrate the “trade-offs” associated with design of digital logic gates.

## Slide 42
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.23: Equivalent circuits for determining the propagation delays (a) tPHL and (b) tPLH of the inverter.

## Slide 43: 13.4. CMOS Logic-Gate Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
CMOS logic gate is extension of inverter.
  NMOS pull-down transistor / network
  PMOS pull-up transistor / network
These two networks are operated by input variables in an complementary fashion.

## Slide 44
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.27: Representation of a three-input CMOS logic gate. The PUN comprises PMOS transistors, and the PDN comprises NMOS transistors.

## Slide 45
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.28: Examples of pull-down networks.

## Slide 46
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.29 Examples of pull-up networks.

## Slide 47
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 13.30 Usual and alternative circuit symbols for MOSFETs.

## Slide 48: 13.4. CMOS Logic Gates
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
13.4.2. The Two-Input NOR Gate
  Y = A + B = AB
13.4.3. The Two-Input NAND Gate
  Y = AB = A + B
13.4.4. A Complex Gate
  Y = A(B + CD) = A + B(C + D)
13.4.6. The Exclusive-OR Function
  Y = AB + AB

## Slide 49
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 50: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
An important performance parameter of the inverter is the amount of power it dissipates. There are two components of power dissipation: static and dynamic. The first is the result of current flow in either the 0 or 1 state (or both). The second occurs when the inverter is switched and has a capacitor load C. Dynamic power dissipation Pdyn = fCVDD2.
The speed of operation of the inverter is characterized by its propagation delay (tP).

## Slide 51: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The digital logic inverter is the basic building block of digital circuits, just as the amplifier is the basic building block of analog circuits.
The static operation of the inverter is described by its voltage-transfer characteristic (VTC). The VTC determines the inverter noise margins. In particular, note that NMH = VOH – VIH and NML = VIL – VOL.
The inverter is implemented using transistors operating as voltage-controlled switches.

## Slide 52: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
A metric that combines speed of operation and power dissipation is the power delay product (PDP = PDtP). The lowr the PDP, the more effective the logic-circuit family is.
Besides speed of operation and power dissipation, the silicon area required for an inverter is the third significant metric in digital IC design.
Predominantly because of its lower power dissipation and good scalability, CMOS is by far the more dominant transistor technology for utilization in logic gate design.

## Slide 53: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Digital IC’s usually utilize the minimum channel length of technology available.
For minimum area (W/L)n is selected equal to 1. However, to reduce tP especially when a major part of C is extrinsic to the inverter. (W/L)n and correspondingly (W/L)p can be increased.

## Slide 54
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 55
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 56
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)