## Slide 1: Chapter #2: Signals and Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 2: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  The terminal characteristics of the ideal op-amp.
  How to analyze circuits containing op-amps, resistors, and capacitors.
  How to use op-amps to design amplifiers having precise characteristics.

## Slide 3: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  How to design more sophisticated op-amp circuits, including summing amplifiers, instrumentation amplifiers, integrators, and differentiators.
  Important non-ideal characteristics of op-amps and how these limit the performance of basic op-amp circuits.

## Slide 4: 2.1.1. The Op Amp Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
terminal #1
  inverting input
terminal #2
  non-inverting input
terminal #3
  output
terminal #4
  positive supply VCC
terminal #5
  negative supply VEE
Notes: A useful integrated circuit implementation of an almost idealized amplifier. Often
VCC = VEE for balance with respect to ground (important as it maintains symmetry when overdriven)
Some OpAmps also have differential outputs
<number>

## Slide 5: 2.1.2. Function and Characteristics of Ideal Op Amp
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
ideal gain is defined below
ideal input characteristic is infinite impedance
ideal output characteristic is zero impedance
differential gain (A) is infinite
bandwidth gain is constant from dc to high frequencies
Q: But, is an amplifier with infinite gain of any use?

## Slide 6: 2.1.2. Function and Characteristics of Ideal Op Amp
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
ideal gain: is defined below
ideal input characteristic: infinite impedance
ideal output characteristic: zero impedance
Notes: Idealized OpAmp:
Infinite input impedance (no source loading)
Extremely high gain (A – watch out for oscillation)
Zero output impedance (can deliver power to a load), but real OpAmps are not Zero (741 has 75 ohm Zout)
Differential input (high degree of “common mode” rejection)
Sometimes differential output
<number>

## Slide 7: 2.1.2. Function and Characteristics of Ideal Op-Amp
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
An amplifier’s input is composed of two components…
  differential input (vdfi) – is difference between inputs at inverting and non-inverting terminals
  common-mode input (vcmi) – is input present at both inverting and non-inverting terminals
Notes: An OpAmp tries to reject the common-mode input while amplifying the differential input.
<number>

## Slide 8: 2.1.2. Function and Characteristics of Ideal Op-Amp
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Similarly, two components of gain exist…
  differential gain (A) – gain applied to differential input ONLY
  common-mode gain (Acm) – gain applied to common-mode input ONLY
Notes: Common mode rejection is the ratio between these two gains (usually stated in dB).
dB = 20 log10(A/Acm)
<number>

## Slide 9: 2.1.2. Function and Characteristics of Ideal Op Amp
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Table 2.1: Characteristics of Ideal Op Amp
  infinite input impedance
  zero output impedance
  zero common-mode gain (Acm = 0)
    complete common-mode rejection
  infinite open-loop gain (A = infinity)
  infinite bandwidth
Notes: This “Ideal” is only approached by IC OpAmps
Zi – usually high enough to ignore
Zo – Often higher than needed – follow by a low output impedance stage (emitter-follower)
Acm – usually quite good
A – usually high enough when not asking for too much gain with feedback
BW – needs to be evaluated in use.
<number>

## Slide 10: 2.1.3. Differential & Common-Mode Signals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How is common-mode input (vcmi) defined in terms of v1 and v2?
Notes: Vid = v2 - v1 ; vcmi = (v2 + v1 )/2
<number>

## Slide 11: 2.1.3. Differential & Common-Mode Signals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Notes: A good equivalent circuit as long as your system is balanced
<number>

## Slide 12: 2.2. The Inverting Configuration
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What are two basic closed-loop op-amp configurations which employ op-amp and resistors alone?
  A: 1) inverting and 2) non-inverting op amp
Notes: Two of the three most used configurations
<number>

## Slide 13: 2.2. The Inverting Configuration
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
question: what are two basic closed-loop op amp configurations which employ op-amp and resistors alone?
  answer: inverting and non-inverting op amp
  note: here we examine the inverting type
source is applied to inverting input
non-inverting input is grounded
R2 facilitates “negative feedback”
R1 regulates level of this feedback
Figure 2.5: The inverting closed-loop configuration.
Notes: How can we calculate the gain?
<number>

## Slide 14: 2.2.1. Closed-Loop Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How does one analyze closed-loop gain for inverting configuration of an ideal op-amp?
  step #1: Begin at the output terminal
  step #2: If vOut is finite, then differential input must equal 0
    virtual short circuit btw v1 and v2
    virtual ground exists at v1
Notes: Step “2” is a deduced fact! – very clever
<number>

## Slide 15: 2.2.1. Closed-Loop Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #3: Define current in to inverting input (i1).
step #4: Determine where this current flows?
  refer to following slide…
Notes: Here we are using Node Equations
<number>

## Slide 16: 2.2. The Inverting Configuration
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
question: what are two basic closed-loop op amp configurations which employ op-amp and resistors alone?
  answer: inverting and non-inverting op-amp
  note: here we examine the inverting type
Figure 2.5: The inverting closed-loop configuration.
i1
i = 0
i1
Notes: Here we are using “Node equations” to solve for amplifier gain.
Note that V2 = V1 ! Why?
V1 is at a “virtual ground” due to the high gain (vo is finite)
<number>

## Slide 17: 2.2.1. Closed-Loop Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #5: Define vOut in terms of current flowing across R2.
step #6: Substitute vin / R1 for i1.
note: this expression is one of the fundamentals of electronics
Notes: We had this result in Circuits!
<number>

## Slide 18: 2.2.1. Closed-Loop Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
question: how will we…
  step #4: define vOut in terms of current flowing across R2
  step #5: substitute vin / R1 for i1.
Figure 2.6: Analysis of the inverting configuration. The circled numbers indicate the order of the analysis steps.
closed-loop gain G = -R2/R1

## Slide 19: 2.2.1. Effect of Finite Open-Loop Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How does the gain expression change if open loop gain (A) is not assumed to be infinite?
  A: One must employ analysis similar to the previous, result is presented below…
ideal gain
non-ideal gain
Notes: Seldom needed as the gain is very high
<number>

## Slide 20: 2.2.1. Effect of Finite Open-Loop Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: Under what condition can G = -R2 / R1 be employed over the more complex expression?
  A: If 1 + (R2/R1) << A, then simpler expression may be used.
ideal gain
non-ideal gain

## Slide 21: Example 2.1: Simple Inverting Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Problem Statement: Consider an inverting configuration with R1 = 1kOhm and R2 = 100kOhm.
Q(a): Find the closed-loop gain (G) for the cases below. In each case, determine the percentage error in the magnitude of G relative to the ideal value.
  cases are A = 103, 104, 105…
Q(b): What is the voltage v1 that appears at the inverting input terminal when vIn = 0.1V.
Q(c): If the open loop gain (A) changes from 100k to 50k, what is percentage change in gain (G)?

## Slide 22: 2.2.3. Input and Output Resistances
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is input resistance for inverting op-amp? How is it defined mathematically?
  A: R1 (refer to math below)
Q: What does this say?
  A: That, for the combination of ideal op-amp and external resistors, input resistance will be finite…
this assumes that ideal op-amp and external resistors are considered “one unit”
Notes: Input resistance is determined by R1
Take this into account in your designs or use a “Buffer amp”
<number>

## Slide 23: Example 2.2: Another Inverting Op-Amp
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Problem Statement: Consider the circuit below...
Q(a): Derive an expression for the closed-loop gain vOut/vIn of this circuit.
Q(b): Use this circuit to design an inverting amplifier with gain of 100 and input resistance of 1Mohm.
  Assume that one cannot use any resistor with resistance larger than 1Mohm.
Q(c): Compare your design with that based on traditional inverting configuration.
Figure 2.8: Circuit for Example 2.2. The circled numbers indicate the sequence of the steps in the analysis.

## Slide 24: Example 2.2: Another Inverting Op-Amp
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The largest resistor on may choose is 1Mohm
Q: Where does one begin (in choosing the resistor values)? Which resistor would you define to be 1Mohm?
  A: The input resistance (R1) should be set as high as possible, therefore 1Mohm
Q: What other resistor values should be defined?
  A: R2 = 1Mohm, R4 = 1Mohm, R3 = 10.2kohm
PART B: Use this circuit to design an inverting amplifier with gain of 100 and input resistance of 1Mohm. Assume that one cannot use any resistor with resistance larger than 1Mohm.
Figure 2.9: A current amplifier based on the circuit of Fig. 2.8. The amplifier delivers its output current to R4. It has a current gain of (1 + R2 /R3), a zero input resistance, and an infinite output resistance. The load (R4), however, must be floating (i.e., neither of its two terminals can be connected to ground).

## Slide 25: 2.2.4. An Important Application – The Weighted Summer
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
weighted summer - is a closed-loop amplifier configuration which provides an output voltage which is weighted sum of the inputs.
Figure 2.10: A weighted summer.
Notes: An important configuration
<number>

## Slide 26: 2.2.4. An Important Application – The Weighted Summer
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
weighted summer - is a closed-loop amplifier configuration which provides an output voltage which is weighted sum of the inputs.
Figure 2.10: A weighted summer.
vIn1
vIn2
vIn3
vOut
Rf
RIn1
RIn2
RIn3
vOut = -[ (Rf./RIn1)vIn1 + (Rf./RIn2)vIn2 + (Rf./RIn3)vIn3 + … ]

## Slide 27: 2.3. The Non-Inverting Configuration
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
non-inverting op-amp configuration – is one which utilizes external resistances (like the previous) to effect voltage gain. However, the polarity / phase of the output is same as input.

## Slide 28: 2.3. The Non-Inverting Configuration
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 2.12: The non-inverting configuration.
source is applied to non-inverting input
inverting input is grounded through R1
R1 and R2 act as voltage divider, regulating negative feedback to the inverting input
node #1
node #2
Notes: <number>

## Slide 29: Characteristics of Non-Inverting Op-Amp Configuration
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Notes: Note the 1+ in the Gain!
<number>

## Slide 30: Configuration and Characteristics of Buffer / Voltage-Follower Op-Amp Configuration
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 2.14: (a) The unity-gain buffer or follower amplifier. (b) Its equivalent circuit model.
Notes: This is a useful configuration to “buffer” sub-circuits.
<number>

## Slide 31: Configuration and Characteristics of Buffer / Voltage-Follower Op-Amp Configuration
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 2.14: (a) The unity-gain buffer or follower amplifier. (b) Its equivalent circuit model.
Main point? For the buffer amp, output voltage is equal (in both magnitude and phase) to the input source. However, any current supplied to the load is drawn from amplifier supplies (VCC, VEE) and not the input source (vI).

## Slide 32: 2.4. Difference Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
difference amplifier – is a closed-loop configuration which responds to the difference between two signals applied at its input and ideally rejects signals that are common to the two.
  Ideally, the amp will amplify only the differential signal (vdfi) and reject completely the common-mode input signal (vcmi). However, a practical circuit will behave as below…

## Slide 33: 2.4. Difference Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
differential gain
differential input
common-mode input
common-mode gain

## Slide 34: 2.4. Difference Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
common-mode rejection ratio (CMRR) – is the degree to which a differential amplifier “rejects” the common-mode input.
  Ideally, CMRR = infinity…

## Slide 35: 2.4. Difference Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 2.15: Representing the input signals to a differential amplifier in terms of their differential and common-mode components.

## Slide 36: 2.4. Difference Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: The op amp itself is differential in nature, why cannot it be used by itself?
  A: It has an infinite gain, and therefore cannot be used by itself. One must devise a closed-loop configuration which facilitates this operation.

## Slide 37: 2.4. Difference Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 2.16: A difference amplifier.

## Slide 38: 2.4.1. A Single Op-Amp Difference Amp
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What are the characteristics of the difference amplifier?
  A: Refer to following equations…
Notes: Note: the resistors must be matched to maintain “balance”!
R1 = R3
R2 = R4
<number>

## Slide 39: A Shift in Notation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Before this point…
  The parameter A is used to represent open-loop gain of an op amp.
  The parameter G is used to represent ideal / non-ideal closed-loop gain of an op amp.
After this point…
  The parameter A is used to represent ideal gain of an op amp in a given closed-loop configuration.
  The parameter G is not used.

## Slide 40: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is one problem associated with the difference amplifier?
  A: Low input impedance.
Q: And, what does this mean practically?
  A: That source impedance will have an effect on gain.
Q: What is the solution?
  A: Placement of two buffers at the input terminals, amplifiers which transmit the voltage level but draw minimal current.

## Slide 41: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: However, can one get “more” from these amps than simply impedance matching?
  A: Yes, maybe additional voltage gain???

## Slide 42: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
question: however, can we get “more” from these amps than simply impedance matching?
  answer: yes, maybe additional voltage gain???
Figure 2.20: A popular circuit for an instrumentation amplifier.
stage #1
non-inverting op amp (A1)
non-inverting op amp (A2)
stage #2
difference op amp (A3)
vOut = (1 + R2/R1)vIn
vOut = (R4/R3)vdfi

## Slide 43: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: However, can one get “more” from these amps than simply impedance matching?
  A: Yes, maybe additional voltage gain???
additional voltage gain

## Slide 44: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
advantages of instrumentation amp
  very high input resistance
  high differential gain
  symmetric gain (assuming that A1 and A2 are matched)
disadvantages of instrumentation amp
  ADi and ACm are equal in first stage – meaning that the common-mode and differential inputs are amplified with equal gain…

## Slide 45: What is problem with ACm = A?
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
differential gain >> common-mode gain
differential gain = common-mode gain
vIn1
vIn2
vIn1
vIn2
A = 10 x 25
A = 10
A = 25

## Slide 46: differential gain >> common-mode gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
vIn1 = 10.03V
vIn2 = 10.02V
A = 10 x 25
vOut= 250 x (10.03-10.02)V
vOut = 2.5V no problem!!!

## Slide 47: differential gain = common-mode gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
A = 10
A = 25
vIn1 = 10.03V
vIn2 = 10.02V
vOut1= 10 x 10.03 = 15V saturation
vOut2= 10 x 10.02 = 15V saturation
vOut= 25 x (15-15)V
vOut = 0V problem!!!

## Slide 48: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
advantages of instrumentation amp
  very high input resistance
  high differential gain
  symmetric gain (assuming that A1 and A2 are matched)
disadvantages of instrumentation amp
  ADi and ACm are equal in first stage – meaning that the common-mode and differential inputs are amplified with equal gain…
  need for matching – if two op amps which comprise stage #1 are not perfectly matched, one will see unintended effects

## Slide 49: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How can one fix this (alleviate these disadvantages)?
  A: Disconnect the two resistors (R1) connected to node X from ground, making the configuration “floating” in nature…
  A: Refer to following slide…

## Slide 50: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 2.20: A popular circuit for an instrumentation amplifier. (b) The circuit in (a) with the connection between node X and ground removed and the two resistors R1 and R1 lumped together. This simple wiring change dramatically improves performance.
Notes: A useful configuration
<number>

## Slide 51: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How can one analyze this circuit?
Notes: Again – maintain balance!
<number>

## Slide 52: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #1: note that virtual short circuit exists across terminals of op amp A1 and A2
step #2: define current flow across the resistor 2R1
step #3: define output of A1 and A2

## Slide 53: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
iR1
vOut1
vOut2
short-ckt

## Slide 54: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #4: Define output of A1 and A2 in terms of input alone

## Slide 55: 2.4.2. The Instrumentation Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #5: Define output of A3.
step #6: Define gain of revised instrumentation amplifier.

## Slide 56: 2.5. Integrators and Differentiators
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
integrator / differentiator amplifier – is one which outputs an integral or derivative of the input signal.

## Slide 57: 2.5.1. The Inverting Configuration with General Impedances
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: Does the transfer function for the inverting op amp change if the feedback and input impedances are not purely resistive?
  A: No, not in form…
Notes: This is also introduced in AC Circuits (The second circuits course, EE221 at Fairfield).
In earlier days we use Analog computers using adders, integrators and multipliers.
Now Simulink (in MatLab) simulates an Analog computer using a digital computer.
<number>

## Slide 58: Example 2.4: Other Op-Amp Configurations
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Consider the circuit on next slide page.
Q(a): Derive an expression for the transfer function vOut / vIn.
Q(b): Show that the transfer function is of a low-pass STC circuit.
Q(c): By expressing the transfer function in standard form of Table 1.2, find the dc-gain and 3dB frequency.

## Slide 59: Example 2.4: Other Op-Amp Configurations
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 2.23: Circuit for Example 2.4.

## Slide 60: 2.5.2. The Inverting Integrator
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How can inverting op-amp be adapted to perform integration?
  A: Utilization of capacitor as feedback impedance.

## Slide 61: 2.5.2. The Inverting Integrator
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 2.24: (a) The miller or inverting integrator. (b) Frequency response of the integrator.

## Slide 62: 2.5.2. The Inverting Integrator
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is the problem with this configuration (related to dc gain)?
  A: At dc frequency (= 0), gain is infinite
  Gain = 1 / (R1CF)
Q: Solution?
  A: By placing a very large resistor in parallel with the capacitor, negative feedback is employed to make dc gain “finite.”

## Slide 63: 2.5.2. The Inverting Integrator
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 2.25: The Miller integrator with a large resistance RF connected in parallel with C in order to provide negative feedback and hence finite gain at dc.

## Slide 64: Example 2.5: Miller Integrator
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Consider the Miller integrator…
Q(a): Find response of a Miller Integrator to input pulse of 1V height and 1ms width.
  R1 = 10kOhm, CF = 10nF
Q(b): If the integrator capacitor is shunted by a 1MOhm resistor, how will the response be modified?
  note: the op amp will saturate at +/- 13V

## Slide 65: 2.5.3. The Op-Amp Differentiator
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How can one adapt integrator to perform differentiation?
  A: Interchange locations of resistors and capacitors.
Figure 2.27: A differentiator.

## Slide 66: 2.5.3. The Op-Amp Differentiator
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 2.27: A differentiator.

## Slide 67: 2.5.3. The Op-Amp Differentiator
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
filtering characteristic is high pass filter
magnitude of transfer function is |VOut / VIn| = RFC1
phase of transfer function is  = -90O
differentiator time-constant is frequency at which unity gain occurs and defined as  = 1 / RFC1
Q: What is the problem with differentiator?
  A: Differentiator acts as noise amplifier, exhibiting large changes in output from small (but fast) changes in input. As such, it is rarely used in practice.
Notes: Again you can parallel the input capacitor to limit the noise problem.
<number>

## Slide 68: 2.6. DC Imperfections
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What will be discussed moving on?
  A: When can one NOT consider an op amp to be ideal, and what effect will that have on operation?
Notes: Our Integrated circuits are good, but not perfect
<number>

## Slide 69: 2.6.1. Offset Voltage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is input offset voltage (VOS)?
  A: An imaginary voltage source in series with the user-supplied input, which effects an op amp output even when idfi = 0.
Figure 2.28: circuit model for an op amp with input offset voltage VOS.
What will happen when short is applied?
Notes: Can be a problem due to the high gain
<number>

## Slide 70: 2.6.1. Offset Voltage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What causes VOS?
  A: Unavoidable mismatches in the differential stage of the op amp. It is impossible to perfectly match all transistors.
Q: Range of magnitude?
  A: 1mV to 5mV
Notes: Even though matching in IC transistors (and resistors) can be very good if the designer takes care to analyze heat flow.
<number>

## Slide 71: 2.6.1. Offset Voltage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What causes VOS?
  A: Unavoidable mismatches in the differential stage of the op amp. It is impossible to perfectly match all transistors.
Q: Range of magnitude?
  A: 1mV to 5mV
This relationship between offset voltage (VOS) and offset dc output (VOsOut) applies to both inverting and non-inverting op amp. However, only if one assumes that VOS is present at non-inverting input.

## Slide 72: 2.6.1. Offset Voltage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How can this offset be reduced?
  A: offset nulling terminals – A variable resistor (if properly set) may be used to reduce the asymmetry present and, in turn, reduce offset.
  A: capacitive coupling – A series capacitor placed between the source and op amp may be used to reduce offset, although it will also filter out dc signals.
Notes: Offset nulling is usually a manual adjustment – not great. It can also be done by careful design of a feedback system.
<number>

## Slide 73: Figure 2.30: The output dc offset voltage of an op-amp can be trimmed to zero by connecting a potentiometer to the two offset-nulling terminals. The wiper of the potentiometer is connected to the negative supply of the op amp.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Notes: See the OpAmp specification sheet for terminal pin numbers.
<number>

## Slide 74: Figure 2.31: (a) A capacitively-coupled inverting amplifier. (b) The equivalent circuit for determining its dc output offset voltage VO.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
dc signals cannot pass!

## Slide 75: 2.6.2. Input Bias and Offset Currents
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
input bias current - is the dc current which must be supplied to the op-amp inputs for proper operation.
    Ideally, this current is zero…
input offset current - the difference between bias current at both terminals
Figure 2.32: The op-amp input bias currents represented by two current sources IB1 and IB2.

## Slide 76: 2.6.2: Input Bias and Offset Currents
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
input bias current - is the dc current which must be supplied to the op-amp inputs for proper operation.
    Ideally, this current is zero…
input offset current - the difference between bias current at both terminals
Figure 2.32: The op-amp input bias currents represented by two current sources IB1 and IB2.

## Slide 77: 2.6.2. Input Bias and Offset Currents
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How can this bias be reduced?
  A: Placement of R3 as additional resistor between non-inverting input and ground.
Q: How is R3 defined?
  A: Parallel connection of RF and R1.

## Slide 78: 2.7.1. Frequency Dependence of the Open-Loop Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The differential open-loop gain of an op-amp is not infinite.
It is finite and decreases with frequency.
It is high at dc, but falls off quickly starting from 10Hz.
Figure 2.39: Open-loop gain of a typical general-purpose internally compensated op amp.
Notes: “Internal compensation” is the attempt by the designer to maintain stability (no parasitic oscillation) in most uses of the OpAmp.
<number>

## Slide 79: 2.7.1. Frequency Dependence of the Open-Loop Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
internal compensation – is the presence of internal passive components (caps) which cause op-amp to demonstrate STC low-pass response.
frequency compensation – is the process of modifying the open-loop gain.
  The goal is to increase stability…
Figure 2.39: Open-loop gain of a typical general-purpose internally compensated op amp.

## Slide 80: 2.7.1: Frequency Dependence of the Open-Loop Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The gain of an internally compensated op-amp may be expressed as shown below…

## Slide 81: 2.7.2. Frequency Response of Closed-Loop Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How can we create a more accurate description of closed loop gain for an inverting-type op-amp?
  step #1: Define closed-loop gain of an inverting amplifier with finite open-loop gain (A)
  step #2: Insert frequency-dependent description of A from last slide
  step #3: Assume A0 >> 1 + R2/R1

## Slide 82: 2.7.2. Frequency Response of Closed-Loop Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How can we create a more accurate description of closed loop gain for an both inverting and non-inverting type op-amps?

## Slide 83: 2.7.2. Frequency Response of Closed-Loop Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
3dB frequency – is the frequency at which the amplifier gain is attenuated 3dB from maximum (aka. dc ) value.
Notes: Eg. The “Half-Power” points of the transfer function
<number>

## Slide 84: 2.8. Large-Signal Operation of Op-Amps
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
2.8.1. Output Voltage Saturation
  If supply is +/- 15V, then vOut will saturate around +/- 13V.
2.8.2. Output Current Limits
  iOut current of op-amp, including that which facilitates feedback, cannot exceed X.
  The book approximates X at 20mA.
Notes: There can be either “clipping” (hard limiting) or soft saturation (smooth reduction in small signal gain)
<number>

## Slide 85: 2.8.3. Slew Rate
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
slew rate – is maximum rate of change of an op-amp (V/us)
Q: How can this be problematic?
  A: If slew rate is less than rate of change of input.
Notes: Exceeding the slew rate can cause signal distortion.
<number>

## Slide 86: 2.8.3. Slew Rate
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: Why does slewing occur?
  A: In short, the bandwidth of the op- amp is limited – so the output at very high frequencies is attenuated…

## Slide 87: 2.8.4. Full-Power Bandwidth
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Op-amp slewing will cause nonlinear distortion of sinusoidal waveforms…
  sine wave
  rate of change

## Slide 88: 2.8.4. Full-Power Bandwidth
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
full-power bandwidth (fM) – the maximum frequency at which amplitude of a sinusoidal input and output are equal
maximum output voltage (VOutMax) – is equal to (A*vIn)
  note: an inverse relationship exists between fM and VOutMax
  note: beyond M, output may be defined in terms of 

## Slide 89: Conclusion
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The IC op-amp is a versatile circuit building block. It is easy to apply, and the performance of op-amp circuits closely matches theoretical predictions.
The op-amp terminals are the inverting terminal (1), the non-inverting input terminal (2), the output terminal (3), the positive-supply terminal (4) to be connected to the positive power supply (VCC), and the negative-supply terminal (5) to be connected to the negative supply (-VEE).

## Slide 90: Conclusion (2)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The ideal op-amp responds only to the difference input signal, that is (v2 - v1). It yields an output between terminals 3 and ground of A(v2 - v1). The open-loop gain (A) is assumed to be infinite. The input resistance (Rin) is infinite. The output resistance (Rout) is assumed to be zero.
Negative feedback is applied to an op-amp by connecting a passive component between its output terminal and its inverting (aka. negative) input terminal.

## Slide 91: Conclusion (3)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Negative feedback causes the voltage between the two input terminals to become very small, and ideally zero. Correspondingly, a virtual short is said to exist between the two input terminals. If the positive input terminal is connected to ground, a virtual ground appears on the negative terminal.

## Slide 92: Conclusion (4)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The two most important assumptions in the analysis of op-amp circuits, assuming negative feedback exists, are:
  the two input terminals of the op-amp are at the same voltage potential.
  zero current flows into the op-amp input terminals.
With negative feedback applied and the loop closed, the gain is almost entirely determined by external components: Vo/Vi = -R2/R1 or 1+R2/R1.

## Slide 93: Conclusion (5)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The non-inverting closed-loop configuration features a very high input resistance. A special case is the unity-gain follower, frequently employed as a buffer amplifier to connect a high-resistance source to a low-resistance load.
The difference amplifier of Figure 2.16 is designed with R4/R3 = R2/R1, resulting in vo = (R2/R1)(vI2 - vI1).
Figure 2.16

## Slide 94: Conclusion (6)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The instrumentation amplifier of Figure 2.20(b) is a very popular circuit. It provides vo = (1+R2/R1)(R4/R3)(vI2 - vI1). It is usually designed with R3 = R4 and R1 and R2 selected to provide the required gain. If an adjustable gain is needed, part of R1 can be made variable.
Figure 2.20(b)

## Slide 95: Conclusion (7)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The inverting Miller Amplifier of Figure 2.24 is a popular circuit, frequently employed in analog signal-processing functions such as filters (Chapter 16) and oscillators (Chapter 17).
The input offset voltage (VOS) is the magnitude of dc voltage that when applied between the op-amp input terminals, with appropriate polarity, reduces the dc offset at the output.
Figure 2.24