## Slide 1: Chapter #3: Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 2: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER WE WILL LEARN:
  The basic properties of semiconductors and, in particular, silicone – the material used to make most modern electronic circuits.
  How doping a pure silicon crystal dramatically changes its electrical conductivity – the fundamental idea in underlying the use of semiconductors in the implementation of electronic devices.

## Slide 3: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER WE WILL LEARN:
  The two mechanisms by which current flows in semiconductors – drift and diffusion charge carriers.
  The structure and operation of the pn junction – a basic semiconductor structure that implements the diode and plays a dominant role in semiconductors.

## Slide 4: 3.1. Intrinsic Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
semiconductor – a material whose conductivity lies between that of conductors (copper) and insulators (glass).
  single-element – such as germanium and silicon.
  compound – such as gallium-arsenide.

## Slide 5: 3.1. Intrinsic Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
valence electron – is an electron that participates in the formation of chemical bonds.
  Atoms with one or two valence electrons more than a closed shell are highly reactive because the extra electrons are easily removed to form positive ions.
covalent bond – is a form of chemical bond in which two atoms share a pair of atoms.
  It is a stable balance of attractive and repulsive forces between atoms when they share electrons.

## Slide 6: 3.1. Intrinsic Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
silicon atom
  four valence electrons
  requires four more to complete outermost shell
  each pair of shared forms a covalent bond
  the atoms form a lattice structure
Figure 3.1 Two-dimensional representation of the silicon crystal. The circles represent the inner core of silicon atoms, with +4 indicating its positive charge of +4q, which is neutralized by the charge of the four valence electrons. Observe how the covalent bonds are formed by sharing of the valence electrons. At 0K, all bonds are intact and no free electrons are available for current conduction.

## Slide 7: 3.1. Intrinsic Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
silicon at low temps
  all covalent bonds – are intact
  no electrons – are available for conduction
  conducitivity – is zero
silicon at room temp
  some covalent bonds – break, freeing an electron and creating hole, due to thermal energy
  some electrons – will wander from their parent atoms, becoming available for conduction
  conductivity – is greater than zero
The process of freeing electrons, creating holes, and filling them facilitates current flow…
Notes: Conductivity not zero, but still low
<number>

## Slide 8: 3.1: Intrinsic Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
silicon at low temps:
  all covalent bonds are intact
  no electrons are available for conduction
  conducitivity is zero
silicon at room temp:
  sufficient thermal energy exists to break some covalent bonds, freeing an electron and creating hole
  a free electron may wander from its parent atom
  a hole will attract neighboring electrons
the process of freeing electrons, creating holes, and filling them facilitates current flow
Figure 3.2: At room temperature, some of the covalent bonds are broken by thermal generation. Each broken bond gives rise to a free electron and a hole, both of which become available for current conduction.

## Slide 9: 3.1. Intrinsic Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
intrinsic semiconductor – is one which is not doped
  One example is pure silicon.
generation – is the process of free electrons and holes being created.
  generation rate – is speed with which this occurs.
recombination – is the process of free electrons and holes disappearing.
  recombination rate – is speed with which this occurs.
Generation may be effected by thermal energy. As such, both generation and recombination rates will be (at least in part) a function of temperature.
Notes: We are assuming pure Crystalline semiconductors as opposed to amorphous semiconductor materials
<number>

## Slide 10: 3.1. Intrinsic Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
thermal generation – effects a equal concentration of free electrons and holes.
  Therefore, electrons move randomly throughout the material.
In thermal equilibrium, generation and recombination rates are equal.
Notes: The holes and electrons are randomly distributed in the material.
<number>

## Slide 11: 3.1. Intrinsic Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
In thermal equilibrium, the behavior below applies…
  ni = number of free electrons and holes / unit volume
  p = number of holes
  n = number of free electrons
Notes: This is the Fermi-Dirac distribution. See http://DoctorD.webhop.net/Courses/BEI/EE231/supplement1_carrierconc.pdf
<number>

## Slide 12: 3.1. Intrinsic Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
ni = number of free electrons and holes in a unit volume for intrinsic semiconductor
B = parameter which is 7.3E15 cm-3K-3/2 for silicon
T = temperature (K)
Eg = bandgap energy which is 1.12eV for silicon
k = Boltzman constant (8.62E-5 eV/K)

## Slide 13: Example 3.1
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Refer to book…

## Slide 14: 3.1. Intrinsic Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: Why can thermal generation not be used to effect meaningful current conduction?
  A: Silicon crystal structure described previously is not sufficiently conductive at room temperature.
    Additionally, a dependence on temperature is not desirable.
Q: How can this “problem” be fixed?
  A: doping
doping – is the intentional introduction of impurities into an extremely pure (intrinsic) semiconductor for the purpose changing carrier concentrations.
Notes: Doping is placing pure crystalline silicon in an environment with a gas containing the desired impurity and elevating the temperature so that high energy atoms penetrate the silicon and randomly bump out some silicon atoms.
<number>

## Slide 15: 3.2. Doped Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
p-type semiconductor
  Silicon is doped with element having a valence of 3.
  To increase the concentration of holes (p).
  One example is boron, which is an acceptor.
n-type semiconductor
  Silicon is doped with element having a valence of 5.
  To increase the concentration of free electrons (n).
  One example is phosophorus, which is a donor.
Notes: Look at the periodic table of the elements. The columns correspond to the number of valence electrons.
<number>

## Slide 16: 3.2. Doped Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
p-type semiconductor
  Silicon is doped with element having a valence of 3.
  To increase the concentration of holes (p).
  One example is boron.
n-type semiconductor
  Silicon is doped with element having a valence of 5.
  To increase the concentration of free electrons (n).
  One example is phosophorus, which is a donor.

## Slide 17: 3.2. Doped Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
p-type doped semiconductor
  If NA is much greater than ni …
    concentration of acceptor atoms is NA
  Then the concentration of holes in the p-type is defined as below.

## Slide 18: 3.2. Doped Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
n-type doped semiconductor
  If ND is much greater than ni …
    concentration of donor atoms is ND
  Then the concentration of electrons in the n-type is defined as below.
The key here is that number of free electrons (aka. conductivity) is dependent on doping concentration, not temperature…

## Slide 19: 3.2. Doped Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
p-type semiconductor
  Q: How can one find the concentration?
    A: Use the formula to right, adapted for the p-type semiconductor.
Notes: These are “densities”
<number>

## Slide 20: 3.2. Doped Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
n-type semiconductor
  Q: How can one find the concentration?
    A: Use the formula to right, adapted for the n-type semiconductor.

## Slide 21: 3.2. Doped Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
p-type semiconductor
  np will have the same dependence on temperature as ni2
  the concentration of holes (pn) will be much larger than holes
  holes are the majority charge carriers
  free electrons are the minority charge carrier
n-type semiconductor
  pn will have the same dependence on temperature as ni2
  the concentration of free electrons (nn) will be much larger than holes
  electrons are the majority charge carriers
  holes are the minority charge carrier

## Slide 22: Example 3.2: Doped Semiconductor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Consider an n-type silicon for which the dopant concentration is ND = 1017/cm3. Find the electron and hole concentrations at T = 300K.

## Slide 23: 3.3.1. Drift Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What happens when an electrical field (E) is applied to a semiconductor crystal?
  A: Holes are accelerated in the direction of E, free electrons are repelled.
Q: How is the velocity of these holes defined?
Notes: The electric field is determined by applied voltages (divided by the distance between the voltages)
<number>

## Slide 24: 3.3.1. Drift Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What happens when an electrical field (E) is applied to a semiconductor crystal?
  A: Holes are accelerated in the direction of E, free electrons are repelled.
Q: How is the velocity of these holes defined?
.E (volts / cm)
.p (cm2/Vs) = 480 for silicon
.n (cm2/Vs) = 1350 for silicon
note that electrons move with velocity 2.5 times higher than holes
Notes: The carriers move slowly, not at the speed of light, but signals can move at near the speed of light.
<number>

## Slide 25: 3.3.1. Drift Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What happens when an electrical field (E) is applied to a semiconductor crystal?
  A: Holes are accelerated in the direction of E, free electrons are repelled.
Q: How is the velocity of these holes defined?
Figure 3.5: An electric field E established in a bar of silicon causes the holes to drift in the direction of E and the free electrons to drift in the opposite direction. Both the hole and electron drift currents are in the direction of E.
HOLES
ELECTRONS

## Slide 26: 3.3.1. Drift Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Assume that, for the single-crystal silicon bar on previous slide, the concentration of holes is defined as p and electrons as n.
Q: What is the current component attributed to the flow of holes (not electrons)?

## Slide 27: 3.3.1. Drift Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #1: Consider a plane perpendicular to the x direction.
step #2: Define the hole charge that crosses this plane.
PART A: What is the current component attributed to the flow of holes (not electrons)?

## Slide 28: 3.3.1. Drift Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #3: Substitute in pE.
step #4: Define current density as Jp = Ip / A.
PART A: What is the current component attributed to the flow of holes (not electrons)?

## Slide 29: 3.3.1. Drift Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is the current component attributed to the flow of electrons (not holes)?
  A: to the right…
Q: How is total drift current defined?
  A: to the right…

## Slide 30: 3.3.1. Drift Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
conductivity () – relates current density (J) and electrical field (E)
resistivity () – relates current density (J) and electrical field (E)

## Slide 31: Example 3.3: Doped Semiconductors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q(a): Find the resistivity of intrinsic silicon using following values – n = 1350cm2/Vs, p = 480cm2/Vs, ni = 1.5E10/cm3.
Q(b): Find the resistivity of p-type silicon with NA = 1016/cm2 and using the following values – n = 1110cm2/Vs, p = 400cm2/Vs, ni = 1.5E10/cm3
note that doping reduces carrier mobility

## Slide 32: Note…
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
for intrinsic semiconductor – number of free electrons is ni and number of holes is pi
for p-type doped semiconductor – number of free electrons is np and number of holes is pp
for n-type doped semiconductor – number of free electrons is nn and number of holes is pn
What are p and n?
  generic descriptions of free electrons and holes
majority charge carriers
minority charge carriers

## Slide 33: 3.3.2. Diffusion Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
carrier diffusion – is the flow of charge carriers from area of high concentration to low concentration.
  It requires non-uniform distribution of carriers.
diffusion current – is the current flow that results from diffusion.

## Slide 34: 3.3.2. Diffusion Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Take the following example…
  inject holes – By some unspecified process, one injects holes in to the left side of a silicon bar.
  concentration profile arises – Because of this continuous hole inject, a concentration profile arises.
  diffusion occurs – Because of this concentration gradient, holes will flow from left to right.
Figure 3.6: A bar of silicon (a) into which holes are injected, thus creating the hole concentration profile along the x axis, shown in (b). The holes diffuse in the positive direction of x and give rise to a hole-diffusion current in the same direction. Note that we are not showing the circuit to which the silicon bar is connected.
inject holes
concentration profile arises
diffusion occurs

## Slide 35: 3.3.2. Diffusion Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How is diffusion current defined?

## Slide 36: Example 3.4: Diffusion
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Consider a bar of silicon in which a hole concentration p(x) described below is established.
Q(a): Find the hole-current density Jp at x = 0.
Q(b): Find current Ip.
  Note the following parameters: p0 = 1016/cm3, Lp = 1m, A = 100m2

## Slide 37: 3.3.3. Relationship Between D and ?
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is the relationship between diffusion constant (D) and mobility ()?
  A: thermal voltage (VT)
Q: What is this value?
  A: at T = 300K, VT = 25.9mV
known as Einstein Relationship

## Slide 38: 3.3.3. Relationship Between D and ?
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is the relationship between diffusion constant (D) and mobility ()?
  A: thermal voltage (VT)
Q: What is this value?
  A: at T = 300K, VT = 25.9mV
known as Einstein Relationship
drift current density (Jdrift)
  effected by – an electric field (E).
diffusion current density (Jdiff)
  effected by – concentration gradient in free electrons and holes.

## Slide 39: 3.4.1. Physical Structure
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
pn junction structure
  p-type semiconductor
  n-type semiconductor
  metal contact for connection
Figure 3.8: Simplified physical structure of the pn junction. (Actual geometries are given in Appendix A.) As the pn junction implements the junction diode, its terminals are labeled anode and cathode.
Notes: This is a semiconductor diode. Anode and cathode are old terms from vacuum tube circuits.
<number>

## Slide 40: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is state of pn junction with open-circuit terminals?
A: Read the below…
  p-type material contains majority of holes
    these holes are neutralized by equal amount of bound negative charge
  n-type material contains majority of free electrons
    these electrons are neutralized by equal amount of bound positive charge

## Slide 41: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
bound charge
  charge of opposite polarity to free electrons / holes of a given material
  neutralizes the electrical charge of these majority carriers
  does not affect concentration gradients

## Slide 42: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What happens when a pn-junction is newly formed – aka. when the p-type and n-type semiconductors first touch one another?
  A: See following slides…

## Slide 43: Step #1: The p-type and n-type semiconductors are joined at the junction.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure: The pn junction with no applied voltage (open-circuited terminals).
n-type semiconductor filled with free electrons
p-type semiconductor filled with holes
junction
Notes: The distribution of carriers is approximately uniform (but random).
<number>

## Slide 44: Step #1A: Bound charges are attracted (from environment) by free electrons and holes in the p-type and n-type semiconductors, respectively. They remain weakly “bound” to these majority carriers; however, they do not recombine.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure: The pn junction with no applied voltage (open-circuited terminals).
positive bound charges
negative bound charges

## Slide 45: Step #2: Diffusion begins. Those free electrons and holes which are closest to the junction will recombine and, essentially, eliminate one another.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure: The pn junction with no applied voltage (open-circuited terminals).

## Slide 46: Step #3: The depletion region begins to form – as diffusion occurs and free electrons recombine with holes.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The depletion region is filled with “uncovered” bound charges – who have lost the majority carriers to which they were linked.
Figure: The pn junction with no applied voltage (open-circuited terminals).
Notes: Now the distribution near the junction is not uniform due to recombination.
<number>

## Slide 47: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: Why does diffusion occur even when bound charges neutralize the electrical attraction of majority carriers to one another?
  A: Diffusion current, as shown in (3.19) and (3.20), is effected by a gradient in concentration of majority carriers – not an electrical attraction of these particles to one another.
Notes: There is an internal electric field formed by the charge distribution near the junction.
<number>

## Slide 48: Step #4: The “uncovered” bound charges effect a voltage differential across the depletion region. The magnitude of this barrier voltage (V0) differential grows, as diffusion continues.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
voltage potential
location (x)
barrier voltage (Vo)
No voltage differential exists across regions of the pn-junction outside of the depletion region because of the neutralizing effect of positive and negative bound charges.
Notes: Barrier in that it resists current flow.
<number>

## Slide 49: Step #5: The barrier voltage (V0) is an electric field whose polarity opposes the direction of diffusion current (ID). As the magnitude of V0 increases, the magnitude of ID decreases.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure: The pn junction with no applied voltage (open-circuited terminals).
diffusion current (ID)
drift current (IS)

## Slide 50: Step #6: Equilibrium is reached, and diffusion ceases, once the magnitudes of diffusion and drift currents equal one another – resulting in no net flow.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
diffusion current (ID)
drift current (IS)
Once equilibrium is achieved, no net current flow exists (Inet = ID – IS) within the pn-junction while under open-circuit condition.
p-type
n-type
depletion region

## Slide 51: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
pn-junction built-in voltage (V0) – is the equilibrium value of barrier voltage.
  It is defined to the right.
  Generally, it takes on a value between 0.6 and 0.9V for silicon at room temperature.
  This voltage is applied across depletion region, not terminals of pn junction.
    Power cannot be drawn from V0.
Notes: And the terminal voltage needs to exceed the barrier voltage before appreciable current flows.
<number>

## Slide 52: The Drift Current IS and Equilibrium
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
In addition to majority-carrier diffusion current (ID), a component of current due to minority carrier drift exists (IS).
Specifically, some of the thermally generated holes in the p-type and n-type materials move toward and reach the edge of the depletion region.
There, they experience the electric field (V0) in the depletion region and are swept across it.
  Unlike diffusion current, the polarity of V0 reinforces this drift current.
Notes: Isis the leakage current that flows when the diode is reverse biased.
<number>

## Slide 53: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Because these holes are free electrons are produced by thermal energy, IS is heavily dependent on temperature
Any depletion-layer voltage, regardless of how small, will cause the transition across junction. Therefore IS is independent of V0.
drift current (IS) – is the movement of these minority carriers.
  aka. electrons from n-side to p-side of the junction

## Slide 54: Note that the magnitude of drift current (IS) is unaffected by level of diffusion and / or V0. It will be, however, affected by temperature.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure: The pn junction with no applied voltage (open-circuited terminals).
diffusion current (ID)
drift current (IS)

## Slide 55: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: Is the depletion region always symmetrical? As shown on previous slides?
  A: The short answer is no.
Q: Why?
  Typically NA > ND
  And, because concentration of doping agents (NA, ND) is unequal, the width of depletion region will differ from side to side.
Notes: Depletion region width is also a function of applied voltage.
<number>

## Slide 56: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: Why?
  A: Because, typically NA > ND.
    When the concentration of doping agents (NA, ND) is unequal, the width of depletion region will differ from side to side.
    The depletion region will extend deeper in to the “less doped” material, a requirement to uncover the same amount of charge.
      xp = width of depletion p-region
      xn = width of depletion n-region

## Slide 57: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The depletion region will extend further in to region with “less” doping. However, the “number” of uncovered charges is the same.

## Slide 58: 3.4.2: Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Width of and Charge Stored in the Depletion Region
  the question we ask here is, what happens once the open-circuit pn junction reaches equilibrium???
  typically NA > ND
  minority carrier concentrations at equilibrium (no voltage applied) are denoted by np0 and pn0
  because concentration of doping agents (NA, ND) is unequal, the width of depletion region will differ from side to side
  the depletion region will extend deeper in to the “less doped” material, a requirement to uncover the same amount of charge
    xp = width of depletion p-region
    xn = width of depletion n-region
dv/dx is dependent of Q/W
charge is equal, but width is different

## Slide 59: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How is the charge stored in both sides of the depletion region defined?
  A: Refer to equations to right. Note that these values should equal one another.

## Slide 60: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What information can be derived from this equality?
  A: In reality, the depletion region exists almost entirely on one side of the pn-junction – due to great disparity between NA > ND.

## Slide 61: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Note that both xp and xn may be defined in terms of the depletion region width (W).

## Slide 62: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Note, also, the charge on either side of the depletion region may be calculated via (3.29) and (3.30).

## Slide 63: Example 3.5
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Refer to book…

## Slide 64: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What has been learned about the pn-junction?
  A: composition
    The pn junction is composed of two silicon-based semiconductors, one doped to be p-type and the other n-type.
  A: majority carriers
    Are generated by doping.
    Holes are present on p-side, free electrons are present on n-side.

## Slide 65: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What has been learned about the pn-junction?
  A: bound charges
    Charge of majority carriers are neutralized electrically by bound charges.
  A: diffusion current ID
    Those majority carriers close to the junction will diffuse across, resulting in their elimination.

## Slide 66: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What has been learned about the pn-junction?
  A: depletion region
    As these carriers disappear, they release bound charges and effect a voltage differential V0.
  A: depletion-layer voltage
    As diffusion continues, the depletion layer voltage (V0) grows, making diffusion more difficult and eventually bringing it to halt.

## Slide 67: 3.4.2. Operation with Open-Circuit Terminals
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What has been learned about the pn-junction?
  A: minority carriers
    Are generated thermally.
    Free electrons are present on p-side, holes are present on n-side.
  A: drift current IS
    The depletion-layer voltage (V0) facilitates the flow of minority carriers to opposite side.
  A: open circuit equilibrium ID = IS

## Slide 68: 3.5.1. Qualitative Description of Junction Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure to right shows pn-junction under three conditions:
  (a) open-circuit – where a barrier voltage V0 exists.
  (b) reverse bias – where a dc voltage VR is applied.
  (c) forward bias – where a dc voltage VF is applied.
Figure 3.11: The pn junction in: (a) equilibrium; (b) reverse bias; (c) forward bias.
Notes: This determines the Diode V-I curve.
<number>

## Slide 69
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure to right shows pn-junction under three conditions:
  (a) open-circuit – where a barrier voltage V0 exists.
  (b) reverse bias – where a dc voltage VR is applied.
  (c) forward bias – where a dc voltage VF is applied.
Figure 3.11: The pn junction in: (a) equilibrium; (b) reverse bias; (c) forward bias.
1) no voltage applied
2) voltage differential across depletion zone is V0
3) ID = IS
1) negative voltage applied
2) voltage differential across depletion zone is V0 + VR
3) ID < IS
1) positive voltage applied
2) voltage differential across depletion zone is V0 - VF
3) ID > IS

## Slide 70: 3.5.1. Qualitative Description of Junction Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
reverse bias case
  the externally applied voltage VR adds to (aka. reinforces) the barrier voltage V0
    …increase effective barrier
  this reduces rate of diffusion, reducing ID
    if VR > 1V, ID will fall to 0A
  the drift current IS is unaffected, but dependent on temperature
  result is that pn junction will conduct small drift current IS
forward bias case
  the externally applied voltage VF subtracts from the barrier voltage V0
    …decrease effective barrier
  this increases rate of diffusion, increasing ID
    k
  the drift current IS is unaffected, but dependent on temperature
  result is that pn junction will conduct significant current ID - IS
minimal current flows in reverse-bias case
significant current flows in forward-bias case
Notes: So the diode is approximately a “one-way” valve!
<number>

## Slide 71: Forward-Bias Case
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Observe that decreased barrier voltage will be accompanied by…
  (1) decrease in stored uncovered charge on both sides of junction
  (2) smaller depletion region
Width of depletion region shown to right.

## Slide 72: Reverse-Bias Case
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Observe that increased barrier voltage will be accompanied by…
  (1) increase in stored uncovered charge on both sides of junction
  (2) wider depletion region
Width of depletion region shown to right.
Notes: Note that the diode in reverse bias looks like a parallel plate capacitor. Varactor diodes are used ac a voltage controlled capacitor.
<number>

## Slide 73: 3.5.2. The Current-Voltage Relationship of the Junction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What happens, exactly, when a forward-bias voltage (VF) is applied to the pn-junction?
  step #1: Initially, a small forward-bias voltage (VF) is applied. It, because of its polarity, pushes majority carriers (holes in p-region and electrons in n-region) toward the junction and reduces width of the depletion zone.
    Note, however, that this force is opposed by the built-in voltage built in voltage V0.

## Slide 74: step #1: Initially, a small forward-bias voltage (VF) is applied. It, because of its polarity, pushes majority (holes in p-region and electrons in n-region) toward the junction and reduces width of the depletion zone.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure: The pn junction with applied voltage.
VF
Note that, in this figure, the smaller circles represent minority carriers and not bound charges – which are not considered here.

## Slide 75: step #2: As the magnitude of VF increases, the depletion zone becomes thin enough such that the barrier voltage (V0 – VF) cannot stop diffusion current – as described in previous slides.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure: The pn junction with applied voltage.
VF
Note that removing barrier voltage does not facilitate diffusion, it only removes the electromotive force which opposes it.

## Slide 76: step #3: Majority carriers (free electrons in n-region and holes in p-region) cross the junction and become minority charge carriers in the near-neutral region.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure: The pn junction with applied voltage.
diffusion current (ID)
drift current (IS)
VF

## Slide 77: step #4: The concentration of minority charge carriers increases on either side of the junction. A steady-state gradient is reached as rate of majority carriers crossing the junction equals that of recombination.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure: The pn junction with applied voltage.
minority carrier concentration
location (x)
VF
For the open-circuit condition, minority carriers are evenly distributed throughout the non-depletion regions. This concentration is defined as either np0 or pn0.

## Slide 78: step #4: The concentration of minority charge carriers increases on either side of the junction. A steady-state gradient is reached as rate of majority carriers crossing the junction equals that of recombination.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure: The pn junction with no applied voltage (open-circuited terminals).
VF
minority carrier concentration
location (x)

## Slide 79: step #5+: Diffusion current is maintained – in spite low diffusion lengths (e.g. microns) and recombination – by constant flow of both free electrons and holes towards the junction.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure: The pn junction with no applied voltage (open-circuited terminals).
VF
flow of holes
flow of electrons
flow of diffusion current (ID)
recombination

## Slide 80: 3.5.2. The Current-Voltage Relationship of the Junction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How is the relationship between forward-bias voltage applied (V.) and minority-carrier holes and electrons defined?
  step #1: Employ (3.33).
    This function describes maximum minority carrier concentration at junction.
  step #2: Subtract pn0 from pn(x) to calculate the excess minority charge carriers.
The key aspect of (3.33) is that it relates the minority-charge carrier concentration at the junction boundary in terms of majority-charge carrier on the opposite side.

## Slide 81: 3.5.2. The Current-Voltage Relationship of the Junction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How is the relationship between forward-bias voltage applied (V.) and minority-carrier holes and electrons defined?
  step #3: Refer to (3.35).
    This function describes the minority carrier concentration as a function of location (x), boundary of depletion region (xn), and diffusion length (Lp).

## Slide 82: 3.5.2: The Current-Voltage Relationship of the Junction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
steady-state minority carrier concentration on both sides of a pn-junction for which NA >> ND
excess concentration
“base” concentration

## Slide 83: 3.5.2: The Current-Voltage Relationship of the Junction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
These excess concentrations effect steady-state diffusion current. However, how is this diffusion current defined?

## Slide 84: 3.5.2. The Current-Voltage Relationship of the Junction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: For forward-biased case, how is diffusion current (ID) defined?
  step #1: Take derivative of (3.35) to define component of diffusion current attributed to flow of holes.
  step #2: Note that this value is maximum at x = xn.

## Slide 85: Q: For forward-biased case, how is diffusion current defined?
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
  step #3: Define the component of maximum diffusion current attributed to minority-carrier electrons – in method similar above.

## Slide 86: Q: For forward-biased case, how is diffusion current defined?
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #4: Define total diffusion current as sum of components attributed to free electrons and holes.

## Slide 87: 3.5.2. The Current-Voltage Relationship of the Junction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: For forward-biased case, how is diffusion current (ID) defined?
  A: Refer to (3.40). This is an important equation which will be employed in future chapters.

## Slide 88: 3.5.2. The Current-Voltage Relationship of the Junction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: Why is diffusion current (ID) dependent on the concentration gradient of minority (as opposed to majority) charge carriers?
  A: Essentially, it isn’t.
    Equation (3.33) defines the minority-charge carrier concentration in terms of the majority-charge carrier concentrations in “other” region.
    As such, the diffusion current (ID) is most dependent on two factors: applied forward-bias voltage (VF) and doping.

## Slide 89: 3.5.2. The Current-Voltage Relationship of the Junction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
saturation current (IS) – is the maximum reverse current which will flow through pn-junction.
  It is proportional to cross-section of junction (A).
  Typical value is 10-18A.
Figure 3.13: The pn junction I–V characteristic.

## Slide 90: Example 3.6: pn-Junction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Consider a forward-biased pn junction conducting a current of I = 0.1mA with following parameters:
  NA = 1018/cm3, ND = 1016/cm3, A = 10-4cm2, ni = 1.5E10/cm3, Lp = 5um, Ln = 10um, Dp (n-region) = 10cm2/s, Dn (p-region) = 18cm2/s
Q(a): Calculate IS .
Q(b): Calculate the forward bias voltage (V).
Q(c): Component of current I due to hole injection and electron injection across the junction

## Slide 91: Summary (1)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Today’s microelectronics technology is almost entirely based on the semiconductor silicon. If a circuit is to be fabricated as a monolithic integrated circuit (IC), it is made using a single silicon crystal, no matter how large the circuit is.
In a crystal of intrinsic or pure silicon, the atoms are held in position by covalent bonds. At very low temperatures, all the bonds are intact; No charge carriers are available to conduct current. As such, at these low temperatures, silicone acts as an insulator.

## Slide 92: Summary (2)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
At room temperature, thermal energy causes some of the covalent bonds to break, thus generating free electrons and holes that become available to conduct electricity.
Current in semiconductors is carried by free electrons and holes. Their numbers are equal and relatively small in intrinsic silicon.
The conductivity of silicon may be increased drastically by introducing small amounts of appropriate impurity materials into the silicon crystal – via process called doping.

## Slide 93: Summary (3)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
There are two kinds of doped semiconductor: n-type in which electrons are abundant, p-type in which holes are abundant.
There are two mechanisms for the transport of charge carriers in a semiconductor: drift and diffusion.
Carrier drift results when an electric field (E) is applied across a piece of silicon. The electric field accelerates the holes in the direction of E and electrons oppositely. These two currents sum to produce drift current in the direction of E.

## Slide 94: Summary (4)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Carrier diffusion occurs when the concentration of charge carriers is made higher in one part of a silicon crystal than others. To establish a steady-state diffusion current, a carrier concentration must be maintained in the silicon crystal.
A basic semiconductor structure is the pn-junction. It is fabricated in a silicon crystal by creating a p-region in proximity to an n-region. The pn-junction is a diode and plays a dominant role in the structure and operation of transistors.

## Slide 95: Summary (5)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
When the terminals of the pn-junction are left open, no current flows externally. However, two equal and opposite currents (ID and IS) flow across the junction. Equilibrium is maintained by a built-in voltage (V0). Note, however, that the voltage across an open junction is 0V, since V0 is cancelled by potentials appearing at the metal-to-semiconductor connection interfaces.
The voltage V0 appears across the depletion region, which extends on both sides of the junction.

## Slide 96: Summary (6)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The drift current IS is carried by thermally generated minority electrons in the p-material that are swept across the depletion region into the n-side. The opposite occurs in the n-material. IS flows from n to p, in the reverse direction of the junction. Its value is a strong function of temperature, but independent of V0.
Forward biasing of the pn-junction, that is applying an external voltage that makes p more positive than n, reduces the barrier voltage to V0 - V and results in an exponential increase in ID (while IS remains unchanged).

## Slide 97: Summary (7)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The drift current IS is carried by thermally generated minority electrons in the p-material that are swept across the depletion region into the n-side. The opposite occurs in the n-material. IS flows from n to p, in the reverse direction of the junction. Its value is a strong function of temperature, but independent of V0.
Forward biasing of the pn-junction, that is applying an external voltage that makes p more positive than n, reduces the barrier voltage to V0 - V and results in an exponential increase in ID (while IS remains unchanged).