## Slide 1: Chapter #4: Diodes
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 2: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER WE WILL LEARN
  the characteristics of the ideal diode and how to analyze and design circuits containing multiple ideal diodes together with resistors and dc sources to realize useful and interesting nonlinear function
  the details of the i-v characteristic of the junction diode (which was derived in Chapter 3) and how to use it to analyze diode circuits operating in the various bias regions: forward, reverse, and breakdown
  a simple but effective model of the diode i-v characteristic in the forward direction: the constant-voltage-drop model

## Slide 3: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
a powerful technique for the application and modeling of the diode (and in later chapters, transistors): dc-biasing the diode and modeling its operation for small signals around the dc-operating point by means of the small-signal model
the use of a string of forward-biased diodes and of diodes operating in the breakdown region (zener diodes), to provide constant dc voltages (voltage regulators)
application of the diode in the design of rectifier circuits, which convert ac voltages to dc as needed for powering electronic equipment
a number of other practical and important applications

## Slide 4: 4.1.1. Current-Voltage Characteristic of the Ideal Diode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
ideal diode – most fundament nonlinear circuit element
  two terminal device
  circuit symbol shown to right
  operates in two modes
    on and off
Figure 4.1: Diode characteristics

## Slide 5: 4.1.1. Current-Voltage Characteristic
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
cathode – negative terminal, from which current flows
anode – positive terminal of diode, into which current flows
voltage-current (VI) behavior is:
  piecewise linear for rated values
  nonlinear beyond this range
Notes: Since this is your first exposure to a nonlinear device:
You can model a diode as piecewise linear.
When forward biased – it is a battery (about 0.6 v) in series with a resistance (the slope of the V-I curve).
When reverse biased it is a small constant current source (up to the reverse breakdown voltage = Zener).
When in reverse breakdown again modeled as a battery (The Zener voltage) in series with a small resistance as in the forward direction.
<number>

## Slide 6: 4.1.1: Current-Voltage Characteristic of the Ideal Diode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
ideal diode: is most fundament nonlinear circuit element
  two terminal device with circuit symbol to right
  operates in two modes forward and reverse bias
figure 4.1.
device symbol with two nodes
mode #1: forward bias = short ckt
mode #2: reverse bias = open ckt.
Notes: The “Cathode” is marked on the diode by a stripe near that terminal.
<number>

## Slide 7: 4.1.1. Current-Voltage Characteristic
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
External circuit should be designed to limit…
  current flow across conducting diode
  voltage across blocking diode
Examples are shown to right…
Figure 4.2: The two modes of operation of ideal diodes and the use of an external circuit to limit (a) the forward current and (b) the reverse voltage.

## Slide 8: 4.1.2: A Simple Application – The Rectifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
One fundamental application of this piecewise linear behavior is the rectifier.
Q: What is a rectifier?
  A: Circuit which converts AC waves in to DC…ideally with no loss.
Figure 4.3(a): Rectifier Circuit
Notes: Of course there is always some loss.
<number>

## Slide 9: 4.1.2: A Simple Application – The Rectifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
This circuit is composed of diode and series resistor.
Q: How does this circuit operate?
  A: The diode blocks reverse current flow, preventing negative voltage across R.
Figure 4.3(a): Rectifier Circuit

## Slide 10: Example 4.1: Diode Rectifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Consider the circuit of Figure 4.4. A source (vS) with peak amplitude of 24V is employed to charge a 12V dc-battery.
  Q(a): Find the fraction of each cycle during which the diode conducts.
  Q(b): Find peak value of diode current and maximum reverse-bias voltage that appears across the diode.
Figure 4.4: Circuit and Waveforms for Example 4.1.

## Slide 11: 4.1.3. Another Application, Diode Logic Gates
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How may diodes be used to create logic gates?
  A: Examples of AND / OR gates are shown right.
    Refer to next slide.
Figure 4.5: Diode logic gates: (a) OR gate; (b) AND gate (in a positive-logic system).
Notes: This is Resistor-Diode-Logic, but is generally never used due to practical reasons. The earliest computers used Resistor-Transistor-Logic (RTL) or Diode-Transistor-Logic (DTL).
<number>

## Slide 12
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
OR GATE
AND GATE
IF vA = 5V THEN diodeA will conduct AND vY = vA = 5V
IF any diode conducts THEN vY = 5V
IF vA = 0V THEN diodeA will conduct AND vY = vA = 0V
+ 5V-
+ 5V -
IF all diodes block THEN vY = 5V

## Slide 13: Example 4.2: More Diodes
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What difficulties are associated with multi-diode circuits?
  A: Circuit cannot be solved without knowledge of diodes’ statuses. Yet, statuses are dependent on the solution.
Figure 4.4: Circuit and Waveforms for Example 4.1.
Figure 4.6: Circuits for Example 4.2.
To apply nodal / mesh techniques, one must have knowledge of all component impedances.
IF vB < 0 THEN ZD1 = 0ohms ELSE ZD1 = open circuit

## Slide 14: Example 4.2: More Diodes
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How does one solve these circuits?
  A: One must use the following steps…
    1) assume the status of all diodes
    2) solve via mesh / nodal analysis
    3) check for coherence
Notes: Assume, then test the assumption to see if it works. Repeat.
<number>

## Slide 15: Example 4.2: More Diodes
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How does one check for coherence?
  A: One must ask the following questions…
    1) Are calculated voltages across all “assumed conducting” diodes forward-biased?
    2) Are the calculated currents through all “assumed blocking” diodes zero?
Q: What does one do, if the solution is not coherent?
  A: One must change one or more of these assumptions and solve as well as check for coherence again.
If answer to either of these is no, then the solution is not physically realizable.

## Slide 16: 4.2. Terminal Characteristics of Junction Diodes
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Most common implementation of a diode utilizes pn junction.
I-V curve consists of three characteristic regions
  forward bias: v > 0
  reverse bias: v < 0
  breakdown: v << 0
discontinuity caused by differences in scale

## Slide 17: 4.2.1. The Forward-Bias Region
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The forward-bias region of operation is entered when v > 0.
I-V relationship is closely approximated by equations to right.
(4.3) is a simplification suitable for large v

## Slide 18: 4.2.1. The Forward-Bias Region
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Equation (4.3) may be reversed to yield (4.4).
This relationship applies over as many as seven decades of current.

## Slide 19: 4.2.1. The Forward-Bias Region
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is the relative effect of current flow (i) on forward biasing voltage (v)?
A: Very small.
  10x change in i, effects 60mV change in v.

## Slide 20: 4.2.1: The Forward-Bias Region
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
cut-in voltage – is voltage, below which, minimal current flows
  approximately 0.5V
fully conducting region – is region in which Rdiode is approximately equal 0
  between 0.6 and 0.8V
fully conducting region

## Slide 21: Example 4.3
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Refer to textbook…

## Slide 22: 4.2.2. The Reverse-Bias Region
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The reverse-bias region of operation is entered when v < 0.
I-V relationship, for negative voltages with |v| > VT (25mV), is closely approximated by equations to right.

## Slide 23: 4.2.2. The Reverse-Bias Region
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
A “real” diode exhibits reverse-bias current, although small, much larger than IS .
  10-9 vs. 10-14Amps
A large part of this reverse current is attributed to leakage effects.

## Slide 24: 4.2.3. The Breakdown Region
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The breakdown region of operation is entered when v < VZK.
  Zener-Knee Voltage (VZK)
This is normally non-destructive.
breakdown region
Notes: Calculate the power dissipated to see if it is “Destructive”.
<number>

## Slide 25
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
V = -VZK
V = -VT
V = 10VT

## Slide 26: 4.3. Modeling the Diode Forward Characteristic
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The previous slides define a robust set of diode models.
Upcoming slides, however, discuss simplified diode models better suited for use in circuit analyses:
  exponential model
  constant voltage-drop model
  ideal diode model
  small-signal (linearization) model

## Slide 27: 4.3.1. The Exponential Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
exponential diode model
  most accurate
  most difficult to employ in circuit analysis
    due to nonlinear nature
Notes: Spice simulations (as in Multisim or LTSpice) use this model.
<number>

## Slide 28: 4.3.1. The Exponential Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How does one solve for ID in circuit to right?
  VDD = 5V
  R = 1kOhm
  ID = 1mA @ 0.7V
A: Two methods exist…
  graphical method
  iterative method
Figure 4.10: A simple circuit used to illustrate the analysis of circuits in which the diode is forward conducting.

## Slide 29: 4.3.2. Graphical Analysis Using Exponential Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #1: Plot the relationships of (4.6) and (4.7) on single graph
step #2: Find intersection of the two…
  load line and diode characteristic intersect at operating point
Figure 4.11: Graphical analysis of the circuit in Fig. 4.10 using the exponential diode model.
Notes: Graphical solutions are a classical approach when dealing with nonlinear equations.
The load Line is determined by the linear portion of the circuit.
<number>

## Slide 30: 4.3.2. Graphical Analysis Using Exponential Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Pro’s
  Intuitive
    b/c of visual nature
Con’s
  Poor Precision
  Not Practical for Complex Analyses
    multiple lines required
Figure 4.11: Graphical analysis of the circuit in Fig. 4.10 using the exponential diode model.

## Slide 31: 4.3.3. Iterative Analysis Using Exponential Method
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #1: Start with initial guess of VD.
  VD(0)
step #2: Use nodal / mesh analysis to solve ID.
step #3: Use exponential model to update VD.
  VD(1) = f(VD(0))
step #4: Repeat these steps until VD(k+1) = VD(k).
  Upon convergence, the new and old values of VD will match.

## Slide 32: 4.3.3. Iterative Analysis Using Exponential Method
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Pro’s
  High Precision
Con’s
  Not Intuitive
  Not Practical for Complex Analyses
    10+ iterations may be required
Notes: This is a job for a computer, not a person.
<number>

## Slide 33: 4.3. Modeling the Diode Forward Characteristic
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How can one analyze these diode-based circuits more efficiently?
A: Find a simpler model.
  One example is assume that voltage drop across the diode is constant.

## Slide 34: 4.3.5. The Constant Voltage-Drop Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The constant voltage-drop diode model assumes that the slope of ID vs. VD is vertical @ 0.7V
Q: How does example 4.4 solution change if CVDM is used?
  A: 4.262mA to 4.3mA
Figure 4.12: Development of the diode constant-voltage-drop model: (a) the…

## Slide 35: 4.3.6. Ideal Diode Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The ideal diode model assumes that the slope of ID vs. VD is vertical @ 0V
Q: How does example 4.4 solution change if ideal model is used?
  A: 4.262mA to 5mA

## Slide 36: 4.1.1: Current-Voltage Characteristic of the Ideal Diode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
ideal diode: is most fundament nonlinear circuit element
  two terminal device with circuit symbol to right
  operates in two modes forward and reverse bias
figure 4.1.
device symbol with two nodes
mode #1: forward bias = short ckt
mode #2: reverse bias = open ckt.

## Slide 37: When to use these models?
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
exponential model
  low voltages
  less complex circuits
  emphasis on accuracy over practicality
constant voltage-drop mode:
  medium voltages = 0.7V
  more complex circuits
  emphasis on practicality over accuracy
ideal diode model
  high voltages >> 0.7V
  very complex circuits
  cases where a difference in voltage by 0.7V is negligible
small-signal model
  this is next…

## Slide 38: 4.3.7. Small-Signal Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
small-signal diode model
  Diode is modeled as variable resistor.
  Whose value is defined via linearization of exponential model.
  Around bias point defined by constant voltage drop model.
    VD(0) = 0.7V

## Slide 39: 4.3.7. Small-Signal Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How is the small-signal diode model defined?
  A: The total instantaneous circuit is divided into steady-state and time varying components, which may be analyzed separately and solved via algebra.
    In steady-state, diode represented as CVDM.
    In time-varying, diode represented as resistor.
Neither of these circuits employ the exponential model – simplifying the “solving” process.

## Slide 40
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
CVDM
Figure 4.14: (a) Circuit for Example 4.5. (b) Circuit for calculating the dc operating point. (c) Small-signal equivalent circuit.
DC
AC
DC
AC
Total Instantaneous Solution (vD.)
Steady-State Solution (VD.)
Time-Varying Solution (vd.)
=
+

## Slide 41: 4.3.7. Small-Signal Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How is the small-signal diode model defined?
  step #1: Consider the conceptual circuit of Figure 4.13(a).
    DC voltage (VD) is applied to diode
    Upon VD, arbitrary time-varying signal vd is super-imposed
Notes: This is the way to accurately analyze a nonlinear system when only small perturbations from the Operating Point are present in the system.
<number>

## Slide 42: 4.3.7. Small-Signal Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
DC only – upper-case w/ upper-case subscript
time-varying only – lower-case w/ lower-case subscript
total instantaneous – lower-case w/ upper-case subscript
  DC + time-varying
Notes: Nomenclature (I will try to be consistent with the text).
<number>

## Slide 43: 4.3.7. Small-Signal Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #2: Define DC current as in (4.8).
step #3: Define total instantaneous voltage (vD) as composed of VD and vd.
step #4: Define total instantaneous current (iD) as function of vD.

## Slide 44: 4.3.7. Small-Signal Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #5: Redefine (4.10) as function of both VD and vd.
step #6: Split this exponential in two.
step #7: Redefine total instant current in terms of DC component (ID) and time-varying voltage (vd).

## Slide 45: 4.3.7. Small-Signal Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #8: Apply power series expansion to (4.12).
step #9: Because vd/VT << 1, certain terms may be neglected.

## Slide 46: 4.3.7. Small-Signal Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
small signal approximation
  Shown to right for exponential diode model.
    total instant current (iD)
    small-signal current (id.)
    small-signal resistance (rd.)
  Valid for for vd < 5mV amplitude (not peak to peak).

## Slide 47: 4.3.7. Small-Signal Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
This method may be used to approximate any function y = f(x) around an operating point (x0, y0).

## Slide 48: 4.3.7: Small-Signal Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How is small-signal resistance rd defined?
  A: From steady-state current (ID) and thermal voltage (VT) as below.
    Note this approximation is only valid for small-signal voltages vd < 5mV.

## Slide 49: Example 4.5: Small-Signal Model
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Consider the circuit shown in Figure 4.14(a) for the case in which R = 10kOhm.
The power supply V+ has a dc value of 10V over which is super-imposed a 60Hz sinusoid of 1V peak amplitude (known as the supply ripple)
  Q: Calculate both amplitude of the sine-wave signal observed across the diode.
    A: vd.(peak) = 2.68mV
Assume diode to have 0.7V drop at 1mA current.

## Slide 50
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 4.14: (a) circuit for Example 4.5. (b) circuit for calculating the dc operating point. (c) small-signal equivalent circuit.

## Slide 51: 4.3.8. Use of Diode Forward Drop in Voltage Regulation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is a voltage regulator?
  A: Circuit whose voltage output remains stable in spite of changes in supply and load.
Q: What characteristic of the diode facilitates voltage regulation?
  A: The approximately constant voltage drop across it (0.7V).
Notes: This is NOT a great voltage regulator, but is instructive.
<number>

## Slide 52: Example 4.6: Diode-Based Voltage Regulator
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Consider circuit shown in Figure 4.15. A string of three diodes is used to provide a constant voltage of 2.1V.
  Q: What is the change in this regulated voltage caused by (a) a +/- 10% change in supply voltage and (b) connection of 1kOhm load resistor.
Figure 4.15: Circuit for Example 4.6.
Notes: This is a “shunt” regulator (shunts excess current from going through the load).
i.e. calculate the percentage of regulation – (Percent output change)/(Percent input change) times 100 of course.
<number>

## Slide 53: 4.4. Operation in the Reverse Breakdown Region – Zener Diodes
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Under certain circumstances, diodes may be intentionally used in the reverse breakdown region.
These are referred to as Zener Diodes.
Notes: A somewhat better way to built a shunt regulator. The diode is used in reverse bias.
<number>

## Slide 54: 4.5. Rectifier Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
One important application of diode is the rectifier –
  Electrical device which converts alternating current (AC) to direct current (DC)
One important application of rectifier is dc power supply.
Figure 4.20: Block diagram of a dc power supply

## Slide 55
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 4.20: Block diagram of a dc power supply
step #1: increase / decrease rms magnitude of AC wave via power transformer
step #2: convert full-wave AC to half-wave DC (still time-varying and periodic)
step #3: employ low-pass filter to reduce wave amplitude by > 90%
step #4: employ voltage regulator to eliminate ripple
step #5: supply dc load .
Notes: The diagrams indicate a “full-wave” rectifier.
<number>

## Slide 56: 4.5.1. The Half-Wave Rectifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
half-wave rectifier – utilizes only alternate half-cycles of the input sinusoid
  Constant voltage drop diode model is employed.
Figure 4.21: (a) Half-wave rectifier (b) Transfer characteristic of the rectifier circuit (c) Input and output waveforms

## Slide 57: 4.5.1. The Half-Wave Rectifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
current-handling capability – what is maximum forward current diode is expected to conduct?
peak inverse voltage (PIV) – what is maximum reverse voltage it is expected to block w/o breakdown?

## Slide 58: 4.5.1. The Half-Wave Rectifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
exponential model? It is possible to use the diode exponential model in describing rectifier operation; however, this requires too much work.
small inputs? Regardless of the model employed, one should note that the rectifier will not operate properly when input voltage is small (< 1V).
    Those cases require a precision rectifier.

## Slide 59: 4.5.2. The Full-Wave Rectifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How does full-wave rectifier differ from half-wave?
  A: It utilizes both halves of the input
    One potential is shown to right.
Figure 4.22: Full-wave rectifier utilizing a transformer with a center-tapped secondary winding.

## Slide 60
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 4.22: full-wave rectifier utilizing a transformer with a center-tapped secondary winding: (a) circuit; (b) transfer characteristic assuming a constant-voltage-drop model for the diodes; (c) input and output waveforms.
The key here is center-tapping of the transformer, allowing “reversal” of certain currents…

## Slide 61
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
When instantaneous source voltage is positive, D1 conducts while D2 blocks…

## Slide 62
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
when instantaneous source voltage is negative, D2 conducts while D1 blocks

## Slide 63: 4.5.2. The Full-Wave Rectifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What are most important observation(s) from this operation?
  A: The direction of current flowing across load never changes (both halves of AC wave are rectified). The full-wave rectifier produces a more “energetic” waveform than half-wave.
    PIV for full-wave = 2VS – VD

## Slide 64: 4.5.3. The Bridge Rectifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
An alternative implementation of the full-wave rectifier is bridge rectifier.
  Shown to right.
Figure 4.23: The bridge rectifier circuit.
Notes: You can buy Bridge Rectifier modules at Radio Shack.
<number>

## Slide 65
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 4.23: The bridge rectifier circuit.
when instantaneous source voltage is positive, D1 and D2 conduct while D3 and D4 block

## Slide 66
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 4.23: The bridge rectifier circuit.
when instantaneous source voltage is positive, D1 and D2 conduct while D3 and D4 block

## Slide 67: 4.5.3: The Bridge Rectifier (BR)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is the main advantage of BR?
  A: No need for center-tapped transformer.
Q: What is main disadvantage?
  A: Series connection of TWO diodes will reduce output voltage.
PIV = VS – VD
Notes: Also you need to be careful to control grounds!
<number>

## Slide 68: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Pulsating nature of rectifier output makes unreliable dc supply.
As such, a filter capacitor is employed to remove ripple.
Figure 4.24: (a) A simple circuit used to illustrate the effect of a filter capacitor. (b) input and output waveforms assuming an ideal diode.
Notes: Reduce ripple, not remove it.
<number>

## Slide 69: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #1: source voltage is positive, diode is forward biased, capacitor charges.
step #2: source voltage is reverse, diode is reverse-biased (blocking), capacitor cannot discharge.
step #3: source voltage is positive, diode is forward biased, capacitor charges (maintains voltage).
Figure 4.24 (a) A simple circuit used to illustrate the effect…

## Slide 70: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: Why is this example unrealistic?
  A: Because for any practical application, the converter would supply a load (which in turn provides a path for capacitor discharging).

## Slide 71: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What happens when load resistor is placed in series with capacitor?
  A: One must now consider the discharging of capacitor across load.

## Slide 72: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The textbook outlines how Laplace Transform may be used to define behavior below.
circuit state #2
circuit state #1
Notes: Laplace transforms are introduced in both the Differential Equations math course and the second Circuits course. They are heavily used in the Signals and Systems and Feedback Control courses.
<number>

## Slide 73: Q: What happens when load resistor is placed in series with capacitor?
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #1: Analyze circuit state #1.
  When diode is forward biased and conducting.
step #2: Input voltage (vI) will be applied to output (vO), minus 0.7V drop across diode.
circuit state #1

## Slide 74: Q: What happens when load resistor is placed in series with capacitor?
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #3: Define output voltage for state #1.
circuit state #1

## Slide 75: Q: What happens when load resistor is placed in series with capacitor?
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #4: Analyze circuit state #2.
  When diode is blocking and capacitor is discharging.
step #5: Define KVL and KCL for this circuit.
  vO = RiL
  iL = –iC
circuit state #2

## Slide 76: Q: What happens when load resistor is placed in series with capacitor?
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #6: Use combination of circuit and Laplace Analysis to solve for vO(t) in terms of initial condition and time…

## Slide 77: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 78: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is VO(0)?
  A: Peak of vI, because the transition between state #1 and state #2 (aka. diode begins blocking) approximately as vI drops below vC.

## Slide 79: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #7: Define output voltage for states #1 and #2.
circuit state #2
circuit state #1

## Slide 80
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 4.25: Voltage and Current Waveforms in the Peak Rectifier Circuit WITH RC >> T. The diode is assumed ideal.
Notes: So in the steady state:
The diode conducts when the input voltage is above the capacitor voltage and the capacitor charges up to the peak voltage of the sinusoid.
When the input voltage is below the capacitor voltage, the capacitor discharges due to the load current. The discharge is approximately linear if the ripple is small.
<number>

## Slide 81: A Couple of Observations
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The diode conducts for a brief interval (t) near the peak of the input sinusoid and supplies the capacitor with charge equal to that lost during the much longer discharge interval. The latter is approximately equal to T.
Assuming an ideal diode, the diode conduction begins at time t1 (at which the input vI equals the exponentially decaying output vO). Diode conduction stops at time t2 shortly after the peak of vI (the exact value of t2 is determined by settling of ID).

## Slide 82: A Couple of Observations
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
During the diode off-interval, the capacitor C discharges through R causing an exponential decay in the output voltage (vO). At the end of the discharge interval, which lasts for almost the entire period T, voltage output is defined as follows – vO(T) = Vpeak – Vr.
When the ripple voltage (Vr) is small, the output (vO) is almost constant and equal to the peak of the input (vI). the average output voltage may be defined as below…

## Slide 83: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How is ripple voltage (Vr) defined?
  step #1: Begin with transient response of output during “off interval.”
  step #2: Note T is discharge interval.
  step #3: Simplify using assumption that RC >> T.
  step #4: Solve for ripple voltage Vr.

## Slide 84: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #5: Put expression in terms of frequency (f = 1/T).
  Observe that, as long as Vr << Vpeak, the capacitor discharges as constant current source (IL).
Q: How is conduction interval (t) defined?
  A: See following slides…
expression to define ripple voltage (Vr)

## Slide 85: Q: How is conduction interval (t) defined?
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #1: Assume that diode conduction stops (very close to when) vI approaches its peak.
step #2: With this assumption, one may define expression to the right.
step #3: Solve for t.
cos(0O)

## Slide 86: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How is peak-to-peak ripple (Vr) defined?
  A: (4.29)
Q: How is the conduction interval (t) defined?
  A: (4.30)

## Slide 87: 4.5.4. The Rectifier with a Filter Capacitor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
precision rectifier – is a device which facilitates rectification of low-voltage input waveforms.
Figure 4.27: The “Superdiode” Precision Half-Wave Rectifier and its almost-ideal transfer characteristic.
Notes: Question: Where does the OpAmp get its power?
<number>

## Slide 88: 4.6: Limiting and Clamping Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is a limiter circuit?
  A: One which limits voltage output.
Figure 4.28: General transfer characteristic for a limiter circuit
Notes: Shown is a symmetric limiter.
<number>

## Slide 89: 4.6. Limiting and Clamping Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
passive limiter circuit
  has linear range
  has nonlinear range
  K < 1
  examples include
    single limiter operate in uni-polar manner
    double limiter operate in bi-polar manner

## Slide 90: 4.6. Limiting and Clamping Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
soft vs. hard limiter
Q: How are limiter circuits applied?
  A: Signal processing, used to prevent breakdown of transistors within various devices.
Figure 4.30: Hard vs. Soft Limiting.
Notes: You always have a limiter in a system whether or not it is desired.
<number>

## Slide 91
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 4.31: Variety of basic limiting circuits.
single limiters employ one diode
double limiters employ two diodes of opposite polarity
linear range may be controlled via string of diodes and dc sources
zener diodes may be used to implement soft limiting

## Slide 92: 4.6.2. The Clamped Capacitor or DC Restorer
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is a dc restorer?
  A: Circuit which removes the dc component of an AC wave.
Q: Why is this ability important?
  A: Average value of this output (w/ dc = 0) is effective way to measure duty cycle
Figure 4.32: The clamped capacitor or dc restorer with a square-wave input and no load
Notes: You can restore the DC value to any desired amount by connecting the diode to a voltage source.
<number>

## Slide 93: 4.6.3: The Voltage Doubler
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: What is a voltage doubler?
  A: One which multiplies the amplitude of a wave or signal by two.
Figure 4.34: Voltage doubler: (a) circuit; (b) waveform of the voltage across D1.
Notes: But it has the ripple period of a half wave rectifier.
<number>

## Slide 94: Summary (1)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
In the forward direction, the ideal diode conducts any current forced by the external circuit while displaying a zero-voltage drop. The ideal diode does not conduct in reverse direction; any applied voltage appears as reverse bias across the diode.
The unidirectional current flow property makes the diode useful in the design of rectifier circuits.
The forward conduction of practical silicon-junction diodes is accurately characterized by the relationship i = ISeV/VT.

## Slide 95: Summary (2)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
A silicon diode conducts a negligible current until the forward voltage is at least 0.5V. Then, the current increases rapidly with the voltage drop increasing by 60mV for every decade of current change.
In the reverse direction, a silicon diode conducts a current on the order of 10-9A. This current is much greater than IS and increases with the magnitude of reverse voltage.

## Slide 96: Summary (3)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Beyond a certain value of reverse voltage (that depends on the diode itself), breakdown occurs and current increases rapidly with a small corresponding increase in voltage.
Diodes designed to operate in the breakdown region are called zener diodes. They are employed in the design of voltage regulators whose function is to provide a constant dc voltage that varies little with variations in power supply voltage and / or load current.

## Slide 97: Summary (4)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
In many applications, a conducting diode is modeled as having a constant voltage drop – usually with value of approximately 0.7V.
A diode biased to operate at a dc current ID has small signal resistance rd = VT/ID.
Rectifiers covert ac voltage into unipolar voltages. Half-wave rectifiers do this by passing the voltage in half of each cycle and blocking the opposite-polarity voltage in the other half of the cycle.

## Slide 98: Summary (5)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The bridge-rectifier circuit is the preferred full-wave rectifier configuration.
The variation of the output waveform of the rectifier is reduced considerably by connecting a capacitor C across the output load resistance R. The resulting circuit is the peak rectifier. The output waveform then consists of a dc voltage almost equal to the peak of the input sine wave, Vp, on which is superimposed a ripple component of frequency 2f (in the full-wave case) and of peak-to-peak amplitude Vr = Vp/2fRC.

## Slide 99: Summary (6)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Combination of diodes, resistors, and possible reference voltage can be used to design voltage limiters that prevent one or both extremities of the output waveform from going beyond predetermined values – the limiting levels.
Applying a time-varying waveform to a circuit consisting of a capacitor in series with a diode and taking the output across the diode provides a clamping function.
By cascading a clamping circuit with a peak-rectifier circuit, a voltage doubler is realized.

## Slide 100: Summary (6)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Beyond a certain value of reverse voltage (that depends on the diode itself), breakdown occurs and current increases rapidly with a small corresponding increase in voltage.
Diodes designed to operate in the breakdown region are called zener diodes. They are employed in the design of voltage regulators whose function is to provide a constant dc voltage that varies little with variations in power supply voltage and / or load current.