## Slide 1: Chapter #6: Bipolar Junction Transistors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 2: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  The physical structure of the bipolar transistor and how it works.
  How the voltage between two terminals of the transistor controls the current that flows through the third terminal, and the equations that describe these current-voltage relationships.
  How to analyze and design circuits that contain bipolar transistors, resistors, and dc sources.
  How the transistor can be used to make an amplifier.

## Slide 3: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  How to obtain linear amplification from the fundamentally nonlinear BJT.
  The three basic ways for connecting a BJT to be able to construct amplifiers with different properties.
  Practical circuits for bipolar-transistor amplifiers that can be constructed by using discrete components.

## Slide 4: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
This chapter examines another three-terminal device.
  bipolar junction transistor
  Presentation of this material mirrors chapter 5.
BJT was invented in 1948 at Bell Telephone Laboratories.
  Ushered in a new era of solid-state circuits.
  It was replaced by MOSFET as predominant transistor used in modern electronics.
Notes: The first transistor (~1955) radio that I ever saw was made with Germanium Bipolar Transistors and amazed me as the previous portable radio we had had two batteries (High Voltage B+ and “D” cells for the tube filaments. I wish we hadn’t thrown it out when it stopped working after a couple of years as it would now be worth several thousand dollars as a museum piece. Bipolar transistors first showed up in EE undergraduate curricula in the mid 1960s.
This Bell Telephone Laboratory invention was awarded a Nobel Prize in Physics: John Bardeen and Walter Brattain received the Nobel Prize in Physics, 1956, together with William Shockley, "for their researches on semiconductors and their discovery of the transistor effect."
<number>

## Slide 5: 6.1. Device Structure and Physical Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.1. shows simplified structure of BJT.
Consists of three semiconductor regions:
  emitter region (n-type)
  base region (p-type)
  collector region (n-type)
Type described above is referred to as npn.
  However, pnp types do exist.

## Slide 6: 6.1.1. Simplified Structure and Modes of Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Transistor consists of two pn-junctions:
  emitter-base junction (EBJ)
  collector-base junction (CBJ)
Operating mode depends on biasing.
  active mode – used for amplification
  cutoff and saturation modes – used for switching.
Notes: It is two diodes back to back with a narrow base region in common
<number>

## Slide 7
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.1: A simplified structure of the npn transistor.

## Slide 8
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.2: A simplified structure of the pnp transistor.
Notes: Note that this is normally implemented by doping regions on the surface of a silicon chip
<number>

## Slide 9
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 10: 6.1.2. Operation of the npn-Transistor in the Active Mode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Active mode is “most important.”
Two external voltage sources are required for biasing to achieve it.
Refer to Figure 6.3.
Figure 6.3: Current flow in an npn transistor biased to operate in the active mode. (Reverse current components due to drift of thermally generated minority carriers are not shown.)

## Slide 11: Current Flow
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Forward bias on emitter-base junction will cause current to flow.
This current has two components:
  electrons injected from emitter into base
  holes injected from base into emitter.
It will be shown that first (of the two above) is desirable.
  This is achieved with heavy doping of emitter, light doping of base.

## Slide 12: Current Flow
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
emitter current (iE) – is current which flows across EBJ
  Flows “out” of emitter lead
minority carriers – in p-type region.
  These electrons will be injected from emitter into base.
  Opposite direction.
Because base is thin, concentration of excess minority carriers within it will exhibit constant gradient.

## Slide 13
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Straight line represents constant gradient.

## Slide 14: Current Flow
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Concentration of minority carrier np at boundary EBJ is defined by (6.1).
Concentration of minority carriers np at boundary of CBJ is zero.
  Positive vCB causes these electrons to be swept across junction.

## Slide 15: Current Flow
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Tapered minority-carrier concentration profile exists.
It causes electrons injected into base to diffuse through base toward collector.
As such, electron diffusion current (In) exists.

## Slide 16: Current Flow
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Some “diffusing” electrons will combine with holes (majority carriers in base).
Base is thin, however, and recombination is minimal.
Recombination does, however, cause gradient to take slightly curved shape.
  The straight line is assumed.

## Slide 17
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Recombination causes actual gradient to be curved, not straight.

## Slide 18: The Collector Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
It is observed that most diffusing electrons will reach boundary of collector-base depletion region.
Because collector is more positive than base, these electrons are swept into collector.
  collector current (iC) is approximately equal to In.
  iC = In

## Slide 19: The Collector Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Magnitude of iC is independent of vCB.
  As long as collector is positive, with respect to base.
saturation current (IS) – is inversely proportional to W and directly proportional to area of EBJ.
  Typically between 10-12 and 10-18A
  Also referred to as scale current.

## Slide 20: The Base Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
base current (iB) – composed of two components:
  ib1 – due to holes injected from base region into emitter.
  ib2 – due to holes that have to be supplied by external circuit to replace those recombined.

## Slide 21: The Base Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
common-emitter current gain () – is influenced by two factors:
  width of base region (W)
  relative doping of base emitter regions (NA/ND)
High Value of 
  thin base (small W in nano-meters)
  lightly doped base / heavily doped emitter (small NA/ND)

## Slide 22: The Emitter Current
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
All current which enters transistor must leave.
  iE = iC + iB
Equations (6.7) through (6.13) expand upon this idea.

## Slide 23: Recapitulation and Equivalent-Circuit Models
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Previous slides present first-order BJT model.
  Assumes npn transistor in active mode.
Basic relationship is collector current (iC) is related exponentially to forward-bias voltage (vBE).
  It remains independent of vCB as long as this junction remains reverse biased.
    vCB > 0

## Slide 24
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.5: Large-signal equivalent-circuit models of the npn BJT operating in the forward active mode.

## Slide 25: Example 6.1.
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Refer to textbook for Example 6.1.

## Slide 26: 6.1.3. Structure of Actual Transistors
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.7 shows a more realistic BJT cross-section.
Collector virtually surrounds entire emitter region.
  This makes it difficult for electrons injected into base to escape collection.
Device is not symmetrical.
  As such, emitter and collector cannot be interchanged.
  Device is uni-directional.

## Slide 27
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.7: Cross-section of an npn BJT.

## Slide 28: 6.1.4. Operation in Saturation Mode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
For BJT to operate in active mode, CBJ must be reverse biased.
  However, for small values of forward-bias, a pn-junction does not operate effectively.
As such, active mode operation of npn-transistor may be maintained for vCB down to approximately -0.4V.
  Only after this point will “diode” begin to really conduct.

## Slide 29: 6.1.4. Operation in Saturation Mode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 30: 6.1.4. Operation in Saturation Mode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Two questions must be asked to determine whether BJT is in saturation mode, or not:
  Is the CBJ forward-biased by more than 0.4V?
  Is the ratio iC/iB less than ?

## Slide 31: 6.1.5. The pnp Transistor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.10: Current flow in a pnp transistor biased to operate in the active mode.

## Slide 32: 6.1.5. The pnp Transistor
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.11: Two large-signal models for the pnp transistor operating in the active mode.

## Slide 33: 6.2. Current-Voltage Characteristics
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.12: Circuit symbols for BJTs.
Notes: These are the most common BJT symbols (US IEEE Standards)
<number>

## Slide 34: 6.2.1. Circuit Symbols and Conventions
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.13: Voltage polarities and current flow in transistors biased in the active mode.

## Slide 35: 6.2.1. Circuit Symbols and Conventions
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Notes: Worth another sticky
<number>

## Slide 36: The Collector-Base Reverse Current (ICB0)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Previously, small reverse current was ignored.
  This is carried by thermally-generated minority carriers.
However, it does deserve to be addressed.
The collector-base junction current (ICBO) is normally in the nano-ampere range.
  Many times higher than its theoretically-predicted value.
Notes: The theory does not fully account for the thin base region
<number>

## Slide 37: 6.2.2. Graphical Representation of Transistor Characteristics
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.15/16: (left) The iC-vBE characteristic for an npn transistor. (right) Effect of temperature on the iC-vBE characteristic. Voltage polarities and current flow in transistors biased in the active mode.

## Slide 38: 6.2.3. Dependence of iC on Collector Voltage – The Early Effect
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
When operated in active region, practical BJT’s show some dependence of collector current on collector voltage.
As such, iC-vCB characteristic is not “straight”.
Notes: The BJT is a current controlled current source.
<number>

## Slide 39
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.18: Large-signal equivalent-circuit models of an npn BJT operating in the active mode in the common-emitter configuration with the output resistance ro included.
Notes: This is a useful model of a BJT
<number>

## Slide 40: 6.2.4. An Alternative Form of the Common-Emitter Characteristics
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The Common-Emitter Current Gain
  A second way to quantify  is changing base current by iB and measuing incremental iC.
The Saturation Voltage VCEsat and Saturation Resistance

## Slide 41
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.19: Common-emitter characteristics. (a) Basic CE circuit; note that in (b) the horizontal scale is expanded around the origin to show the saturation region in some detail. A much greater expansion of the saturation region is shown in (c).
Notes: There are instruments that show these curves on a CRT. (Curve tracers)
<number>

## Slide 42
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.20: A simplified equivalent-circuit model of the saturated transistor.

## Slide 43: 6.3. BJT Circuits at DC
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 44: 6.4. Applying the BJT in Amplifier Design
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Similar to the configuration presented in Chapter 5, an amplifier may be designed by transistor and series resistance.
However, it is necessary to model the voltage transfer characteristic (VTC).
  Equation (6.26)
Appropriate biasing is important to ensure linear gain, and appropriate input voltage swing.
  Small-signal model is employed to model the amp’s operation.

## Slide 45
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Notes: Biasing a bipolar transistor is easier than biasing a MOSFET.
<number>

## Slide 46
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.32: Biasing the BJT amplifier at a point Q located on the active-mode segment of the VTC.

## Slide 47
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 48: 6.6. Basic BJT Amplifier Configurations
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 49: 6.6.1. Three-Basic Configurations
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.48: The three basic configurations of BJT amplifier. The biasing arrangements are not shown.

## Slide 50: 6.6.3. The Common-Emitter (CE) Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Of three configurations, the CE amplifier is most widely used.
Figure 6.50(a) shows a common-emitter amplifier – with biasing arrangement omitted.
  signal course (vsig)
  source resistance (Rsig)
  input resistance (Rin)
  gain (Avo)
  output resistance (Ro)
  transconductance (Gv)

## Slide 51: Common-Emitter Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.50: (a) Common-Emitter Amplifier fed with a signal vsig from a generator with a resistance Rsig. (b) The common-emitter amplifier circuit with the BJT replaced with its hybrid-pi model.

## Slide 52: Characteristic Parameters of the CE Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Replacing BJT with hybrid-pi model yields the expressions to right…

## Slide 53: Characteristic Parameters of the CE Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Three Observations
  The input resistance Rin = r = /gm is moderate to low in value.
  The output resistance Ro = RC is moderate to high in value.
  The open-circuit voltage gain (Avo) can be high – making the CE configuration the workhorse in BJT amplifier design.

## Slide 54: Overall Voltage Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 55: 6.6.5. The Common-Base (CB) Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 6.53: (a) CB amplifier with bias details omitted; (b) Amplifier equivalent circuit with the BJT represented by its T Model.
Notes: Not as heavily used as the other two configurations, but has a high frequency advantage.
<number>

## Slide 56: 6.6.7. Summary and Comparisons
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The CE configuration is one of the best suited for realizing the bulk of the gain required in an amplifier. Depending on the magnitude of the gain required, either a single stage o a cascade of two or three stages may be used.
Including a resistor Re in the emitter lead of the CE stage provides a number of performance improvements at the expense of gain reduction.
The low input resistance of the CB amplifier makes it useful only in specific applications.
The emitter follower finds application as a voltage buffer for connecting a high resistance source to a low-resistance load.
Notes: Re is a feedback element.
The emitter follower (common collector) is very useful (high input impedance and low output impedance)
<number>

## Slide 57
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Notes: Another sticky?
<number>

## Slide 58: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Depending on the bias condition on its two junctions, the BJT can operate in one of three possible modes:
  cut-off (both junctions reverse biased)
  active (the EBJ forward-biased and CBJ reversed)
  saturation (both junctions forward biased)
For amplifier applications, the BJT is operated in the active mode. Switching applications make use of the cutoff and saturation modes.
A BJT operating in the active mode provides a collector current iC = ISexp{vBE/VT}. The base current iB = iC/, and emitter current iE = iC + iB.

## Slide 59: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
To ensure operation in the active mode, the collector voltage of an npn-transistor must be kept higher than approximately 0.4V below the base voltage. For a pnp-transistor, the collector voltage must be lower than approximately 0.4V above the base voltage. Otherwise, the CBJ becomes forward-biased and the transistor will enter saturation.
At a constant collector current, the magnitude of the base emitter voltage decreases by about 2mV for every 1OC rise in temperature.
The BJT will be at the edge of saturation when |vCE| is reduced to about 0.3V.

## Slide 60: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
In the active mode, iC shows a slight dependence on vCE. This phenomenon, known as the Early Effect, is modeled by ascribing a finite output resistance to the BJT: ro = |VA|/I’C where VA is the Early Voltage and I’C is the dc collector current without the Early Effect taken into account.
The dc analysis of transistor circuits is generally simplified by assuming |VBE| = 0.7V.
To operate as a linear amplifier, the BJT is biased in the active region and the signal vbe is kept small (vbe << VT).
Bias design seeks to establish a dc collector current that is as independent of  as possible.

## Slide 61: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
For small signals, the BJT functions as a linear voltage-controlled current source with transconductance gm = IC/VT. The input resistance between base and emitter, looking into the base, is r = /gm. The input resistance between bae and emitter, looking into the emitter is re = 1/gm.
Three basic BJT amplifier configurations are shown in Figure 6.48. A summary of their characteristic parameters is provided in Table 6.5.
Notes: I prefer to think of it as a base current controlled collector current source.
<number>