## Slide 1: Chapter #7: Building Blocks of Integrated Circuit Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 2: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER WE WILL LEARN
  The basic integrated-circuit (IC) design philosophy and how it differs from that for discrete-circuit design.
  The basic gain cells of IC amplifiers, namely, the CS and CE amplifiers with current-source loads.
  How to increase the gain realized in the basic gain cells by employing the principle of cascoding.
  Analysis and design of the cascode amplifier and the cascode current source in both their MOS and bipolar forms.

## Slide 3: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER WE WILL LEARN
  How current sources are used to bias IC amplifiers and how the reference current generated in one location is replicated at various other locations on the IC chip by using current mirrors.
  Some ingenious analog circuit design techniques that result in current mirrors with vastly improved characteristics.
  How to pair transistors to realize amplifiers with characteristics superior to those obtained from a single-transistor stage.

## Slide 4: 7.1. Integrated Circuit Design Philosophy
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Integrated-circuit fabrication technology imposes constraints on – and provides opportunities to – the circuit designer.
  large capacitors are not available
  very small capacitors are easy to fabricate
One objective is to realize as many functions as possible using MOS transistors only.
Reduction of device size is of great concern.
In this text, focus is placed on CMOS circuit fabrication.

## Slide 5: 7.2. The Basic Gain Cell
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Two types of basic gain cells exist:
  Common-source (CS)
  Common-emitter (CE)
Both are loaded with constant-current source.
  This is done because of difficulties associated with fabrication of exact resistances.
  It also facilitates increased gain.
These circuits are referred to as current-source loaded / active loaded.

## Slide 6
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.1 The basic gain cells of IC amplifiers: (a) current-source- or active-loaded common-source amplifier; (b) current-source- or active-loaded common-emitter amplifier; (c) small-signal equivalent circuit of (a); and (d) small-signal equivalent circuit of (b).

## Slide 7: 7.2. The Basic Gain Cell
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 8: 7.2.2. The Intrinsic Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
For the BJT, one can derive a formulate for the intrinsic gain Avo = gmro using the formulas below.

## Slide 9: 7.2.2. The Intrinsic Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
A0 is simply ratio of the Early Voltage (VA) and thermal voltage (VT)
  The value of VA ranges from 5V to 35V for modern technologies.
  The value of A0 ranges from 200V/V to 5000V/V, as such.
There are three possible expressions for gm, two are particularly useful here.

## Slide 10: 7.2.2. The Intrinsic Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 11: 7.2.2. The Intrinsic Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The expression (7.13) is one most comparable to the BJT (7.9).
Note the following points:
  The quantity of VOV/2 is a design parameter.
    Its value has been decreasing with technological developments.
  The numerator quantity is both process dependent (through VA’) and device dependent (through L).
    Its value has been decreasing with technological developments.
  From (7.14) we see that A0 may be increased by using a longer MOSFET and operating at lower VOV.
    This is not without trade-offs (refer to textbook).

## Slide 12
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 13: 7.2.3. Effect of the Output Resistance of the Current-Source Load
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The current-source load of the CS amplifier in Figure 7.1(a) can be implemented using a PMOS transistor biased in the saturation region to provide the required current I, as shown in Figure 7.3(a).
Figure 7.1(a)
Figure 7.3(a)

## Slide 14: 7.2.3. Effect of the Output Resistance of the Current-Source Load
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 15: 7.2.3. Effect of the Output Resistance of the Current-Source Load
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.3 (a): The CS amplifier with the current-source load implemented with a p-channel MOSFET Q2 ; (b) the circuit with Q2 replaced with its large-signal model; and (c) small-signal equivalent circuit of the amplifier.

## Slide 16: 7.2.4. Increasing the Gain of the Basic Cell
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Q: How can we increase the voltage gain obtained from basic gain cell?
  A: Find a way to raise the level of output resistance.
  A: Seek a circuit that passes the current gmvi provided by the amplifying transistor right through.
    But increases the resistance from ro to a much larger value.
Figure 7.5: To increase the voltage gain realized in the basic gain cell shown in (a), a functional block, shown as a black box in (b), is connected between d1 and the load.

## Slide 17: 7.2.4. Increasing the Gain of the Basic Cell
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The black box of Figure 7.5. is a current buffer – aka. a device which passes voltage but lowers resistance level.
Two important observations should be made:
  It is not sufficient to raise output resistance of amplifying transistor only.
  Placing CG (or a CB) circuit on top of the CS (or CE) amplifying transistor to implement the current-buffering action is called cascading.

## Slide 18: 7.3. The Cascode Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Cascoding refers to the use of the transistor connected in the common-gate (or common-base) configuration.
Provides current buffering for the output of a common-source (or common-emitter) amplifying transistor.
Figure 7.6. illustrates this technique for MOS case.

## Slide 19: 7.3. The Cascode Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.6: The current-buffering action of Figure 7.5(a) is implemented using a transistor Q2 connected in the CG configuration. Here VG2 is the dc bias voltage.

## Slide 20: 7.3.2. The MOS Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.7(a) shows the MOS cascode amplifier without a load circuit and with the gate of Q2 connected to signal ground.
  This circuit is valid for small-signal calculations only.
Objective is to determine the parameters gm and RO of the equivalent circuit shown in Figure 7.7(b).
If the node d2 of the equivalent circuit is short-circuited to ground, the current flowing through the short-circuit will equal Gmvi.
  Note that Gm = io/vi.

## Slide 21: 7.3.2. The MOS Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.7: (a) A MOS cascode amplifier prepared for small-signal calculations; (b) output equivalent circuit of the amplifier in (a); (c) the cascode amplifier with the output short-circuited to determine Gm; (d) equivalent circuit of the situation in (c).

## Slide 22: 7.3.2. The MOS Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 23: 7.3.2. The MOS Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.8: Determining the output resistance of the MOS cascode amplifier.

## Slide 24: 7.3.2. The MOS Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
If the cascode amplifier is loaded with an ideal constant-current source as shown in Figure 7.9(a), the voltage gain realized can be found from the equivalent circuit in Figure 7.9(b) as Avo = –gm1Ro.

## Slide 25: 7.3.2. The MOS Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.9 (a) A MOS cascode amplifier with an ideal current-source load; (b) equivalent circuit representation of the cascode output.

## Slide 26: 7.3.2. The MOS Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Cascoding may be employed to raise the output resistance of the current-source load as shown in Figure 7.10.
  Here, Q4 is the current-source transistor and Q3 is the CG cascode transistor.
  Voltage VG3 and VG4 are the dc bias voltages.
  The cascode transistor (Q3) multiplies the output resistance of Q4, ro4 to provide an output resistance for the cascode current source of…
    Ro = (gm3ro3)ro4
Combining a cascode amplifier with a cascode current source results in the circuit shown in Figure 7.11.

## Slide 27: 7.3.2. The MOS Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.10 Employing a cascode transistor Q3 to raise the output resistance of the current source Q4.

## Slide 28: 7.3.2. The MOS Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.11: A cascode amplifier with a cascode current-source load.

## Slide 29
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.12: (a) The cascode amplifier with a load resistance RL. Only signal quantities are shown. (b) Determining v01. (c) Determining Rin2.

## Slide 30: 7.3.3. Distribution of Voltage Gain in a Cascode Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 31: 7.3.3. Distribution of Voltage Gain in a Cascode Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
If ro2 is infinite, as was assumed previously, then Rin2 reduces to 1/gm2 – verifying the result found there.
If ro2 cannot be neglected, as is always the case in IC amplifiers, the input resistance depends on the value of RL in an interesting fashion.
  The load resistance (RL) is divided by the factor (gm2ro2).
This transformation is illustrated in Figure 7.13.

## Slide 32: 7.3.3. Distribution of Voltage Gain in a Cascode Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.13: The impedance-transformation properties of the common-gate amplifier. Depending on the values of RS and RL, one can sometimes write Rin = RL/(gmro) and Ro = (gmro)RS. However, such approximations are not always justified.

## Slide 33: 7.3.3. Distribution of Voltage Gain in a Cascode Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 34: 7.3.4. The Output Resistance of a Source-Degenerated CS Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Previous sections discuss benefits obtained when resistance RS is included in the source lead of the CS amplifier.
  Such a resistance is referred to as a source-degeneration resistance because of its action is reducing the effective transconductance of the CS stage to gm/(1+gmRs).
Output resistance is defined as below.

## Slide 35: 7.3.4. The Output Resistance of a Source-Degenerated CS Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.14: The output resistance expression of the cascode can be used to find the output resistance of a source-degenerated common-source amplifier. Here, a useful interpretation of the result is that Rs increases the output resistance by the factor (1 + gmRs).

## Slide 36: 7.3.5. Double Cascoding
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
If still a higher output resistance and correspondingly higher gain are required, it is still possible to add another level of cascoding – as illustrated in Figure 7.15.
Observe that Q3 is the second cascode transistor, and it raises the output resistance by (gm3ro3).
Figure 7.15: Double cascoding.

## Slide 37: 7.3.6. The Folded Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
To avoid the problem of stacking a large number of transistors across a low-voltage power supply, one may use a PMOS transistor for the cascode device – as shown in Figure 7.16.
This provides an alternative to the design proposed in previous section.
Figure 7.16: The folded cascode.

## Slide 38: 7.3.7. The BJT Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.17(a) shows the BJT cascode amplifier with an ideal current-source load.
Voltage VB2 is a dc bias voltage for the CB cascode transistor Q3.
Objective is to determine the parameters Gm and Ro of the equivalent circuit of Figure 7.17(b).
As in case of MOS cascode, Gm is the short-circuit transconductance and can be determined from the circuit in Figure 7.17(c).

## Slide 39
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.17: (a) A BJT cascode amplifier with an ideal current-source load; (b) small-signal equivalent-circuit representation of the output of the cascode amplifier; (c) the cascode amplifier with the output short-circuited to ground, and (d) equivalent circuit representation of (c).

## Slide 40: 7.3.7. The BJT Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 41: 7.3.7. The BJT Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.18: Determining the output resistant Ro of the BJT cascode amplifier.

## Slide 42: 7.3.7. The BJT Cascode
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.19: Determining the output resistant Ro of the BJT cascode amplifier.

## Slide 43: 7.3.8. The Output Resistance of an Emitter-Degenerated CE Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
As done in MOS case, one may adapt the expression for Ro derived from BJT cascode (equation 7.43).
For the case of a CE amplifier with resistance Re connected in its emitter – as shown in Figure 7.20(a).
The output resistance is obtained from equation 7.43 by replacing ro2 with ro, gm2 with gm, r2 with r, and ro1 with Re.

## Slide 44: 7.3.8. The Output Resistance of an Emitter-Degenerated CE Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.20: (a) Output resistance of a CE amplifier with emitter degeneration; (b) The impedance transformation properties of the CB amplifier. Note that for  = infinity, these formulas reduce to those for the MOSFET case (Figure 7.13).

## Slide 45: 7.3.9. BiMOS Cascodes
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Certain advanced CMOS technologies allow the fabrication of bipolar transistors.
They permit the circuit designer to combine MOS and bipolar transistors in circuits that take advantage of the unique features of each.
The resulting technology is called BiCMOS.
Figure 7.21. shows two possible BiCMOS cascode amplifiers.
  The circuit in Figure 7.21(a) uses a MOS transistor for the amplifying device and a BJT for the cascode device.
  The advantage of this circuit is an infinite input resistance as compared with all BJT case.

## Slide 46
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.21: BiCMOS cascodes.

## Slide 47: 7.4. IC Biasing – Current Sources, Current Mirrors, and Current-Steering Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Biasing in integrated-circuit design is based on the use of constant-current sources.
  On an IC chip with a number of amplifier stages, a constant dc current (reference current) is generated at one location and is then replicated at various other locations for biasing.
    This is known as current steering.
This approach has the advantage that the effort expended on generating a predictable and stable reference current need not be repeated.

## Slide 48: 7.4.1. The Basic MOSFET Current Source
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.22. shows the circuit of a simple MOS constant-current source.
The head of the circuit is transistor Q1, the drain of which is shorted to the gate, thereby forcing it to operate in saturation mode – equation (7.52).
The drain current of Q1 is supplied by VDD through resistor R which in most cases is located outside of the IC chip.
If one considers transistor Q2, it is realized that it has VGS identical to Q1 – thus (7.54) through (7.59) apply.

## Slide 49: 7.4.1. The Basic MOSFET Current Source
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.22 Circuit for a basic MOSFET constant-current source. For proper operation, the output terminal, that is, the drain of Q2, must be connected to a circuit that ensures that Q2 operates in saturation.
Figure 7.23: Basic MOSFET current mirror.

## Slide 50: 7.4.1. The Basic MOSFET Current Source
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 51: 7.4.1. The Basic MOSFET Current Source
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The combination of Q1 and Q2 is referred to as a current mirror.
Figure 7.23 depicts the current-mirror circuit with the input reference current shown as being supplied by a current source for both simplicity and generality.
The current gain or current transfer ratio f the mirror is given by (7.55).
The effect of Vo on Io is defined in equations (7.56) through (7.59).

## Slide 52: 7.4.1. The Basic MOSFET Current Source
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 53: 7.4.1. The Basic MOSFET Current Source
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.24: Output characteristic of the current source in Fig. 7.22 and the current mirror of Fig. 7.23 for the case of Q2 matched to Q1.

## Slide 54: 7.4.2. MOS Current-Steering Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Once a constant current has been generated, it can be replicated to provide dc bias or load current for the various stages of the amplifier in an IC.
Current mirrors can be used to achieve this goal.

## Slide 55: 7.4.2. MOS Current-Steering Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.25: A current-steering circuit.

## Slide 56: 7.4.2. MOS Current-Steering Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.26: Application of the constant currents I2 and I5 generated in the current-steering circuit of Fig. 7.25. Constant-current I2 is the bias current for the source follower Q6, and constant-current I5 is the load current for the common-source amplifier Q7.

## Slide 57: 7.4.3. BJT Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The basic BJT current mirror is shown in Figure 7.28.
It works in a fashion very similar to the MOS mirror. However, with two important differences:
  The non-zero bias current causes an error in current mirroring (magnitude of current conducted).
  The current transfer ratio is determined by the relative areas of the emitter-based junctions of Q1 and Q2.
The textbook provides a more detailed description of the BJT-based current mirror – including equations which correspond to those provided for MOS-based mirror.

## Slide 58: 7.4.3. BJT Circuits
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.28: The basic BJT current mirror.

## Slide 59: 7.5. Current-Mirror Circuits with Improved Performance
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Adaptations of the traditional current exist with improved performance. They include:
  7.5.1. Cascode MOS Mirror
    Previous sections demonstrate the cascoding of transistors may be used to increase gain and acquire “better” performance.
  7.5.2. A Bipolar Mirror with Base-Current Compensation
    Base-current compensation may be used to eliminate the effect of bias current on mirror operation. In other words, how may its operation be made more like the MOS implementation.

## Slide 60: 7.5. Current-Mirror Circuits with Improved Performance
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Adaptations of the traditional current exist with improved performance. They include:
  7.5.3. The Wilson Current Mirror
    The addition of a diode-connected transistor in series with Q2 may reduce the effect of  on output resistance.
  7.5.4. The Wilson MOS Mirror
    No  parameter exists for MOS. However, Wilson’s adaptation may be used to increase output resistance and, in turn, gain.
  7.5.5. The Wildar Current Source
    A resistor RE is included in the emitter lead of Q2.

## Slide 61: 7.5. Current-Mirror Circuits with Improved Performance
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.34: The Wilson bipolar current mirror: (a) circuit showing analysis to determine the current transfer ratio; (b) determining the output resistance.

## Slide 62: 7.5. Current-Mirror Circuits with Improved Performance
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.35: The Wilson MOS mirror: (a) circuit; (b) analysis to determine output resistance; (c) modified circuit.

## Slide 63: 7.5. Current-Mirror Circuits with Improved Performance
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.36: The Widlar current source.

## Slide 64: 7.5. Current-Mirror Circuits with Improved Performance
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 7.35: The Wilson MOS mirror: (a) circuit; (b) analysis to determine output resistance; (c) modified circuit.

## Slide 65: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Integrated-circuit fabrication technology offers the circuit designer many exciting opportunities, the most important of which is the large number of inexpensive small-area MOS transistors. An overriding concern for IC designers, however, is the minimization of chip area or “silicon real estate.” As a result, large-valued resistors and capacitors are virtually absent.
The basic gain cell of IC amplifier is the CS (CE) amplifier with a current-source load. For an ideal current-source load (i.e. one with infinite output resistance), the transistor operates in an open-circuit fashion and thus provides the maximum gain possible: Avo = -gmro = -A0.

## Slide 66: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The intrinsic gain A0 is given by A0 = VA / VT for a BJT and A0 = VA/(VOV/2) for a MOSFET. For a BJT, A0 is constant independent of bias current and device dimensions. For a MOSFET, A0 is inversely proportional to ID1/2. See equation 7.15.
Simple current-source loads reduce the gain realized in the basic gain cell because of their finite resistance (usually comparable to the value of ro of the amplifying transistor).
To raise the output resistance of the CS or CE transistor, we stack a CG or CB transistor on top. This is cascoding. The CG or CB transistor in the cascode passes the current gm1vi provided by the CS or CE transistor.

## Slide 67: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
A MOS cascode amplifier operating with an ideal current source load achieves a gain of (gmro)2 = A02.
To realize the full advantage of cascoding, the load current-source must also be cascoded, in which case a gain as high as 1/2A02 can be obtained.
Double cascoding is possible in the MOS case only. However, the large number of transistors in the stack between the power-supply rails results in the disadvantages of a severely limited output-signal swing. The folded-cascode configuration helps to resolve this issue.

## Slide 68: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
A CS amplifier with a resistance Rs in its source lead has an output resistance Ro = (1+gmRS)ro. The corresponding formula for the BJT case is Ro = [1+gm(Re||r)]ro.
Biasing in integrated circuits utilizes current sources. As well, current sources are used as load devices. Typically an accurate and stable reference current is generated and then replicated to provide bias current for the various amplifier stages on the chip. The heart of the current-steering circuitry utilized to perform this function is the current mirror.
The MOS current mirror has a current transfer ratio of (W/L)2/(W/L)1. For a bipolar mirror, the ratio is IS2/IS1.

## Slide 69: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Bipolar mirrors suffer from the finite b, which reduces the accuracy of the current transfer ratio.
Both bipolar and MOS mirrors of the basic type have a finite output resistance equal to ro of the output device. Also, for proper operation, a voltage of at least 0.3V is required across the output transistor of a simple bipolar mirror (|VOV| for the MOS case).
Cascoding can be applied to current mirrors to increase their output resistances. An alternative that also solves the  problem is the bipolar case is the Wilson circuit.