## Slide 1: Chapter #8: Differential and Multistage Amplifiers
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 2: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER YOU WILL LEARN:
  The essence of the operation of the MOS and the bipolar differential amplifiers: how they reject common-mode noise or interference and amplify differential signals.
  The analysis and design of MOS and BJT differential amplifiers.
  Differential amplifier circuits of varying complexity; utilizing passive resistive loads, current-source loads, and cascodes - the building blocks studied in Chapter 7.
  An ingenious and highly popular differential-amplifier circuit that utilizes a current-mirror load.

## Slide 3: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
IN THIS CHAPTER YOU WILL LEARN:
  The structure, analysis, and design of amplifiers composed of two or more stages in cascade. Two practical examples are studied in detail: a two-stage CMOS op-amp and four-stage bipolar op-amp.

## Slide 4: Introduction
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The differential-pair of differential-amplifier configuration is widely used in IC circuit design.
  One example is input stage of op-amp.
  Another example is emitter-coupled logic (ECL).
Technology was invented in 1940’s for use in vacuum tubes – the basic differential-amplifier configuration was later implemented with discrete bipolar transistors.
However, the configuration became most useful with invention of modern transistor / MOS technologies.

## Slide 5: 8.1. The MOS Differential Pair
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 8.1: MOS differential-pair configuration.
Two matched transistors (Q1 and Q2) joined and biased by a constant current source I.
FET’s should not enter triode region of operation.

## Slide 6: 8.1. The MOS Differential Pair
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 8.1: The basic MOS differential-pair configuration.

## Slide 7: 8.1.1. Operation with a Common-Mode Input Voltage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Consider case when two gate terminals are joined together.
  Connected to a common-mode voltage (VCM).
  vG1 = vG2 = VCM
Q1 and Q2 are matched.
Current I will divide equally between the two transistors.
  ID1 = ID2 = I/2, VS = VCM – VGS
    where VGS is the gate-to-source voltage.

## Slide 8: 8.1.1. Operation with a Common-Mode Input Voltage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Equations (8.2) through (8.8) describe this system, if channel-length modulation is neglected.
  Note specification of input common-mode range (VCM).

## Slide 9: 8.1.2. Operation with a Differential Input Voltage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
If vid is applied to Q1 and Q2 is grounded, following conditions apply:
  vid = vGS1 – vGS2 > 0
  iD1 > iD2
The opposite applies if Q2 is grounded etc.
The differential pair responds to a difference-mode or differential input signals.

## Slide 10: 8.1.2. Operation with a Differential Input Voltage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 8.4: The MOS differential pair with a differential input signal vid applied.

## Slide 11: 8.1.2. Operation with a Differential Input Voltage
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Two input terminals connected to a suitable dc voltage VCM.
Bias current I of a “perfectly” symmetrical differential pair divides equally.
  Zero voltage differential between the two drains (collectors).
To steer the current completely to one side of the pair, a difference input voltage vid of at least 21/2VOV (4VT for bipolar) is needed.

## Slide 12: 8.1.3. Large-Signal Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Objective is to derive expressions for drain current iD1 and iD2 in terms of differential signal vid = vG1 – vG2.
Assumptions:
  Perfectly Matched
  Channel-length Modulation is Neglected
  Load Independence
  Saturation Region

## Slide 13: 8.1.3. Large-Signal Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #1: Expression drain currents for Q1 and Q2.
step #2: Take the square roots of both sides of both (8.11) and (8.12)
step #3: Subtract (8.14) from (8.15) and perform appropriate substitution.
step #4: Note the constant-current bias constraint.

## Slide 14: 8.1.3. Large-Signal Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
step #5: Simplify (8.15).
step #6: Incorporate the constant-current bias.
step #7: Solve (8.16) and (8.17) for the two unknowns – iD1 and iD2.
  Refer to (8.23) and (8.24).

## Slide 15: 8.1.3. Large-Signal Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 8.6 Normalized plots of the currents in a MOSFET differential pair. Note that VOV is the overdrive voltage at which Q1 and Q2 operate when conducting drain currents equal to I/2, the equilibrium situation. Note that these graphs are universal and apply to any MOS differential pair
Figure 8.6: Normalized plots of the currents in a MOSFET differential pair. Note that VOV is the overdrive voltage at which Q1 and Q2 operate when conducting drain currents equal to I/2, the equilibrium situation. Note that these graphs are universal and apply to any MOS differential pair

## Slide 16: 8.1.3. Large-Signal Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Transfer characteristics of (8.23) and (8.24) are nonlinear.
Linear amplification is desirable and vid will be as small as possible.
For a given value of VOV, the only option is to keep vid/2 much smaller than VOV.

## Slide 17: 8.1.3. Large-Signal Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 8.7: The linear range of operation of the MOS differential pair can be extended by operating the transistor at a higher value of VOV .

## Slide 18: 8.2. Small-Signal Operation of the MOS Differential Pair
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 19: 8.2.1. Differential Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Two reasons single-ended amplifiers are preferable:
  Insensitive to interference.
  Do not need bypass coupling capacitors.

## Slide 20: 8.2.1. Differential Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
For MOS pair, each device operates with drain current I/2 and corresponding overdrive voltage (VOV).
   = 1
MOS: gm = I/VOV
BJT: gm = I/2VT
MOS: ro = |VA|/(I/2).

## Slide 21: 8.2.1. Differential Gain
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
vi1 = VCM + vid/2 and vi2 = VCM – vid/2 causes a virtual signal ground to appear on the common-source (common-emitter) connection
Current in Q1 increases by gmvid/2 and the current in Q2 decreases by gmvid/2.
Voltage signals of gm(RD||ro)vid/2 develop at the two drains (collectors, with RD replaced by RC).

## Slide 22: 8.2.2. The Differential Half-Circuit
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 8.9 (right): The equivalent differential half-circuit of the differential amplifier of Figure 8.8.
Here Q1 is biased at I/2 and is operating at VOV.
This circuit may be used to determine the differential voltage gain of the differential amplifier Ad = vod/vid.

## Slide 23: 8.2.3. The Differential Amplifier with Current-Source Loads
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
To obtain higher gain, the passive resistances (RD) can be replaced with current sources.
Ad = gm1(ro1||ro3)
Figure 8.11: (a) Differential amplifier with current-source loads formed by Q3 and Q4. (b) Differential half-circuit of the amplifier in (a).

## Slide 24: 8.2.4. Cascode Differential Amplifier
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Gain can be increased via cascode configuration – discussed in Section 7.3.
  Ad = gm1(Ron||Rop)
  Ron = (gm3ro3)ro1
  Rop = (gm5ro5)ro7
Figure 8.12: (a) Cascode differential amplifier; and (b) its differential half circuit.

## Slide 25: 8.2.5. Common-Mode Gain and Common-Mode Rejection ratio (CMRR)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Equation (8.43) describes effect of common-mode signal (vicm) on vo1 and vo2.

## Slide 26
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)

## Slide 27: 8.2.5. Common-Mode Gain and Common-Mode Rejection ratio (CMRR)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
When the output is taken single-ended, magnitude of common-mode gain is defined in (8.46) and (8.47).
Taking the output differentially results in the perfectly matched case, in zero Acm (infinite CMRR).

## Slide 28: 8.2.5. Common-Mode Gain and Common-Mode Rejection ratio (CMRR)
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Mismatches between the two sides of the pair make Acm finite even when the output is taken differentially.
  This is illustrated in (8.49).
Corresponding expressions apply for the bipolar pair.

## Slide 29: 8.3. The BJT Differential Pair
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Figure 8.15 shows the basic BJT differential-pair configuration.
It is similar to the MOSFET circuit – composed of two matched transistors biased by a constant-current source – and is modeled by many similar expressions.
Figure 8.15: The basic BJT differential-pair configuration.

## Slide 30: 8.3.1. Basic Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
To see how the BJT differential pair works, consider the first case of the two bases joined together and connected to a common-mode voltage VCM.
  Illustrated in Figure 8.16.
Since Q1 and Q2 are matched, and assuming an ideal bias current I with infinite output resistance, this current will flow equally through both transistors.
Figure 8.16: Different modes of operation of the BJT differential pair: (a) the differential pair with a common-mode input voltage VCM; (b) the differential pair with a “large” differential input signal; (c) the differential pair with a large differential input signal of polarity opposite to that in (b); (d) the differential pair with a small differential input signal vi. Note that we have assumed the bias current source I to be ideal.

## Slide 31: 8.3.1. Basic Operation
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
To see how the BJT differential pair works, consider the first case of the two bases joined together and connected to a common-mode voltage VCM.
  Illustrated in Figure 8.16.
Since Q1 and Q2 are matched, and assuming an ideal bias current I with infinite output resistance, this current will flow equally through both transistors.
Figure 8.16: Different modes of operation of the BJT differential pair: (a) the differential pair with a common-mode input voltage VCM; (b) the differential pair with a “large” differential input signal; (c) the differential pair with a large differential input signal of polarity opposite to that in (b); (d) the differential pair with a small differential input signal vi. Note that we have assumed the bias current source I to be ideal.

## Slide 32: 8.3.2. Input Common-Mode Range
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
Refer to the circuit in Figure 8.16(a).
The allowable range of VCM is determined at the upper end by Q1 and Q2 leaving the active mode and entering saturation.
Equations (8.66) and (8.67) define the minimum and maximum common-mode input voltages.

## Slide 33: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The differential-pair or differential-amplifier configuration is most widely used building block in analog IC designs. The input stage of every op-amp is a differential amplifier.
There are two reasons for preferring differential to single-ended amplifiers: 1) differential amplifiers are insensitive to interference and 2) they do not need bypass and coupling capacitors.
For a MOS (bipolar) pair biased by a current source I, each device operates at a drain (collector, assuming  = 1) current of I/2 and a corresponding overdrive voltage VOV (no analog in bipolar). Each device has gm=1/VOV (I/2VT for bipolar).

## Slide 34: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
With the two input terminals connected to a suitable dc voltage VCM, the bias current I of a perfectly symmetrical differential pair divides equally between the two transistors of the pair, resulting in zero voltage difference between the two drains (collectors). To steer the current completely to one side of the pair, a difference input voltage vid of at least 21/2VOV is needed.
Superimposing a differential input signal vid on the dc common-mode input voltage VCM such that vI1 = VCM + vid/2 and vI2 = VCM – vid/2 causes a virtual signal ground to appear on the common-source (common-emitter) connection.

## Slide 35: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
The analysis of a differential amplifier to determine differential gain, differential input resistance, frequency response of differential gain, and so on is facilitated by employing the differential half-circuit which is a common-source (common-emitter) transistor biased at I/2.
An input common-mode signal vicm gives rise to drain (collector) voltage signals that are ideally equal and given by –vicm(RD/2RSS)[-vicm(RC/2REE) for the bipolar pair], where RSS (REE) is the output resistance of the current source that supplies the bias current I.

## Slide 36: Summary
Oxford University Publishing
Microelectronic Circuits by Adel S. Sedra and Kenneth C. Smith (0195323033)
While the input differential resistance Rid of the MOS pair is infinite, that for the bipolar pair is only 2r but can be increased to 2(+1)(re+Re) by including resistances Re in the two emitters. The latter action, however, lowers Ad.
Mismatches between the two sides of a differential pair result in a differential dc output voltage (Vo) even when the two input terminals are tied together and connected to a dc voltage VCM. This signifies the presence of an input offset voltage VOS = VO/Ad. In a MOS pair, there are three main sources for VOS. Two exist for the bipolar pair.