## Slide 1: Chapter #9: Frequency Response
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 2: Introduction
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  How coupling and bypass capacitors cause the gain of discrete circuit amplifiers to fall off at low frequencies, and how to obtain an estimate of the frequency fL at which the gain decreases by 3dB below its value at midband.
  The internal capacitive effects present in the MOSFET and the BJT and how to model these effects by adding capacitances to the hybrid-p model of each of the two transistor types.
  The high-frequency limitation on the gain of the CS and CE amplifiers and how the gain falloff and the upper 3-dB frequency fH are mostly determined by the small capacitances between the drain and gate (collector and base).

## Slide 3: Introduction
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
IN THIS CHAPTER YOU WILL LEARN
  Powerful methods for the analysis of the high-frequency response of amplifier circuits of varying complexity.
  How the cascode amplifier studied in Chapter 7 can be designed to obtain wider bandwidth than is possible with CS and CE amplifiers.
  The high-frequency performance of the source and emitter followers.
  The high-frequency performance of differential amplifiers.
  Circuit configurations for obtaining wideband amplification.

## Slide 4: Introduction
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Previously assumed that gain is constant and independent of frequency.
  implied that bandwidth was infinite
  this is not true
Middle-frequency band (midband) is the range of frequencies over which device gain is constant.

## Slide 5
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.1: Sketch of the magnitude of the gain of a discrete-circuit BJT or MOS amplifier versus frequency. The graph delineates the three frequency bands relevant to frequency-response determination.

## Slide 6: 9.1. Low Frequency Response of the Common-Source and Common-Emitter Amplifiers
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.2(a) shows a discrete-circuit, common-source amplifier.
  coupling capacitors CC1 and CC2
  bypass capacitor CS
Objective is to determine the effect of these capacitances on gain (Vo/Vsig).
At low frequencies, their reactance (1/jC) is high and gain is low.

## Slide 7: 9.1.1. The CS Amplifier
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Determining Vo/Vsig
  figure 9.2(b) illustrates this process
  circuit with dc sources eliminated
  small-signal analysis
  ignore ro

## Slide 8: 9.1.1. The CS Amplifier
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 9: 9.1.1. The CS Amplifier
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 10
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.2: (a) Capacitively coupled common-source amplifier. (b) Analysis of the CS amplifier to determine its low-frequency transfer function. For simplicity, ro is neglected.

## Slide 11
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.3: Sketch of the low-frequency magnitude response of a CS amplifier for which the three pole frequencies are sufficiently separated for their effects to appear distinct.

## Slide 12: 9.1.1. The CS Amplifier
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Determining the Pole Frequencies by Inspection
  Reduce VSig to zero.
  Consider each capacitor separately.
  Find the total resistance seen between terminals of each capacitor.

## Slide 13: 9.1.2. The CE Amplifier
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.4. shows common-emitter amplifier.
  coupling capacitors CC1 and CC2
  emitter bypass capacitor CE
Effect of these capacitors felt at low frequencies.
Objective is to determine amplifier gain and transfer function.
This analysis is somewhat more complicated than CS case.

## Slide 14
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.4: (a) A capacitively coupled common-emitter amplifier. (b) The circuit prepared for small-signal analysis.

## Slide 15: 9.1.2. The CE Amplifier
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 16
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.5: Analysis of the low-frequency response of the CE amplifier of Fig. 9.4: (a) the effect of CC1 is determined with CE and CC2 assumed to be acting as perfect short circuits; (b) the effect of CE is determined with CC1 and CC2 assumed to be acting as perfect short circuits;

## Slide 17
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.5: (continued ) (c) the effect of CC2 is determined with CC1 and CE assumed to be acting as perfect short circuits; (d) sketch of the low-frequency gain under the assumptions that CC1, CE, and CC2 do not interact and that their break (or pole) frequencies are widely separated.

## Slide 18: 9.1.2. The CE Amplifier
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 19: 9.2. Internal Capacitive Effects and the High-Frequency Model of the MOSFET and BJT
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
MOSFET has internal capacitance (this is apparent).
  The gate capacitive effect: The gate electrode forms a parallel plate capacitor with the channel.
  The source-body and drain-body depletion layer capacitances: These are the capacitances of the reverse-biased pn-junctions.
Previously, it was assumed that charges are acquired instantaneously - resulting in steady-state model.
  This assumption poses problem for frequency analysis.

## Slide 20: The Gate Capacitive Effect
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 21: The Junction Capacitances
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 22
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.6 (a) High-frequency, equivalent-circuit model for the MOSFET. (b) The equivalent circuit for the case in which the source is connected to the substrate (body). (continued)

## Slide 23
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.6: (continued) (c) The equivalent-circuit model of (b) with Cdb neglected (to simplify analysis).

## Slide 24: The MOSFET Unity-Gain Frequency (fT)
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 25
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 26: 9.2.2. The BJT
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Like MOSFET, previously it was assumed that transistor action was instantaneous.
  steady-state model
  neglects frequency-dependence
Actual transistors exhibit charge-storage.
An augmented BJT model is required to examine this dependence.

## Slide 27: 9.2.2. The BJT
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 28
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 29: The Cutoff Frequency
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 30
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 31
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 32
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 33: 9.3. High-Frequency Response of the CS and CE Amplifiers
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Objective is to identify the mechanism that limits high-frequency performance.
  As well as fine AM.
Figure 9.12: Frequency response of a direct-coupled (dc) amplifier. Observe that the gain does not fall off at low frequencies, and the midband gain AM extends down to zero frequency.

## Slide 34: 9.3.1. The Common-Source Amplifier
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.13(a) shows high-frequency equivalent-circuit model of a CS amplifier.
MOSFET is replaced with model of Figure 9.6(c).
It may be simplified using Thevenin’s theorem.
Also, bridging capacitor (Cgd) may be redefined.
Cgd gives rise to much larger capacitance Ceq.
  The multiplication effect that it undergoes is known as the Miller Effect.

## Slide 35
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.13: Determining the high-frequency response of the CS amplifier: (a) equivalent circuit; (b) the circuit of (a) simplified at the input and the output; (Continued)

## Slide 36
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.13: (Continued) (c) the equivalent circuit with Cgd replaced at the input side with the equivalent capacitance Ceq; (d) the frequency response plot, which is that of a low-pass, single-time-constant circuit.

## Slide 37: 9.3.2. The Common-Emitter Amplifier
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.14(a) shows high-frequency equivalent circuit of a CE amplifier.
  BJT is replaced.
  This figure applies to both discrete and IC amps.
This figure may be simplified using Thevenin’s theorem.
Cin is simply sum of C and Miller capacitance C(1+gmRL’)

## Slide 38
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.14: Determining the high-frequency response of the CE amplifier: (a) equivalent circuit; (b) the circuit of (a) simplified at both the input side and the output side; (continued)

## Slide 39
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)

## Slide 40: 9.4. Useful Tools for the Analysis of the High-Frequency Response of Amplifiers
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
The approximate method used in previous sections to analyze the high-frequency response of amps provides an “ok” estimate.
However, it does not apply to more complex circuits.
This section discusses other tools.

## Slide 41: 9.4.1. The High Frequency Gain Funcion
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Amp gain is expressed as function of s in equation (9.61).
  A(s) = AMFH(s)
The value of AM may be determined by assuming transistor internal capacitances are open circuited.
This allows derivation of equation (9.62).

## Slide 42: 9.4.2. Determining the 3-dB Frequency fH
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
High-frequency band closest to midband is generally of greatest concern.
  Designer needs to estimate upper 3dB frequency.
If one pole (predominantly) dictates the high-frequency response of an amplifier, this pole is called dominant-pole response.
  As rule of thumb, a dominant pole exists if the lowest-frequency pole is at least two octaves (a factor of 4) away from the nearest pole or zero.

## Slide 43: 9.4.4. Miller’s Theorem
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Consider the situation shown in Figure 9.17(a).
  It is part of a larger circuit which is unknown.
Miller’s Theorem states that impedance Z can be replaced with two impedances:
  Z1 connected between node 1 and ground
    (9.76a) Z1 = Z/(1-K)
  Z2 connected between node 2 nd ground where
    (9.76b) Z2 = Z/(1-1/K)

## Slide 44
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.17: The Miller equivalent circuit.

## Slide 45: 9.5.1. The Equivalent Circuit
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.19: Generalized high-frequency equivalent circuit for the CS amplifier.

## Slide 46: 9.5.2. Analysis Using Miller’s Theorem
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.20: The high-frequency equivalent circuit model of the CS amplifier after the application of Miller’s theorem to replace the bridging capacitor Cgd by two capacitors: C1 = Cgd(1-K) and C2 = Cgd(1-1/K), where K = V0/Vgs.

## Slide 47: 9.5.3. Analysis Using Open-Circuit Time Constants
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.21: Application of the open-circuit time-constants method to the CS equivalent circuit of Fig. 9.19.

## Slide 48: 9.5.4. Exact Analysis
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.22: Analysis of the CS high-frequency equivalent circuit.

## Slide 49: 9.5.4. Exact Analysis
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.23: The CS circuit at s = sZ. The output voltage Vo = 0, enabling us to determine sZ from a node equation at D.

## Slide 50: 9.5.5. Adapting the Formulas for the Case of the CE Amplifier
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.24: (a) High-frequency equivalent circuit of the common-emitter amplifier. (b) Equivalent circuit obtained after Thévenin theorem has been employed to simplify the resistive circuit at the input.

## Slide 51: 9.5.6. The Situation When Rsig is Low
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
Figure 9.25: (a) High-frequency equivalent circuit of a CS amplifier fed with a signal source having a very low (effectively zero) resistance. (b) The circuit with Vsig reduced to zero. (continued)

## Slide 52: Summary
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
The coupling and bypass capacitors utilized in discrete-circuit amplifiers cause the amplifier gain to fall off at low frequencies. The frequencies of the low-frequency poles can be estimated by considering each of these capacitors separately and determining the resistance seen by the capacitor. The highest-frequency pole is that which determines the lower 3-dB frequency (fL).
Both MOSFET and the BJT have internal capacitive effects that can be modeled by augmenting the device hybrid-pi model with capacitances.
  MOSFET: fT = gm/2(Cgs+Cgd)
  BJT: fT = gm/2(C+C)

## Slide 53: Summary
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
The internal capacitances of the MOSFET and the BJT cause the amplifier gain to fall off at high frequencies. An estimate of the amplifier bandwidth is provided by the frequency fH at which the gain drops 3dB below its value at midband (AM). A figure-of-merit for the amplifier is the gain-bandwidth product (GB = AMfH). Usually, it is possible to trade gain for increased bandwidth, with GB remaining nearly constant. For amplifiers with a dominant pole with frequency fH, the gain falls off at a uniform 6dB/octave rate, reaching 0dB at fT = GB.
The high-frequency response of the CS and CE amplifiers is severly limited by the Miller effect.

## Slide 54: Summary
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
The method of open-circuit time constants provides a simple and powerful way to obtain a reasonably good estimate of the upper 3-dB frequency fH. The capacitors that limit the high-frequency response are considered one at a time with Vsig = 0 and all other capacitances are set to zero (open circuited). The resistance seen by each capacitance is determined, and the overall time constant (H) is obtained by summing the individual time constants. Then fH is found as 1/2H.
The CG and CB amplifiers do not suffer from the Miller effect.
The source and emitter followers do not suffer from Miller effect.

## Slide 55: Summary
The College of New Jersey (TCNJ) – ELC251 Electronics I
http://anthony.deese.googlepages.com
Based on Textbook: Microelectronic Circuits by Adel S. Sedra (0195323033)
The high-frequency response of the differential amplifier can be obtained by considering the differential and common-mode half-circuits. The CMRR falls off at a relatively low frequency determined by the output impedance of the bias current source.
The high-frequency response of the current-mirror-loaded differential amplifier is complicated by the fact that there are two signal paths between input and output: a direct path and one through the current mirror.
Combining two transistors in a way that eliminated or minimizes the Miller effect can result in much wider bandwidth.