## Slide 1: Analog and Digital Filter Design Advanced digital filter design using Matlab
Miroslav Lutovac and Dejan Tosic

## Slide 2: Overview
Drawback of the classic design
Advanced design paradigm
AFDesign toolbox
Example design
MATLAB script Lecture16.m

## Slide 3: Drawback of the classic design
The principal drawback of the classical digital filter design is in returning only one solution
That solution can be unacceptable for many practical implementations
Advanced approach provides
  reduced filter complexity for the desired performance
  better performances for the required complexity

## Slide 4: Advanced design paradigm
Advanced digital filter design introduces straightforward procedures to map the filter specification into a design space, that is, a set of ranges for parameters that we use in the filter design
We search this design space for the optimum solution according to given criteria, such as optimized group delay

## Slide 5: Design example
Design a lowpass filter that satisfies the following specification:
Fp = 1600 Hz
Fs = 1696 Hz
Ap = 0.2 dB
As = 40 dB
Fsamp = 8 kHz
Goal: Optimize group delay

## Slide 6: Classic design
Fp = 1600; Fs = 1696;
Ap = 0.2; As = 40;
Fsamp = 8000; Fnyquist = Fsamp/2;
Wp = Fp/Fnyquist;
Ws = Fs/Fnyquist;
[N, Wn] = ellipord(Wp, Ws, Ap, As)
[num,den] = ellip(N, Ap, As, Wn)
[H,f]=freqz(num, den, 512, Fsamp);
[Gd,fGd]=grpdelay(num,den,512,Fsamp);
plot(fGd,Gd);
figure; plot(f,-20*log10(abs(H)));
Gdmax is over 100

## Slide 7: Advanced design: AFDesign
Gdmax has been reduced to 70

## Slide 8: Design parameters
Design parameters
D = {n, , , fp}
Filter order n
Selectivity factor 
Ripple factor 
Actual passband edge fp

## Slide 9: Design alternative D1
D1 design has higher attenuation in the stopband than is required by the specification. We choose D1 design when we prefer to achieve as large an attenuation as possible in the stopband.

## Slide 10: Design alternative D2
D2 design has lower attenuation in the passband than is required by the specification. We choose this design when we prefer to achieve as low an attenuation as possible in the passband.

## Slide 11: Design alternative D3a
D3a design has the sharpest magnitude response. Disadvantages of D3a can be very high Q-factors and large variation of the group-delay in the passband. This is MATLAB default design.

## Slide 12: Design alternative D3b
D3b design has the sharpest magnitude response. Disadvantages of D3b can be very high Q-factors. The variation of the group delay can be high, but its maximal value can be moved into the transition region, so the group-delay variation can be acceptable in the passband.

## Slide 13: Design alternative D4a
D4a has a smoother magnitude response, and that is the main reason for lower Q-factors and smaller variation of the group delay in the passband.

## Slide 14: Design alternative D4b
D4b has a smoother magnitude response. D4b usually yields very low Q-factors and small variation of the group delay in the passband. D4b has a very low ripple factor.

## Slide 15: Group delay
The maximum delay is obtained for D3a and D3b, while D4a and D4b have lower group-delay variation.

## Slide 16: AFDesign: D5 – minimal Q-factor
Gdmax has been reduced to 60

## Slide 17: AFDesign: Bandpass

## Slide 18: Further reading
M. D. Lutovac, D. V. Tošić, B. L. Evans
Filter Design for Signal Processing Using MATLAB and Mathematica
Prentice Hall Upper Saddle River, New Jersey ISBN 0-201-36130-2, (c) 2001
http://kondor.etf.bg.ac.yu/~lutovac/