## Slide 1: Analog and Digital Filter Design Review Systems
Miroslav Lutovac and Dejan Tosic

## Slide 2: Overview
Definition of a system
Block diagram
System properties
Linear time-invariant (LTI) system
Response of LTI systems
Convolution
MATLAB exercises

## Slide 3: What is a system?
A signal is a physical quantity, or quality, which conveys information
Systems take one or more signals as input, perform operations on the signals, and produce one or more signals as output
A system is a group of related parts working together, or an ordered set of ideas, methods, or ways of working

## Slide 4: Definition of a system
Implementation point-of-view: a system is an arrangement of physical components connected or related in such a manner as to form and/or act as an entire unit
Signal processing perspective: a system can be viewed as any process that results in the transformation of signals, in which systems act on signals in prescribed ways
Mathematical: a system as a mapping of N input signals onto M output signals; the mapping carries out a transformation on the input signals according to a set of rules

## Slide 5: Basic definitions
Single-variable system (SISO system) has only one input and only one output
Multivariable system (MIMO system) has more than one input or more than one output
Input-output relationship (external description) is an equation that describes the relation between the input and the output of a system
Black box concept: the knowledge of the internal structure of a system is unavailable; the only access to the system is by means of the input ports and the output ports

## Slide 6: Time response
One-dimensional system: required for processing a signal that is a function of the single independent variable
We assume that the independent variable is time even in cases where the independent variable is a physical quantity other than time
Time response is the output signal as a function of time, following the application of a set of prescribed input signals, under specified operating conditions

## Slide 7: Continuous-time system
Continuous-time system: the input and output signals are continuous time

## Slide 8: Discrete-time system
Discrete-time system has discrete-time input and output signals

## Slide 9: Digital system
A discrete-time system is digital if it operates on discrete-time signals whose amplitudes are quantized
Quantization maps each continuous amplitude level into a number
The digital system employs digital hardware
  explicitly in the form of logic circuits
  implicitly when the operations on the signals are executed by writing a computer program

## Slide 10: Analysis and design
Analysis of a system is investigation of the properties and the behavior (response) of an existing system
Design of a system is the choice and arrangement of systems components to perform a specific task
Design by analysis is accomplished by modifying the characteristics of an existing system
Design by synthesis: we define the form of the system directly from its specifications

## Slide 11: Block diagram
Block diagram is a pictorial representation of a system that provides a method for characterizing the relationships among the components
Single block with one input and one output is the simplest form of the block diagram
Interior of the rectangle representing the block contains (a) component name, (b) component description, or (c) the symbol for the mathematical operation to be performed on input to yield output
Arrows represent the direction of signal flow

## Slide 12: Elements of block diagram
Summing point
Takeoff point

## Slide 13: Interconnections of blocks
Blocks connected in cascade
Blocks connected in feedback
Blocks connected in parallel

## Slide 14: State
For some systems, the output at time t0 depends not only on the input applied at t0, but also on the input applied before t0
The state is the information at t0 that, together with input for t ≥ t0, determines uniquely output for t ≥ t0
Dynamical equation is the set of equations that describes unique relations between the input, output, and state

## Slide 15: Relaxed system
A system is said to be relaxed at time t0 if the output for t ≥ t0 is solely and uniquely determined by the input for t ≥ t0
If the concept of energy is applicable, the system is said to be relaxed at t0 if no energy is stored in the system at t0
A system is said to be zero-input if the output for t ≥ t0 is solely and uniquely determined by the state

## Slide 16: Causality and stability
A system is called causal if the output depends only on the present and past values of the input
Intuitively, a stable system is one that will remain at rest unless excited by an external source and will return to rest if all excitations are removed
A relaxed system is BIBO stable (bounded-input bounded-output) if every bounded input produces a bounded output

## Slide 17: Time-invariant system
A relaxed system is time-invariant if a time shift in the input signal causes a time shift in the output signal
In the case of discrete-time digital systems, we often use the term shift-invariant instead of time-invariant
Characteristics and parameters of a time-invariant system do not change with time

## Slide 18: Linear system
Consider a relaxed system in which there is one independent variable t
A linear system is a system which has the property that if
input x1(t) produces an output y1(t) and
input x2(t) produces an output y2(t), then
input c1 x1(t) + c2 x2(t) produces an output c1 y1(t) + c2 y2(t) for any x1(t), x2(t) and arbitrary constants c1 and c2

## Slide 19: Principle of superposition
The response y(t) of a linear system due to several inputs x1(t), x2(t), … xN(t) acting simultaneously is equal to the sum of the responses of each input acting alone
If yi(t) is the response due to the input xi(t), then

## Slide 20: Linear time-invariant (LTI) system
Continuous-time system is LTI if its input-output relationship can be described by the ordinary linear constant coefficient differential equation
Discrete-time system is LTI if its input-output relationship can be described by the linear constant coefficients difference equation

## Slide 21: Response of an LTI system
Free response (zero-input response) is the solution of the differential equation when the input is zero
Forced response (zero-state response) is the solution of the differential equation when the state is zero
Total response is the sum of the free response and the forced response
Total response can be viewed, also, as the sum of the steady-state response and transient response
Steady-state response is that part of the total response which does not approach zero as time approaches infinity
Transient response is that part of the total response which approaches zero as time goes to infinity

## Slide 22: Procedure for analyzing a system
Determine the equations for each system component
Choose a model for representing the system (e.g., block diagram)
Formulate the system model by appropriately connected the components
Determine the system characteristics

## Slide 23: Convolution integral
Unit impulse response is the output of a continuous-time LTI system to a unit impulse input when the state is zero
If we know the input and impulse response of a causal LTI system, the forced response can be found by the convolution integral

## Slide 24: Transient system specifications
Unit step response is the output of an LTI system to a unit step input when the state is zero
Overshoot, Delay time, Rise time, Settling time

## Slide 25: Convolution sum
Unit impulse response is the output of a discrete-time LTI system to a unit impulse input when the state is zero
If we know the input and impulse response of a causal LTI system, the forced response can be found by the convolution sum

## Slide 26: MATLAB exercise 2.1, page 62
h = inline('exp(-t).*(t>0)', 't'); x = inline('sin(t).*(t>0)', 't'); u = inline('exp(-(t-tau)).*(… (t-tau)>0).*sin(tau).*(tau>0)', 'tau', 't'); r=inline('0.5*(exp(-t)-cos(t)+sin(t)).*(t>0)','t'); t1 = 0; t2 = 6; TR = [t1, t2]; subplot(2,1,1) fplot(h, TR, 2e-3, 1, ':b') hold on; fplot(x, TR, 2e-3, 1, '-r') hold off legend('impulse response', 'input') ti = t1:0.2:t2; y = []; for i = 1:length(ti) y = [y, quad(u,0,ti(i),1e-8,0,ti(i))]; end; subplot(2,1,2); plot(ti, y); xlabel('t'); ylabel('forced response') hold on; fplot(r, TR, 2e-2, 1, 'or') legend('numerical', 'exact')

## Slide 27: MATLAB exercise 2.5, page 62
k = 0:15; h = ((0.7).^k).*(k>=0); x = (k>=0) - (k>=4); c = conv(h,x); y = c(1:length(x)); subplot(3,1,1); stem(k,h,'g'); ylabel('h_k','FontSize',14); axis([k(1) k(end) -1 2]); subplot(3,1,2); stem(k,x,'b'); ylabel('x_k','FontSize',14); axis([k(1) k(end) -1 2]); subplot(3,1,3); stem(k,y,'r'); xlabel('k','FontSize',14); ylabel('y_k','FontSize',14); axis([k(1) k(end) -1 3]);

## Slide 28: Drawing systems in MATLAB with DrawFilt

## Slide 29: Further reading
M. D. Lutovac, D. V. Tošić, B. L. Evans
Filter Design for Signal Processing Using MATLAB and Mathematica
Prentice Hall Upper Saddle River, New Jersey ISBN 0-201-36130-2, (c) 2001
http://kondor.etf.bg.ac.yu/~lutovac/