## Slide 1: Analog and Digital Filter Design Digital filters FIR and IIR structures
Miroslav Lutovac and Dejan Tosic

## Slide 2: Overview
Review: Discrete-time system, Digital system, LTI system
Impulse response
Definition of FIR and IIR systems
FIR and IIR structures
MATLAB examples
FDAtool design example

## Slide 3: Review: Discrete-time system
Discrete-time system has discrete-time input and output signals

## Slide 4: Review: Digital system
A discrete-time system is digital if it operates on discrete-time signals whose amplitudes are quantized
Quantization maps each continuous amplitude level into a number
The digital system employs digital hardware
  explicitly in the form of logic circuits
  implicitly when the operations on the signals are executed by writing a computer program

## Slide 5: Linear time-invariant (LTI) system
Discrete-time system is LTI if its input-output relationship can be described by the linear constant coefficients difference equation
The output sample y() might depend on all input samples that can be represented as

## Slide 6: MATLAB example 1
N = 80; k = 0:(N-1);
b0 = 1;
b1 = -1;
b2 = 1;
B = [b0 b1 b2];
f = 1/8;
x = sin(2*pi*f*k+pi/6);
y = filter(B,1,x);
subplot(2,1,1)
systemFIR(0,0,4,5,10,'b')
subplot(2,1,2)
plot(k,x,'go', k,y,'bo',...
k,x,'g-', k,y,'b-')
legend('input','output')
MATLAB filter command corresponds to the symbol 

## Slide 7: Impulse response
Response of a system to the unit impulse sequence is called the unit impulse response or impulse response for short

## Slide 8: MATLAB example 2
N = 16; k = 0:(N-1);
b0 = 1; b1 = -1; b2 = 2;
B = [b0 b1 b2];
x = (k==0);
y = filter(B,1,x);
subplot(3,1,1) systemFIR(0,0,4,5,10,'b')
subplot(3,1,2) stem(k,x,'r') ylabel('input')
subplot(3,1,3) stem(k,y,'b') ylabel('output')

## Slide 9: What are FIR and IIR systems?
A discrete system is said to be an FIR system if its impulse response has zero-valued samples for n > M > 0
Integer number M is called the length of the impulse response
IIR system is a discrete system with an infinite impulse response
FIR = Finite Impulse Response IIR = Infinite Impulse Response

## Slide 10: MATLAB example 3
N = 80; k = 0:(N-1);
a = 0.97;
B = [0 1];
A = [1 -a];
x = (k==0);
y = filter(B,A,x);
subplot(3,1,1) draw1stIIR(0,0,4,5,10,'b')
subplot(3,1,2) stem(k,x,'r') ylabel('input')
subplot(3,1,3) stem(k,y,'b') ylabel('output')
The impulse response does not vanish after finite number of samples

## Slide 11: Basic FIR structures
Direct form, Transposed form, Cascade form, Linear-phase, Symmetric

## Slide 12: Direct form 2nd order

## Slide 13: Transposed direct form 2nd order

## Slide 14: Cascade direct form

## Slide 15: Direct form (Tapped delay line)

## Slide 16: Transposed direct form

## Slide 17: Linear-phase type 1

## Slide 18: Linear-phase type 2

## Slide 19: Symmetric FIR type I

## Slide 20: Symmetric FIR type II

## Slide 21: Basic IIR structures
Direct form, Transposed form

## Slide 22: Direct form I 2nd order

## Slide 23: Direct form II 1st order

## Slide 24: Direct form II 2nd order

## Slide 25: Cascade direct form II

## Slide 26: Transposed direct form II 1st order

## Slide 27: Transposed direct form II 2nd order

## Slide 28: FIR design example
4th order linear-phase filter

## Slide 29: FDAtool FIR design example

## Slide 30: File, Export …

## Slide 31: Edit, Convert Structure …

## Slide 32: FIR example designs

## Slide 33: Further reading
M. D. Lutovac, D. V. Tošić, B. L. Evans
Filter Design for Signal Processing Using MATLAB and Mathematica
Prentice Hall Upper Saddle River, New Jersey ISBN 0-201-36130-2, (c) 2001
http://kondor.etf.bg.ac.yu/~lutovac/